.

# PRE-CONSTRUCTION

# INFORMATION

Design Supply and Installation of Part New Heating Solution

Clarence House Euclid Street Swindon SN1 2SG

July2019 v1

CONTENTS

SECTION 1		-		DESCRIPTION OF PROJECT

SECTION 2		-		CLIENT’S CONSIDERATIONS AND MANAGEMENT					REQUIREMENTS

SECTION 3		-		ENVIRONMENTAL RESTRICTIONS AND

EXISTING ON-SITE RISKS

SECTION 4		-		SIGNIFICANT DESIGN AND CONSTRUCTION												HAZARDS

SECTION 5		-		HEALTH & SAFETY FILE

|  | Name | Date |
| --- | --- | --- |
| Prepared By | Ian Taylor | 24/09/2019 |
| Approved By | Karen E Kent | 24/09/2019 |

# Swindon Borough Council

# Civic Offices

# Swindon

Amendment Schedule

| Change no. | Date | DETAILS | By |
| --- | --- | --- | --- |
| 0 | 24/09/2019 | Initial distribution of Issue 01 | IT |

# CONSTRUCTION (DESIGN AND MANAGEMENT) REGULATIONS 2007

# PRE-CONSTRUCTION INFORMATION

# 1.	Description of Project

A.	Details and Location of Construction Work

|  | Design Supply and Installation of a part new heating system at Clarence House Euclid Street Swindon SN1 2SG |
| --- | --- |

i.	Key Dates																																																										ii.	Mobilisation

|  | Planned Start Date: 27th Jan 2020 Planned Finish Date: 6th March 2020 Project Duration: 6 Weeks |  | Minimum time for mobilisation after appointment of the Principal Contractor: 3/4 weeks. |
| --- | --- | --- | --- |

B.	Contact Details

i.	Client Details

|  | Gerry O’Connor Tel: 01793 463452 Swindon Borough Council email go’connor@swindon.gov.uk Wyvern House Theatre Square Swindon SN1 1QN |
| --- | --- |

ii.	Principal Designer Details

|  | Ian Taylor Tel: 07429383986 Swindon Borough Council email: itaylor@swindon.gov.uk Wyvern House Theatre Square Swindon SN1 1QN |
| --- | --- |

iii.	Project Manager Details

|  | Ian Taylor Tel: 0742938986 Wyvern House Theatre Square email:itaylor@swindon.gov.uk Swindon Borough Council Swindon SN1 1QN |
| --- | --- |

iv.	Lead Designer Details

|  | Ian Taylor Tel: 0742938986 email: itaylor@swindon,gov,uk Swindon Borough Council Wyvern House Theatre Square Swindon SN1 1QN |
| --- | --- |

v.	M&E Designer Details

|  | Ian Taylor Tel: 0742938986 email: itaylor@swindon.gov.uk Swindon Borough Council Wyvern House Theatre Square Swindon SN1 1QN |
| --- | --- |

vi.	Structural Engineer Details

|  | To be appointed by main contractor if required |
| --- | --- |

C.		Will the structure be used as a workplace, taking into account the Workplace (Health, Safety and Welfare) Regulations 1992?

|  | YES |
| --- | --- |

D.	Extent and Location of existing Records & Plans

|  | H&S File – None available O&M – None available Asbestos survey/register – See Appendix J of contract documentation Legionella Assessment – N/A Gas (Mains /LPG) –Natural Gas to boiler room Electrics (Underground & Overhead) – underground supply, exact location to be confirmed on site Water (Foul & Storm) – to existing mains sewers Water (Mains) - underground supply, exact location to be confirmed on site Comms (BT, Cable, I.T) - underground CCTV – Exact locations to be confirmed on site Alternative power sources (wind, water, ground source & solar) – N/A Geotechnical Survey – N/A Archaeological – N/A Structural (steel sequence, Loadings) – N/A Dilapidation – N/A Environmental (Fauna & Flora) N/A Existing hazardous substances (Anthrax, Vermin, Lead, radon etc.) Asbestos containing materials, are present. Current Fire Plans/Procedures (site and adjoining) – N/A Emergency plans / procedures (other than fire) – N/A Existing plant (Sprinklers, Dry/wet risers, Lifts, Boilers, Pressure systems, window cradles) – Passenger lifts within the building.. Heating Ventilation & Air conditioning (HVAC) As built drawings – N/A Designers risk assessments - With Lead Designer |
| --- | --- |

2. 	Client’s Considerations and Management Requirements

A.						Arrangements for:

i.	Planning and managing the construction work, including the health & safety goals for the project

|  | The health and safety objective is to complete the project on time and as specified with due regard to the health, safety and welfare of the Principal Contractor’s employees, other Contractor’s employees, Client’s employees, visitors and uninvited members of the public. A hazard identification and hierarchy of risk control system will be required by the Principal Contractor to eliminate, reduce, isolate or control any risks from hazards identified throughout the project to achieve the safety goals Hazards which are identified throughout the project are to be managed and controlled by the Principal Contractor by the creation of specific work task risk assessments and method statements to reduce risks. The Principal Contractor will appoint a competent person (i.e. who has attained the CITB Site Manager Safety Training Sceme or similar) who has responsibility for the daily management of the project In addition, the Principal Contractor shall set out in his Construction Phase Plan or suitable Method Statement specific proposals to reduce accidents/incidents. These proposals shall identify: The most likely types of hazards (i.e. Working at height, lifting operations, confined spaces etc) on the project The control measures proposed Target accident levels for the project (which should be set to give a clear improvement on current company statistics) Procedures for training, monitoring, review and audit Whether workforce incentive schemes are appropriate, and if so, the details How the above is to be ‘sold’ to all on site, particularly the subcontract labour The Principal Contractor shall implement a comprehensive monitoring and Audit regime to ensure that risks to his employees, other contractors, and anyone else who could be effected are adequately controlled. The Principal Contractor must instigate a suitable regime of formal site safety inspections on a weekly basis with a 6 monthly audit of their health and safety management systems by a competent person. Both inspections and audits are to be recorded and made available for inspection by the Client, his representative and the CDM Co-ordinator |
| --- | --- |

i.	Planning and managing the construction work, including the health & safety goals for the project (continued)

|  | The Principal Contractor is required to submit a Construction Phase Plan or suitable Method Statement which addresses significant hazards such as: Segregation of unauthorised persons Working in occupied premises Manual Handling Lifting operations Work in Confined Spaces Working from Height (Methods/equipment used) Work equipment (PAT tested/storage/daily visual inspections) Protection against electrical hazards Work involving asbestos removal not covered under notifiable projects Uncontrolled pedestrian movement Daily waste transfers The Principal Contractor is to include, as a minimum, the following Site Rules that will apply to the project: Appropriate PPE to be worn at all times Mobile phones only to be used within the site welfare facilities, except if needed for an emergency Camera phones or other image capturing devices are not permitted on site No radios, ipods or similar No smoking All operatives will wear identification at all times No wearing of shorts No swearing Keep a tidy and secure work area (no work equipment is to be left unattended). This includes welfare facilities and storage areas Emergency access/egress routes to be kept clear at all times. All operatives and visitors to sign in and out of the site when arriving or leaving |
| --- | --- |

ii. 			Arrangements for communication and liaison between Client and others

|  | The Principal Contractor is to attend meetings with any third parties as requested, (i.e. Contract Administrator, Project Manager) The Principal Contractor shall attend a weekly meeting with the Project Manager to advise on progress and significant works that may affect their undertaking. Agenda items should include: Principal Contractor Work agenda for forthcoming week Special deliveries Unusual/hazardous activities Details of any accidents/incidents Non-contract health and safety concerns Project Management Project amendments Special activities At design meetings the Principal Contractor is to present a programme to enable adequate control of health and safety issues, such as permit to work requirements, etc. Design/progress meetings are to be identified by the Project Manager. All meetings are to be attended by the Principal Contractor The Principal Contractor shall communicate to the Principal designer any additional design work and/or unforeseen eventualities necessitating changes to the design which could affect the Construction Phase Plan or suitable Method Statement. Any changes required as a result of design changes shall be agreed with the Principal Designer. Designers and the Principal Contractor shall liaise with the Principal Designer to initiate and agree the arrangements for the provision of information for the Health and Safety File. Provision of relevant information for inclusion in the Health and Safety File must be continuous throughout the project to enable the Principal Designer to complete the file to the agreed time scales as per section 5 of this document. Any weekend or out of hours working will be by prior arrangement with the Project Manager. A list of operatives to be supplied to the Contract Administrator on request This document will remain live and will be amended and distributed as required. |
| --- | --- |

iii.	Arrangements for security of the site

|  | All contractors’ personnel are to be monitored by signing in and out at all times. The Principal Contractor is to provide security in accordance with the requirements of the project. Site access and egress should be managed by a suitable and sufficient controlling and monitoring system to prevent unauthorised access by any third party. |
| --- | --- |

iv.     Arrangements for welfare provision

|  | It is the Principal Contractor’s responsibility to ensure that the welfare facilities are of a standard laid down in the Construction (Design and Management) Regulations 2015 or better for the anticipated number of persons that will be using them, and that they are adequetly maintained and cleaned according to conditions and amount of use. If necessary he shall enhance the facilities to ensure he is providing welfare facilities which are truly reflective of an employer that is seriously committed to raising standards. This should manifest itself in the standard of provision (space, repair, and decor), consumables (towels, soaps) and cleanliness (separation of dirty areas, cleaning frequency). The Principal Contractor shall set out his specific proposals regarding quantity and location of welfare facilities in the Construction Phase Plan or suitable Method Statement. |
| --- | --- |

B.	Requirements relating to the health & safety of the Client’s employees or customers or those involved in the project

i.	Site hoarding and segregation requirements

|  | The principal contractor is to ascertain the need for security fencing to the site. If deemed necessary the work area will be appropriately secured/isolated from the public using Heras fencing ‘No Entry to Unauthorised Persons’ signage displayed. The remainder of the site’s areas will remain in use/accessible to the residents and staff for the duration of the works. A site plan showing the location of site waste, storage, office and welfare facilities must be included as part of the Principal Contractor’s Construction Phase Plan or suitable Method Statement. |
| --- | --- |

ii.	Special on site transport arrangements or vehicle movement restrictions

|  | All vehicle and plant movement in relation to works on the construction site will be controlled and supervised by a competent banksman. Any vehicles and plant will be appropriately secured when not in use. All car park and access roads surrounding the building will be maintained for emergency vehicle access at all times. |
| --- | --- |

iii.     Client permit to work systems

|  | No client permit to work systems are currently in place The Principal Contractor will be required to implement a permit to work system for hazardous activities should the need become apparent. Details regarding the permit to work system must be included as part of the Principal Contractor’s Construction Phase Plan or suitable Method Statement. |
| --- | --- |

iv.					Fire Precautions

|  | There is a fire alarm present within the property. The property’s fire extinguishers must not be used – If fire extinguishers are required for emergency use, the Principal Contractor must supply them. |
| --- | --- |

v.							Emergency procedures and means of escape

|  | During the period of this project, there must be a suitable and sufficient emergency plan in place to protect against potential emergency situations, details of which must be included as part of the Principal Contractor’s Construction Phase Plan or suitable Method Statement. Systems to be operational include: A means of raising an audible alarm in the case of a fire Means of escape – with all on site made explicitly aware Suitable types and numbers of fire fighting equipment Coordination, communication and agreement of all emergency plans must be shared with the adjacent construction site. The nearest Fire and Rescue Station is located at: Swindon Fire Station Drove Road Swindon SN1 3AD Tel: 01793 401240 (for Fire safety advice only) All calls for emergency assistance must be by 999 The Principal Contractor must keep all people on site informed at all times of any changes to temporary means of escape before they are implemented. The Principal Contractor must agree all temporary means of escape with the Local Authority where proposed circulation and escapes routes may affect access for the Emergency services. |
| --- | --- |

v.							Emergency procedures and means of escape (continued)

|  | Drawings must be maintained to show all temporary means of escape routes for residents, visitors and construction workers during the construction phase. All temporary means of escape must be kept clear of obstructions at all times and provided with adequate lighting and signage at regular intervals on long routes and changes of directions. Suitable signage should be located where they are clearly visible and must be securely fixed. The Principal Contractor will be responsible for developing proposals and providing signage for the construction site to cover day to day access, information and emergency matters. The Principal Contractor will provide suitably trained first aid personnel and adequate equipment as appropriate for the hazards and amount of operatives working on the project Any RIDDOR notifications must be communicated (brief details) to the Project Manager and the Principal Designer as soon as practical after the accident/incident. All RIDDOR notifications are to be recorded, and information regarding investigations and subsequent actions are to be reviewed at monthly progress meetings. The nearest A&E department is located at: Great Western Hospital Marlborough Rd Swindon SN3 6BB Tel: 01793 604020 |
| --- | --- |

vi.    “No go areas” or other authorisation requirements

|  | No contractor is permitted to areas within the property not affected by the works without prior agreement/authorisation from the tenant. |
| --- | --- |

vii.    Confined Spaces

|  | The Principal Contractor must develop and implement procedures for safe working and emergency evacuation in any areas identified as necessary with details included as part of the Principal Contractor’s Construction Phase Plan or suitable Method Statement. |
| --- | --- |

viii.			Smoking and Parking restrictions

|  | An external area within the site boundary will be designated as the smoking area, and will need to include an appropriate means of putting out cigarettes. There will be adequate contractor parking in the car park/designated areas within the site as agreed with the site managers. |
| --- | --- |

ix.  			Other requirements

|  | No radios or Audio equipment to be used |
| --- | --- |

3.						Environmental restrictions and existing on-site hazards

A.     Safety hazards including:

i. 	Boundaries and access, including temporary access

|  | Narrow streets – All approach roads to the site are standard two way traffic; access to the site is via the main road Bridges – None known within the immediate vicinity Height restrictions – None known within the vicinity Weight restrictions – None known within the vicinity Turning space – limited turning space within the public parking area Lack of parking – parking is available in the public parking area. . |
| --- | --- |

ii.	Restrictions on deliveries, waste collection or storage

|  | Access to the site is via A/B class roads, The Principal Contractor to ensure a competent banksman is always available to supervise deliveries/collections. Vehicular access to, and egress from, the site will be prohibited during the following times: - No restrictions |
| --- | --- |

iii. 	Adjacent Land Uses and Related Restrictions

|  | Railways – The main line is approximately 4km North West of the site Water (rivers, canals, ponds etc.) – On site Other construction sites – None known within the vicinity Industrial sites – Chaney Manor Industrial Estate is approx. 5km to the North East of the site. Busy traffic routes – The nearest main road is outside the site Entertainment (nightclubs etc.) Town Centre The surrounding area is a Town Centre |
| --- | --- |

iv. 				Existing storage of hazardous materials

|  | The Principal Contractor must review prior to full commencement on site. No known hazardous chemicals/materials are stored on site other than domestic cleaning goods. The Principal Contractor is to ensure any hazardous materials used are disposed of, or managed in a legally compliant manner. |
| --- | --- |

v. 						Location of existing services (Underground, overhead and concealed)

|  | The exact location of any underground services/utilities is unknown. A full utility survey must be completed prior to the commencment of any excavations or groundworks, with a ‘cat scan’ carried out to accurately locate any underground services prior to any groundwork, with the service runs clearly marked. All local utility surveys must be scrutinsed prior to commencing any work. No significant overhead hazards identified |
| --- | --- |

vi. 		Ground conditions, underground structures or water courses (that may affect works)

|  | Not known in the immediate vicinity of the works. |
| --- | --- |

vii. 		Information about existing structures (stability, structural form, fragile or hazardous materials, or anchorage points for fall arrest systems)

|  | The existing property dates from the 1900’s and is constructed from Brick/stone built building and is assumed in good condition with no known structural faults or defects. |
| --- | --- |

viii. 		Previous structural modifications (including weakening or strengthening)

|  | The exact details of any such works for the property are not known. |
| --- | --- |

ix. 			Fire Damage, Ground shrinkage, movement or poor maintenance which may have affected the structure

|  | None known |
| --- | --- |

x. 					Difficulties relating to plant or equipment in the premises

|  | None known |
| --- | --- |

xi. 	Health and safety information contained in earlier design, construction or as built drawings

|  | All relevant information can be viewed via the Project Manager. |
| --- | --- |

xii.							Additional safety hazards

All appointed contractors must be competent and well resourced to undertake the project work awarded. They are expected to have full awareness of the inherent hazards associated with refurbishment and construction hazards within their own specialist areas, and have the ability to manage those risks to current legal standards and industry best practice. Pedestrian routes must be maintained in a safe condition at all times where plant/equipment movement may create or deposit debris.

B.     Health Hazards, including:

i.       Asbestos, including results of surveys

|  | There is an Asbestos management survey the property a copy of which is included within the tender documentation. Asbestos containing materials were found within the building but should not be affected by the proposed works. If any new Asbestos Containing Materials (ACM) are identified or presumed, work must stop immediately and be referred to the SBC Asbestos Manager for appraisal and action to enable suitable work plan to be created. Any removal works not under licence is to be completed by competent persons and works must be as required by best practice and HSE guidance. All works involving ACM’s must be recorded and works completed on approval of SBC Asbestos Manager and carried out in full accordance with the Control of Asbestos Regulations 2012. Asbestos register is to be updated at all times as necessary, and amendments recorded. |
| --- | --- |

ii.      Existing hazardous materials

|  | The Principal Contractor must review prior to full commencement on site. The Principal Contractor is to ensure any hazardous materials are disposed of, or managed in a legally compliant manner. The Principal Contractor must ensure suitable and sufficient controls measures are implemented, and that details of which must be included as part of the Principal Contractor’s Construction Phase Plan or suitable Method Statement. |
| --- | --- |

iii.     Contaminated land including results of surveys

|  | If any evidence of contamination or hazards are discovered during any excavation works, work must cease, the Project Manager must be informed, and a full geotechnical survey must be completed , and any remedial actions completed prior to the recommencement of the works. Due to arsenic known to be a regular contaminant present in the soil across Swindon, any operatives carrying out any excavations must wear appropriate PPE to prevent absorption (rubber, not cloth) |
| --- | --- |

iv.     Existing structures containing hazardous materials

|  | There are none known at present however, should any be identified the Principal Contractor must ensure suitable and sufficient controls measures are implemented, and that details of which must be included as part of the Principal Contractor’s Construction Phase Plan or suitable Method Statement. |
| --- | --- |

v.     Health risks arising from clients activities

|  | None identified |
| --- | --- |

vi.							Additional health hazards

Particular attention must be made to ensure suppression of any dust and/or noise which may disturb the residential premises in the local vicinity. Appropriate precautions must be taken with the Principal Contractor ensuring that suitable and sufficient controls measures are implemented, and that details of which must be included as part of the Principal Contractor’s Construction Phase Plan or suitable Method Statement.

4.     Significant design and construction hazards

A      Significant design assumptions and suggested work methods, sequences or other control measures

|  | No significant design or construction hazards have been identified by the Designer |
| --- | --- |

B.    Arrangements for Coordination of ongoing design work and handling design Change

|  | Should site conditions or additional works require the design to be revised the Principal Contractor shall bring this to the attention of the Contract Administrator and the Principal Designer. They will then notify members of the project team as appropriate. Where a significant health and safety issue arises this shall be discussed with the Principal Designer. The Contractor shall pass the Construction Phase Plan or suitable Method Statement to the Principal Designer prior to commencement of the works. At the end of the contract, the Principal Contractor shall pass the revised Construction Phase Plan or suitable Method Statement, including modifications, to the Principal Designer. |
| --- | --- |

C.     Information on significant risks identified during design

|  | The Initial Design Team for planning purposes has not at this stage reported on any significant risks identified during the design stage that would not normally be encountered by a competent contractor. On appointment, the design team must create and maintain a suitable risk register to identify significant health and safety risks and guidance to control those risks. The Principal Designer will support and provide guidance regarding the creation of the register. The risk register must incorporate all risks associated with The Construction Phase Future cleaning and maintenance Future demolition or dismantling The Principal Designer will manage the communication of the register to all parties. |
| --- | --- |

D.     Materials requiring particular precautions

|  | The Design Team must identify any materials to be used that would require any special or specific precautions that would not normally be known by a competent Principal Contractor. The manufacturers’ or suppliers’ safety data sheets for any hazardous materials and products should be obtained and appropriate precautions observed. If any substance identified to be used during the progression of these works Has a Working Exposure Limit (WEL) as defined by the COSHH Regulations, a full risk assessment must be completed. The Principal Contractor shall ensure that the exposure is either prevented or, where not reasonably practicable, is adequately controlled. The Principal Contractor should also ensure that all persons affected by the work are informed of the Working Exposure Limit and the method of control, and that Operatives are given appropriate instruction, training and supervision to ensure that the work can be carried out safely. |
| --- | --- |

5.						Health & Safety File

Format and content

|  | Designers and the Principal Contractor should provide relevant information regarding the project to the Principal Designer. Instructions to amend the file will be communicated by the Principal Designer. Information must be provided continually throughout the project, and 1 week prior to completion of the works at the latest. Initially, it is required that one hard and one electronic copy will be provided before completion of the project. |
| --- | --- |