Decoration to Communal Areas

The works will comprise of decoration to the internal communal areas to 2 and 3 storey blocks of flats.

The contractor shall undertake a survey and submit a schedule of works based on bespoke rates for decoration in Appendix P. The survey must be accurate in measurements.

Scope

Decoration will be undertaken to all internal walls, ceilings, timber and metal surfaces (excluding flat entrance doors).

The contractor must ensure all surfaces are protected prior to any works commencing. Wash down ceiling, walls, woodwork and metalwork to throughout communal area.

Rub down, prepare and apply 2 coats of eggshell paint to walls and ceilings areas. Wire brush, prepare for and apply one coat of primer, one undercoat, two coats of gloss paint on metal balustrading, and railings ne 300mm girth. Thoroughly prepare shed door architraves and apply one undercoat and one gloss coat to wood surfaces not exceeding 300mm girth. Rub down, prepare for and apply one coat of primer, one undercoat and two coats of gloss paint to all surfaces of any type or size of single timber shed door (one sides and edges).

Access

The contractor shall include in their rates the cost of any scaffolding, and access required to undertake the works safely.

The contractor must ensure that access/ egress to individual flats is maintained at all times.