Appendix B1

# Technical Specification

# 2017

## Solent Room

## Technical Specifications

### Stage

- 49’ width wall to wall

- 32’/ 10 metres performing width

- 20’/ 6 metres depth

- 18’/ 5.4 metres Maximum flat height

- 2 x Stage steps from auditorium available on request

- No Rake

- No safety iron main tabs act as iron, where possible they should be kept clear to form firebreak

- Main tabs take 9 seconds to travel in or out, and can be controlled from prompt corner or LX desk

- 4 x triple E track for cloths

- 3 x manual hemp barrels

- Maximum set height 16’

#### Ideal set height 14’

# Maximum cloth size 40’ / 12 metres X 18’/ 5.5 metres

### Crossover

- The back dock is used as the crossover between Stage Left and Stage Right

##### Stage risers and stage extensions (steeldeck)

- These are available in 6’X 4’ sections, 40 pieces are available with

- Inter-changeable heights. Maximum number in each height shown below:

  - 12 risers at 9”high (23cm)

  - 12 risers at 12”high (30cm)

  - 22 risers at 18”high (46cm)

  - 12 risers at 24”high (61cm)

  - 10 risers at 27”high (69cm)

  - 10 risers at 36”high (92cm)

  - 12 risers at 39”high (99cm - stage height)

Stage Power

| 32 amp singles phase | 1 |
| --- | --- |
| 63 amp single phase | 1 |
| 125 amp 3 phase | 1 |
| 63 amp 3 phase | 2 |
| Note, either 125amp 3 phase or 2 X 63amp 3 Phase can be use by way of a shunt |

Ladders

| Zarges A-Frame Ladder | 1 |
| --- | --- |
| Straight Ladder | 1 |
| Little Giant Step Ladder | 1 |
| Tallescope | 1 |

Pianos

| Yamaha C7 Grand Piano | 1 |
| --- | --- |
| Yamaha Clavinova Elec Piano | 1 |

Pyrotechnics

| Le Maitre Pyro Flash Controller | 1 |
| --- | --- |
| Le Maitre Rapid Fire Unit | 1 |
| Various Pyro FX on request, we do hold some standard effects |

Stage FX

| Look Unique 2.1 Hazer | 2 DSL + DSR |
| --- | --- |
| LeMaitre Mini MIst | 2 |
| LeMaitre Pea Souper | 2 |
| Magic FX Swirl Fan | 1 |

### Lights

| Avolites Pearl Expert | 1 |
| --- | --- |
| Light Processor Dimmer Racks | 288 Channels |
| Long nosed Parcans | 110 |
| Short nosed Parcans | 6 |
| Floor Cans | 10 |
| 26° Source 4 junior | 2 |
| 25°/50° Source 4 zoom | 4 |
| 15°/30° Source 4 | 8 |
| Fresnell | 18 |
| Star Cloth + Light source | 1 |
| 1.2 HMI Follow Spot | 2 (With mechanical dimmer, 4 colour changer and iris control) |
| Mirror Ball | 1 |

LED and Moving heads

| Prolights Moonstone Moving Spot | 6 |
| --- | --- |
| Prolights Diamond 19 moving wash | 4 |
| Visage LED HyperMOVE | 12 |
| LumiPar 18Q pro | 10 |
| Prolights Studio Cobs | 10 |

Projection

| Christie D12HD-H | 1 |
| --- | --- |
| Draper UFS Fastfold Screen, 498cm X 284cm 16:9 | 1 |
| CYP Switchable HDMI & VGA HDBaseT Transmitter | 1 (from stage or control room) |

### Sound

| Yamaha LS9 32 Channel | 1 |
| --- | --- |
| KV2 ESD15 | 4 Flown Focused on tiered seating |
| KV2 ESD6 | 4 Front Fills |
| KV2 ESD12 | 2 Stage left and Right |
| OHM TRS 218 | 2 |
| EV SX300 speaker | 2 Flown stage monitors |
| TurboSound TXD-12M Monitors | 6 |
| KV2 ESP 4000 | 1 |
| QSC RMX 1850HD Amp | 3 |
| Amcron Geodyne Amp | 3 |
| Microphones |  |
| SM 58 | 3 |
| Studio Spares S900 | 3 |
| SM 57 | 2 |
| Sennheiser E845 | 2 |
| Crown PZM Boundry mic | 3 |
| AKG 747 | 6 |
| AKG D12 | 1 |
| AKG D112 | 1 |
| AKG C1000s | 2 |
| Sennheiser e604 | 3 |
| Rode NT4 | 2 |
| Wireless Systems |
| Sennheiser EW300 G2 Hand Held e935 | 2 |
| Sennheiser EW300 G2 Hand Held e945 | 2 |
| Sennheiser EW300 G2 Belt Packs | 16 |
| Sennheiser EW300 G2 Receiver | 16 |
| Sennheiser A 1031-U Antenna | 2 |
| Sennheiser EM 1-E | 4 |
| Outboard and Playback |  |
| Denon CD Player | 1 |
| Sony Mini Disk Player | 3 |
| iMac | 1 with QLab Pro Installed |
| Focusrite 2i2 | 1 |
| Lexicon MPX550 | 1 |

Octagon Room

Sound

| Yamaha MG12 XU | 1 |
| --- | --- |
| KV2 EX6 | 2 |
| EV SB180 | 1 |
| Sennheiser XS wireless Channel 70 Handheld Transmitter | 2 |
| Sennheiser XS wireless Channel 70 Reciever | 2 |

### Lights

| Jands Stage CL | 1 |
| --- | --- |
| Prolights Display Cobs | 10 |
| Dimmable house lights through desk |  |