EXTERNAL DECORATION OF RIVERBANK HOUSE

FOR

TORRIDGE DISTRICT COUNCIL

Preliminaries/General Conditions

Small Projects Version

(Minor Works Contract)

| Issue Number: | 1.0 | Date: | Dec 2009 |
| --- | --- | --- | --- |
| Approved: | A Waite | Next Review Date |  |

Specification for Minor Works Contract Preliminaries

Contents

A	Preliminaries/General Conditions

| A10 PROJECT PARTICULARS |  |
| --- | --- |
| A11 TENDER AND CONTRACT DOCUMENTS |  |
| A12 THE SITE/EXISTING BUILDINGS |  |
| A20 MW THE CONTRACT |  |
| A30 TENDERING/SUB-LETTING/SUPPLY |  |
| A31 PROVISION, CONTENT AND USE OF DOCUMENTS |  |
| A32 MANAGEMENT OF THE WORKS |  |
| A33 QUALITY STANDARDS/CONTROL |  |
| A34 SECURITY/SAFETY/PROTECTION |  |
| A36 FACILITIES/TEMPORARY WORK/SERVICES |  |
| A37 OPERATION/MAINTENANCE OF THE FINISHED BUILDING |  |
| A38 EXECUTION OF WORK AND DAMAGES IN THE EVENT OF DELAY. |  |
| A39 CONTINGENCIES |  |

| A10 PROJECT PARTICULARS: |
| --- |
| Names of Parties: The following terms where appearing in the conditions of Contract, Specification of Works or other context in connection with this Contract shall be construed as follows: |
| 100 | Employer and Client: | The Chairman and Councillors, Torridge District Council, Riverbank House, BIDEFORD. EX39 2QG. |  |
| 110 | The Principal Contractor: The Contractor. | The person or persons who have duly entered into a legal contract with the Employer for the execution of the Works and shall include his heirs, executors, administrators and assignees. |  |
| 120 | Contract Administrator (hereinafter referred to as ‘CA’): | Mr Simon Hoare MCIAT Torridge District Council, Riverbank House, BIDEFORD. EX39 2QG. |  |
| 130 | CDM Co-ordinator: | Andrew Waite FRICS Torridge District Council, Riverbank House, BIDEFORD. EX39 2QG. |  |
| 140 | The Project Nature: | Decoration and minor repairs to maintain the outside of the building. |  |
| 150 | Location: | Riverbank House, BIDEFORD Devon. EX39 2QG |  |
| A11 | DRAWINGS AND OTHER DOCUMENTS |  |
|  | All Plans, drawings and other documents relating to the contract are available to download on www.devontenders.gov.uk |  |
| 100 | THE TENDER DRAWINGS are: as identified in the Specification and Tender Documents. |  |
| 110 | THE CONTRACT DRAWINGS will be the same as the tender drawings. |  |
| 120 | THE PRE-TENDER HEALTH AND SAFETY PLAN is identified in these preliminaries under Section A34. It refers to information given elsewhere in the preliminaries, specification and drawings. |  |
| A12 | THE SITE/EXISTING BUILDINGS The building consists of a two storey (ground & first floor) modern building with a flat roof. Located near the River Torridge |  |
| 110 | THE SITE: Comprises the curtilage and buildings identified in the Schedule of Works and/or drawings. |  |
| 120 | EXISTING MAINS/SERVICES: The contractor shall allow for all precautions to secure all sewers, drainage connections, gas, water, telephone and electrical mains, services and lines to avoid injury by or through carrying out the works. Diversions of any services will only be carried out with approval of the CA. The contractor should liaise with all Utility Companies in respect of existing and new services and equipment to be installed on site. Services shall be identified on the Utility plans but the contractor shall be responsible to locate all services on site. |  |
| 130 | Any damage to services within or around the building resulting from execution of the works shall be notified to the CA immediately and any appropriate service authority. The Contractor shall be responsible for making arrangements for any damage to be made good, to the satisfaction of the service authority or private owners as appropriate, including any consequential damage, all at his own expense. |  |
| 200 | ACCESS TO THE SITE: is as identified on the drawings. The contractor’s access will be restricted to normal working hours between 8am and 7pm. Working out of hours will not normally be permitted and must always be by prior written agreement with the Contract Administrator. |  |
| 210 | USE OF THE SITE: Do not use the site for any purpose other than carrying out the Works Approval shall be obtained for the siting of temporary equipment, access routes, etc which shall be reinstated to their original condition on completion. The contractor shall allow for any protection of internal fixtures and fittings such as furniture, floor coverings etc; covering up during progress if deemed necessary, and subsequent replacement to the satisfaction of the CA. |  |
| 220 | SURROUNDING LAND/BUILDING USES: Adequate protection shall be allowed for and the contractor shall be responsible for making good any damage caused. |  |
| 230 | RISKS TO HEALTH AND SAFETY Working at height. Staff and members of the public moving into and out of the building. |  |
| 240 | SITE VISIT: Before tendering, the Contractor should inspect the drawings and visit the site to satisfy himself as to the local conditions and accessibility of the site of the operation. The Contractor should take into account the supply of and conditions affecting labour, water or services and any other conditions which may affect the execution of works, ascertaining any additional charges as no allowance or claim in respect of want of knowledge will be entertained. Also, no allowance can be made for the omission of any item, which can be implied by the drawings or Specification taken either separately or together forming part of this Contract. |  |
| 250 | SITE VISITS may be made by appointment with the CA. Access for the purpose of initial survey and for carrying out the works, is to be pre-arranged with the Contract Administrator, Mr Andrew Champion on Bideford (01237) 428753. |  |
|  | A20 THE CONTRACT |  |
| 100 | AGREEMENT FOR MINOR WORKS 2005: The form of contract will be the JCT Agreement for Minor Building Works 2005 Edition Revision 2, 2009 incorporating all current amendments. Nothing in these preliminaries shall override or be deemed to override the JCT Agreement for Minor Building Works 2005 Revision 2, 2009. (Prior to completion of this section refer to the MW User Checklist Appendix A) |  |
|  | RECITALS 1-5 1st Recital The work is identified in the Contract particulars. Architect/Contract Administrator: See Section A10. 2nd Recital Documents are as identified in the Specification. 3rd Recital Priced schedule of rates. 4th Recital The Quantity Surveyor shall be the Client. |  |
|  | 5th Recital Project is not notifiable CDM Co-ordinator is as A10. Name and Address of Principal Contractor is as A10. CDM Planning Period (2 weeks) Commencement date/End Date Alternative A will apply Alternative B will be deleted 6th Recital Not applicable 7th Recital Not applicable Sustainable Development and Environmental (schedule 3 para 4) will not apply. |  |
|  | ARTICLES 1-5 Article 3: The Architect/Contract Administrator shall mean Torridge District Council. Article 4: Alternative 3 shall be deleted. Delete Article 7B and Article 7A shall appoint as Article 6. CONDITIONS 1-9 |  |
|  | 4.5 Final Certificate Not applicable |  |
|  | 4.6 Contribution, levy and tax changes This clause to be deleted |  |
|  | 5.2 Value Added Tax Clause B1.1 of the Supplementary Memorandum does not apply. |  |
|  | 6.2 Injury or damage to property - public liability. Insurance cover to be not less than £5,000,000. |  |
|  | 6.3B Insurance of the Works and any existing structures by Employer/Contractor - Fire etc. Clause 6.3A/6.3B will be deleted. (Delete as applicable) 920 Construction Industry Scheme The Contractor’s attention is drawn to The Construction Industry Scheme, which came into effect on the 1st August 1999. The provisions of this Scheme are set out in the Inland Revenue Booklet IR 14/15 (CIS). The Contractor will be required to satisfy the Employer that he had a valid Registration Chart (CIS4) or Subcontractors Tax Certificate (CIS6) or Construction Tax Certificate (CIS5) as indicated in the booklet. |  |
|  | The Contractor is specifically reminded that it is his duty and responsibility to satisfy himself as to the status of all subcontractors whether nominated or otherwise. |  |
| 110 | VALUE ADDED TAX. The Contractor will be required where applicable to pay such rate of tax as is legally demandable on the costs of the supply of goods and services to him by suppliers and sub-contractors, where nominated or otherwise. |  |
| 111 | When submitting tender Contractors shall not include for any output Value Added Tax, which may become chargeable to the Council under the Act but Contractors shall, when submitting their accounts, include tax invoices in accordance with the Act. Tax invoices shall be submitted for each Work Order issued by the Council. |  |
| A30 | TENDERING/SUB-LETTING/SUPPLY |  |
|  | MAIN CONTRACT TENDERING |  |
| 100 | SCOPE: These conditions are supplementary to those stated in the invitation to tender and on the Form of Tender. |  |
| 110 | PRICING INSTRUCTIONS: The tenderer is required to submit with his tender, a fully priced preambles and schedule of works and the total carried forward to a Summary of Building Costs. |  |
| 120 | TENDERING PROCEDURE will be in accordance with the principles of the Construction Industry Board “Code of Practice for the selection of Main Contractors” clause 4.7 with the overall price dominant. |  |
| 130 | EXCLUSIONS: If the Contractor cannot tender for any part(s) of the work as defined in the tender documents he must inform the CA as soon as possible, defining the relevant part(s) and stating the reasons for his inability to tender. |  |
| 140 | ACCEPTANCE OF TENDER: The Employer and his representatives: Offer no guarantee that the lowest or any tender will be recommended for acceptance or accepted. Tenders will be accepted and assessed based on value for Money measures and as such the lowest tender may not be successful. The Employer will not be responsible for any cost incurred in the preparation of any tender in the event of any tenderer withdrawing a tender before acceptance or declining to accept a formal contract on being called upon to do so after his or their tender has been accepted by or on behalf of the Employer for a period of 12 months following the date of withdrawal. The tender shall be accepted by official electronic order. All invoices must show this order number for payment. |  |
| 150 | PERIOD OF VALIDITY: Tenders must remain open for consideration (unless previously withdrawn) for not less than 8 weeks from the date fixed for the submission of tenders. Information on the date for possession/ commencement is provided in the Form of Tender. |  |
| 160 | PROJECTS WITHOUT QUANTITIES: Tenders must include for all work shown or described in the tender documents as a whole or clearly apparent as being necessary for the complete and proper execution of the Works. |  |
| 170 | PRICING OF SPECIFICATION: Alterations and qualifications to the specification must not be made without the written consent of the CA. Tenders containing unauthorised alterations or qualifications may be rejected. Costs relating to items in the specification, which are not priced will be deemed to have been included elsewhere in the tender. |  |
| 171 | FIXED PRICE: Tenders shall be submitted on a fixed price basis on every respect. The tenderer shall allow for all fluctuations in the prices of labour and materials and ensure they have been taken into account. |  |
| 172 | VALUE ADDED TAX: Tenders shall be submitted exclusive of V.A.T. The Contractor will be entitled to recover the VAT for which the Employer is liable as detailed in the Supplemental Agreement to the Contract. |  |
| 180 | THE PRICED SPECIFICATION must be submitted when requested. |  |
| 190 | A SCHEDULE OF RATES (unpriced) is included with the tender documents. The Contractor may insert additional items. A fully priced copy must be submitted with any tender. |  |
| 200 | TENDER STAGE METHOD STATEMENTS must be submitted within one week of request describing how and when the Contractor proposes and undertakes to carry out the following: works as requested in the Health and Safety Plan. The Contractor may, at his discretion and at the same time, submit method statements for other parts of the Works. |  |
| 210 | ALTERNATIVE TENDERS: In addition to and at the same time as his tender based upon the date or period specified in the Form of Tender, the tenderer may, at his discretion, submit an alternative tender based upon a different date for completion or period. If any such tender is accepted the date for completion inserted in the Appendix to the Contract will be the date stated in the alternative tender or determined from the period stated in the alternative tender. |  |
| 220 | SUBSTITUTE PRODUCTS: If the Contractor wishes to substitute products of different manufacture to those specified, written details must be submitted with the tender giving reasons for each proposed substitution. Substitutions, which have not been notified at tender stage may not be considered. Substitutions sanctioned by the CA will be subject to the verification requirements of clause A31/130. |  |
|  | SUBLETTING/SUPPLY. |  |
| 230 | SUB-CONTRACTORS: No part of the works shall be sub-let to other persons without written consent between the contracting parties. The employer shall have power to obtain estimates and select firms to carry out work covered by prime cost or provisional sums. The Contractor is to ensure that the work of any sub-contractor is covered in all aspects as maintained in the General Conditions and is to obtain written agreement as necessary to comply with same. A Letter of Intent should be obtained from all sub-contractors that they will comply fully to the Principal Contractors Health and Safety Policy - a copy shall be passed to the CA, who shall retain the right to accept or reject Sub-Contractors on the basis of their statement. |  |
| 240 | CORRUPTION: The tendered/contractor shall not offer to give or agree to give any person any gift or consideration of any kind as an inducement or reward for obtaining or executing the contract with the employer. In such circumstances the employer can cancel the contract and recover from the contractor the amount of any loss resulting from the cancellation of the contract. A copy of the Councils Whislteblowing Policy will be issued to the Contractor at the Initial Contract Meeting. |  |
| 250 | RACE RELATIONS: All Contractors shall fully comply to the Provisions of the Race Relations Act 1976 and all subsequent Amendments. All Contractors should have a suitable Policy to exclude racial discrimination in their Company and in relation to sub- contractors and suppliers. |  |
| A31 | PROVISION, CONTENT AND USE OF DOCUMENTS |  |
|  | DEFINITIONS AND INTERPRETATIONS |  |
| 100 | IN WRITING: When required to notify, inform, instruct, agree, confirm, obtain information, obtain approval or obtain instructions do so in writing. |  |
| 110 | APPROVAL means the approval in writing of the CA unless specified otherwise. |  |
| 120 | CROSS-REFERENCES TO THE SPECIFICATION: The Contractor shall check all cross references to or in a specification and report any discrepancies to the CA. |  |
| 130 | EQUIVALENT PRODUCTS: Where the specification permits substitution of a product of different manufacture to that specified and such substitution is desired, before ordering the product notify the CA and, when requested, submit for verification documentary evidence that the alternative product is equivalent in respect of material, safety, reliability, function, compatibility with adjacent construction, availability of compatible accessories and, where relevant, appearance. Submit certified English translations of any foreign language documents. |  |
|  | Any proposal for use of an alternative product must also include proposals for substitution of compatible accessory products and variation of details as necessary, with evidence of equivalent durability, function and appearance of the construction as a whole. If such substitution is sanctioned, and before ordering products, provide revised drawings, specification and manufacturer’s guarantees as required by CA. |  |
| 140 | EQUIVALENT PRODUCTS: Wherever products are specified by proprietary name and the phrase ‘or equivalent’ is not included, it is to be deemed included. |  |
| 150 | REFERENCES TO BSI DOCUMENTS are to the versions and amendments listed in the BSI Standards Catalogue current at the date of tender. |  |
| 160 | SIZES: Unless otherwise stated: Products are specified by their co-ordinating sizes. Cross-section dimensions of timber shown on drawings are nominal sizes before any required planning. |  |
| 170 | FIX ONLY means all labours in unloading, handling, storing and fixing in position, including use of all plant. |  |
| 180 | SUPPLY AND FIX: Unless stated otherwise all items given in the schedule of work and/or on the drawings are to be supplied and fixed complete. |  |
|  | TERMS USED IN REFURBISHMENT/ALTERATION |  |
| 200 | REMOVE means disconnect, dismantle as necessary and remove the stated element, work or component and all associated accessories, fastening, supports, linings and bedding materials, and dispose of unwanted materials. It does not include removing associated pipework, wiring, ductwork or other services. |  |
| 210 | KEEP FOR REUSE means: During removal prevent damage to the stated components or materials, and clean off bedding and jointing materials. Stack neatly, adequately protect and store until required by the Employer or for use in the Works as instructed. |  |
| 220 | REPLACE means: Remove the stated existing components, features and finishes. Provide and fit in lieu new components, features or finishes, which, unless specified otherwise, must match those, which have been removed. Make good as necessary. |  |
| 230 | REPAIR means carry out local remedial work to components, features and finishes as found in the existing building, resecure or refix as necessary and leave in a sound and neat condition. It does not include: - Replacement of components or parts of components. - Redecoration. |  |
| 240 | MAKE GOOD means carry out local remedial work to components, features and finishes which have been disturbed by other, previous work under this Contract and leave in a sound and neat condition. It does not include: - Replacement of components or parts of components. - Redecoration. The meaning of the term shall not be limited by this definition where used in connection with the defects liability provisions of the Contract. |  |
| 250 | EASE means make minor adjustments to moving parts of the stated component to achieve good fit in both open and closed positions and ensure free movement in relation to fixed surrounds. Make good as necessary. |  |
| 260 | TO MATCH EXISTING means use products, materials and methods to match closely all visual characteristics and features of the existing work, with joints between existing and new work as inconspicuous as possible, all to approval of appearance. |  |
|  | DOCUMENTS PROVIDED ON BEHALF OF EMPLOYER |  |
| 270 | DIMENSIONS: The accuracy of dimensions scaled from the drawings is not guaranteed. Obtain from the CA any dimensions required but not given in figures on the drawings nor calculable from figures on the drawings. |  |
| 280 | THE SPECIFICATION: All sections of the specification must be read in conjunction with Main Contract Preliminaries/General Conditions. |  |
|  | DOCUMENTS PROVIDED BY CONTRACTOR |  |
| 290 | TECHNICAL LITERATURE: The Contractor is required to keep copies of the following on site, readily accessible for reference by all supervisory personnel: Manufacturers’ current technical literature relating to all products to be used in the Works. Those parts of BS 8000 ‘Workmanship on Building Sites’ which are invoked in the specification. |  |
| 300 | MAINTENANCE INSTRUCTIONS AND GUARANTEES: Retain copies delivered with components and equipment (failing which, obtain), register with manufacturer as necessary and hand over to CA on or before Practical Completion. |  |
| 310 | VARIATIONS: All variations shall be approved in writing prior to execution. No variation shall vitiate the contract. The basis of valuation of variations shall be in accordance with the original pricing for the contract or the schedule of rates. Where works are on a daywork basis they shall be according to the Daywork schedule, which forms part of the contract. Where requested the contractor shall submit dayworks sheets detailing labour, plant and materials within 1 week for these works. |  |
| 320 | IDENTIFICATION CARDS: The Contractor shall ensure that all members of staff who visit Council Properties carry and shown an identification card which has on it a photograph of the employee, contractors name and telephone number. |  |
| A32 | MANAGEMENT OF THE WORKS |  |
| 100 | INSURANCES: Before starting work on site submit satisfactory documentary evidence and/or policies and receipts for the insurances required by the Conditions of Contract. |  |
| 110 | INSURANCE CLAIMS: If any event occurs which may give rise to any claim or proceeding in respect of loss or damage to the Works or injury or damage to persons or property arising out of the Works, forthwith give notice in writing to the Employer, the CA and the Insurers. Indemnify the Employer against any loss, which may be caused by failure to give such notice. |  |
| 120 | OWNERSHIP: Materials arising from the alteration work are to become the property of the Contractor except where otherwise stated. Remove from site as work proceeds. |  |
| 130 | HARDCORE: Brick rubble or other hard materials arising from the work may be reused as hardcore, subject to compliance with the specification. |  |
| 140 | PROGRAMME: As soon as possible and before staring work on site prepare in an approved form a programme for the Works, which must make allowance for all: - Planning and mobilisation by the Contractor - Subcontractor’s work - Running in, adjustment and testing of engineering services - Work resulting from instructions issued in regard to the expenditure of provisional sums - Work by others concurrent with the Contract Submit 2 copies to CA. |  |
| 150 | CA’S SITE MEETINGS: The CA will hold site meetings to review progress and other matters. Meetings will normally be held monthly. Ensure the availability of accommodation and attend all such meetings. The CA will chair the meetings but it will be the Contractors responsibility to take and distribute the minutes. |  |
| 160 | NOTICE OF COMPLETION: Give CA at least 1 week’s notice of the anticipated dates of practical completion of the whole or parts of the Works. |  |
| 170 | ESTIMATED COST OF VARIATIONS: If the CA issues details of a proposed instruction with a request for an estimate of cost, submit such an estimate without delay and in any case within 7 days. |  |
| 180 | MEASUREMENTS: Give reasonable notice to the Quantity Surveyor before covering up work, which the Quantity Surveyor requires to be measured. |  |
| 190 | INTERIM VALUATIONS: At least 7 days before the established dates for interim valuations submit to the CA details of amounts due under the Contract together with all necessary supporting information. |  |
| 200 | REMOVAL OF WORKPERSONS: The right is reserved for immediate removal of any workperson who in the opinion of the CA is incompetent. |  |
| 210 | OVERTIME. Should the rate of progress lag so as to endanger the completion of the Contract within the time stated in the Appendix to the Contract Conditions or within any extended time fixed under clause 2.2 of the said conditions, the Contractor shall arrange for overtime to be worked at his own expense. |  |
| 211 | Should the Contractor wish to work other than the recognised hours, he shall give notice in writing to the Contract Administrator who will (in agreement with the Property Manager) grant permission if he considers the proposals reasonable and the Contractor shall make all necessary provisions for carrying out the works in a proper and safe manner. The Contract Administrator reserves to himself the right to instruct the Contractor to work abnormal hours where he considers there is undue delay in completing the Contract. Where permission or instructions are given the Contractor shall not be entitled to any additional payments for such working except where the ‘Contract Administrator agrees that such working is occasioned by virtue of conditions unascertainable at the date of Tender and it is confirmed in writing. |  |
| 220 | SITE ADMINISTRATION. The Contractor shall allow in his Tender for all on and off site management costs. |  |
| A33 | QUALITY STANDARDS/CONTROL |  |
|  | MATERIALS AND WORK GENERALLY |  |
| 110 | CONTRACT GOOD PRACTICE: Where and to the extent that materials, products and workmanship are not fully detailed or specified they are to be: Of a standard appropriate to the Works and suitable for the functions stated in or reasonably to be inferred from the project documents, and In accordance with good building practice. |  |
| 120 | GENERAL QUALITY OF PRODUCTS: Products to be new unless otherwise specified. For products specified to a British or European Standard obtain certificates of compliance from manufacturers when requested. Where a choice of manufacturer or source is allowed for any particular product, the whole quantity required must be of the same type, manufacture and/or source unless otherwise approved. Produce written evidence of sources of supply when requested. Ensure that the whole quantity of each product required is of consistent kind, size, quality and overall appearance. Where consistency of appearance is desirable ensure consistency of supply from the same source. Do not use different colour batches where they can be seen together. If products are prone to deterioration or have a limited shelf life, order in suitable quantities to a programme and use in appropriate sequence. Do not use if there are any signs of deterioration, setting or other unsatisfactory condition. No asbestos based products are permitted. |  |
| 130 | PROPRIETARY PRODUCTS: Handle, store, prepare and use or fix each product in accordance with its manufacturer’s current printed or written recommendations. Inform CA if these conflict with any other specified requirement. Submit copies when requested. The tender will be deemed to be based on the products specified and recommendations on their use given in the manufacturer’s literature current at the date of tender. Where British Board of Agreement certified products are used, comply with the limitations, recommendations and requirements of the relevant valid certificates. Concrete cast insitu / precast testing shall be carried out. |  |
| 140 | CHECKING COMPLIANCE OF PRODUCTS: Check all documentation and the products themselves to ensure compliance with the project documents. Where different types of any product are specified, check to ensure that the correct type is being used in each location. In particular, check that: The sources, types, qualities, finishes and colours are correct, and match any approved samples. All accessories and fixings, which should be supplied with the products, have been supplied. Sizes are correct. Where tolerances are critical, measure a sufficient quantity to ensure compliance. The delivered quantities are correct, to ensure that shortages do not cause delays in the work. The products are clean, undamaged and in good condition. Products, which have a limited shelf life, are not out of date. |  |
| 150 | PROTECTION OF PRODUCTS: Prevent over-stressing, distortion and other damage. Keep clean and free from contamination. Prevent staining, chipping, scratching or other disfigurement, particularly of products exposed to view in the finished work. Keep dry to prevent premature setting, moisture movement and similar defects. Where appropriate store off the ground and allow free air movement between stored products. Prevent excessively high or low temperatures and rapid changes of temperature in the products. Protect adequately from rain, damp, frost, sun and other elements as appropriate. Ensure that products are at a suitable temperature and moisture content at time of sue. Ensure that sheds and covers are of ample size, in good weatherproof condition and well secured. Keep different types and grades of products separately and adequately identified. Keep products in their original wrappings, packings or containers, until immediately before they are used. Wherever possible retain protective wrappings after fixing and until shortly before Practical Completion. Ensure that protective measures are fully compatible with and not prejudicial to the products/materials. |  |
| 160 | SUITABILITY OF RELATED WORK AND CONDITIONS: Provide all trades with necessary details of related types of works. Before starting each type of work, ensure that: Previous work is appropriately complete, in accordance with the project documents, to a suitable standard and in a suitable condition to receive the new work. All necessary preparatory work has been carried out, including provision for services, openings, supports, fixings, damp proofing, priming and sealing. The environmental conditions are suitable, particularly that the building is suitably weathertight. |  |
| 170 | GENERAL QUALITY OF WORKMANSHIP: Operatives must be appropriately qualified, skilled and experienced for the type and quality of work, i.e. ACOPS, plant and machinery. Take all necessary precautions to prevent damage to the work form frost, rain and other hazards. Inspect components and products carefully before fixing or using and reject any, which are defective. Fix or lay securely, accurately and in alignment. Provide suitable, packings at screwed and bolted fixings to take up tolerances and prevent distortion. Comply with correct torque settings. Adjust location and fixing of components and products so that joints, which are left open to view, are even and regular. Ensure that all moving parts operate properly and freely. Do not cut, grind or plane pre-finished components and products to remedy binding or poor fit without approval. |  |
| 180 | BS 8000: BASIC WORKMANSHIP: Where BS 8000 gives recommendations on working methods, compliance will be deemed to be a matter of industry good practice and not a requirement of the CA. If there is any conflict or discrepancy between the recommendations of BS 8000 on the one hand and the project documents on the other, the latter will prevail. |  |
| 190 | WATER FOR THE WORKS: If other than mains supply is proposed provide evidence of suitability. |  |
| 200 | Where applicable the water supply installation and fittings shall comply to the Water Supply (Water Fittings) Regulations 1999 or as current. |  |
|  | SAMPLES/APPROVALS |  |
| 210 | SAMPLES: Where approval of a product is specified the requirement for approval relates to a sample of the product and not to the product as used in the Works. Submit a sample or other evidence of suitability. Do not confirm orders or use the product until approval of the sample has been obtained. Retain approved sample in good, clean condition on site. Ensure that the product used in the Works matches the approved sample. |  |
| 220 | APPROVALS: Where and to the extent that products or work are specified to be approved or the CA instructs or requires that they are to be approved, the same must be supplied and executed to comply with all other requirements and in respect of the stated or implied characteristics either: To the express approval of the CA or To match a sample expressly approved by the CA as a standard for the purpose. |  |
|  | ACCURACY/SETTING OUT GENERALLY |  |
| 230 | SETTING OUT: Check the levels and dimensions of the site against those shown on the drawings, and record the results on a copy of the drawings. Notify CA in writing of any discrepancies and obtain instructions before proceeding. |  |
| 240 | SETTING OUT: Inform CA when overall setting is complete and before commencing construction. |  |
| 250 | APPEARANCE AND FIT: Arrange the setting out, erection, juxtaposition of components and application of finishes to ensure satisfactory fit at junctions, no practically or visually unacceptable changes in plane, line or level and a true, regular finished appearance. Wherever satisfactory accuracy, fit and/or appearance of the work are likely to be critical or difficult to achieve obtain approval of proposals or of the appearance of the relevant aspects of the partially finished work as early as possible. |  |
|  | SERVICES GENERALLY |  |
| 260 | SERVICES REGULATIONS: Any work carried out to or which affects new or existing services must be in accordance with the Bye Laws or Regulations of the relevant Statutory Authority. |  |
| 270 | SERVICE RUNS: Make adequate provision for services, including unobstructed routes and fixings. Wherever possible ducts, chases and holes are to be formed during construction rather than cut. |  |
| 280 | MECHANICAL AND ELECTRICAL SERVICES must have final tests and commissioning carried out so that they are in full working order at practical completion. |  |
|  | SUPERVISION/INSPECTION/DEFECTIVE WORK |  |
| 290 | DEFECTS IN EXISTING CONSTRUCTION to be reported to CA without delay. Obtain instructions before proceeding with work which may: Cover up or otherwise hinder access to the defective construction, or Be rendered abortive by the carrying out of remedial work. |  |
| 300 | TIMING OF TESTS AND INSPECTIONS: Agree dates and times of tests and inspections with CA several days in advance, to enable the CA and other affected parties to be present. On the previous working day to each such test or inspection confirm that the work or sample in question will be ready or, if not ready, agree a new date and time. |  |
| 310 | PROPOSALS FOR RECTIFICATION OF DEFECTIVE WORK/PRODUCTS: As soon as possible after any part(s) of the work or any products are known to be not in accordance with the Contract, or appear that they may not be in accordance, submit proposals to CA for opening up, inspection, testing, making good, adjustment of the Contract Sum, or removal and re-execution. Such proposals may be unacceptable to the CA, and he may issue contrary instructions. |  |
|  | WORK AT OR AFTER PRACTICAL COMPLETION |  |
| 320 | GENERALLY: Make good all damage consequent upon the work. Remove all temporary markings and protective coverings. Clean the works thoroughly inside and out including all accessible ducts and voids, remove all splashes, deposits, efflorescence, rubbish and surplus materials. Cleaning materials and methods to be as recommended by manufacturers of products being cleaned, and to be such that there is no damage or disfigurement to other materials. Obtain COSHH dated data sheets for all materials used for cleaning and ensure they are used only as recommended by their manufacturers. Touch up minor faults in newly painted/repainted work, carefully matching colour. Repaint badly marked areas back to suitable breaks or junctions. Adjust, ease and lubricate moving parts as necessary to ensure easy and efficient operation, including doors, windows, drawers, ironmongery, appliances, valves and controls. |  |
| 330 | SECURITY AT PRACTICAL COMPLETION: Leave the Works secure with all accesses locked. Account for and adequately label all keys and hand over to Employer with itemised schedule, retaining duplicate schedule signed by Employer as a receipt. |  |
| 340 | MAKING GOOD DEFECTS: Make arrangements with the CA and give reasonable notice of the precise dates for access to the various parts of the Works for purposes of making good defects. Inform CA when remedial works to the various parts of the Works are completed. |  |
| 350 | MAINTENANCE PERIODS. The Contractor shall be responsible for a period of three months after the certificate of practical completion of the works for correction, entirely at his own expense, any defect or imperfection which may arise during this period, whether due to poor materials, defective workmanship or what ever other source is attributable under the Conditions of Contract. |  |
| 351 | The Contractor shall be responsible for a period of twelve months after the certificate of practical completion of the works for correction, entirely at his own expense, any defect or imperfection which may arise during this period, whether due to poor materials, defective workmanship or what ever other source is attributable under the Conditions of Contract. |  |
| 360 | ACTS AND BUILDING REGULATIONS. The work is to be carried out in conformity with Building Regulations as amended from time to time, or Acts of Parliament for the time being in force, through the duration of the Contract. |  |
| 370 | ATTENDANCE. All works are to be carried out by skilled workman controlled by a competent foreman who is used to the particular class of works being carried out. A site foreman is to be employed on the site throughout the duration of the contract and to whom instructions can be given in the absence of the Contractor. |  |
| 380 | FEES & CHARGES. The Contractor shall comply with the provisions of any Acts of Parliament relating to the Works and to the regulations and By-Laws of the Local Authorities and he shall give all notices required, and pay all fees, charges in connection therewith. |  |
| 390 | SHEDS, EQUIPMENT & VEHICALS. The Contractor is to allow in his tender and provide all ropes, ladders, scaffolding, vehicles and plant necessary for the proper execution of the work. This shall also include the provision of sheds for materials, shelter and heating for workmen, offices and canteen where necessary and a clean, thoroughly deodorised sanitary convenience. Allowance is to be made for the removal of all such items at completion and for the removal of all such items where and when directed by the Contract Administrator. |  |
| 391 | All apparatus used on site must be robust enough to safely carry out its required function. It should be maintained and repaired by a competent person. All portable and hand held electrical tools should operate on an 110V supply, use transformers when the only available supply is 240V. Include for bringing to site maintaining and removing on completion. |  |
| A34 | SECURITY/SAFETY/PROTECTION |  |
|  | GENERALLY |  |
| 100 | THE PRE-TENDER HEALTH AND SAFETY PLAN is integral with the project Preliminaries, including but not restricted to the sections set out below: Nature of the project: Sections A10 and A13. The existing environment: Section A12. Existing drawings: Section A11 and A12. The design: Section A34. Construction materials: Section A34. Site-wide elements: Section A12. Overlap with client’s undertaking: Sections A34 and A36. Site Rules; Sections A34 and A35. Continuing Liaison: Section A31. |  |
| 120 | THE CONSTRUCTION PHASE HEALTH AND SAFETY PLAN developed from the Pre-tender Health and Safety Plan must be submitted to the CA not less than 2 weeks before the proposed date for start of construction work. Construction work must not commence until the Employer has confirmed in writing that in his view the Construction Phase Health and Safety Plan includes the procedures and arrangements required by the CDM Regulations. The plan must include: Detailed proposals for managing health and safety during the construction phase together with site rules and emergency procedures. Method statements related to the hazards identified in the pre-tender health and safety plan and/or statements on how the hazards will be addressed and other significant hazards identified by the Contractor. |  |
| 130 | HSE APPROVED CODES OF PRACTICE: Comply with the following: Management of health and safety at work. Managing construction for health and safety. Asbestos regulations. |  |
| 140 | SECURITY: Adequately safeguard the site, the Works, products, materials, plant, and any existing buildings affected by the Works from damage and theft. Take all reasonable precautions to prevent unauthorised access to the site, the Works and adjoining property. |  |
| 141 | The Contractor shall provide all necessary day watching to ensure the safety of the public, the Contractor’s own employees and the authorised agents of the Employer. The sole responsibility for the safety of the Works, for any damage or theft and for the proper protection of the public will rest with the Contractor. |  |
| 142 | The Contractor shall maintain proper discipline over workman employed on the Works and will be held entirely responsible for any loss or damage occasioned by neglect in this particular. |  |
| 143 | The Contractor and his workmen are not to trespass on neighbouring properties or land. Only by agreement with the owners and occupiers concerned may they enter these properties or land and every endeavour must be made to avoid inconvenience. |  |
|  | The Contractor shall ensure that all buildings are maintained in a secure condition at all times and that no equipment is left unattended and insecure that may be used to gain access or exit to and from the building. The Contractor Shall ensure that unauthorised access to ladders; scaffolding and unauthorised use of plant cannot be made at any time. The Contractor shall be responsible for the security of his own plant and materials not fixed. |  |
| 150 | STABILITY: Accept responsibility for the stability and structural integrity of the Works during the Contract, and support as necessary. Prevent overloading: details of design loads may be obtained from CA. |  |
| 160 | OCCUPIED PREMISES: Existing buildings will be occupied and/or used during the Contract as follows: as identified in the Specification and Health and Safety Plan. Carry out the Works without undue inconvenience and nuisance and without danger to occupants and users. If it transpires that compliance with this clause requires certain operations to be carried out during overtime, and such overtime is not required for any other reason, the extra cost will be paid to the Contractor, provided that such overtime is authorised by the CA in advance. |  |
| 170 | EMPLOYER’S REPRESENTATIVES SITE VISITS: Inform the CA in advance of all safety provisions and procedures (including those relating to materials which may be deleterious), which will require the compliance of the Employer or his representatives when visiting the site. Provide protective clothing and/or equipment for the Employer and his representatives as appropriate. |  |
|  | PROTECT AGAINST THE FOLLOWING: |  |
| 180 | NOISE: Comply generally with the recommendations of BS 5228: Part 1, clause 9.3 for minimising noise levels during the execution of the Works. Noise levels from the works are to be kept below 85 dB(A) when measured from the site boundary between 9.00am and 5.00pm. Fit all compressors, percussion tools and vehicles with effective silencers of a type recommended by manufacturers of the compressors, tools or vehicles. Do not use pneumatic drills and other noisy appliances during the period 5.00pm to 9.00am without consent of the CA. Do not use or permit employees to use radios or other audio equipment in ways or at times which may cause nuisance. |  |
| 190 | POLLUTION: Take all reasonable precautions to prevent pollution of the site, the Works and the general environment including streams and waterways. |  |
| 200 | USE OF PESTICIDES: Use only where specified or approved, and then only suitable products as listed in the UK Pesticide Guide. Where work is near water, drainage ditches or land drains, comply with the MAFF guidelines for the use of herbicides on weeds in or near watercourses and lakes. Observe all precautions recommended by the manufacturer and remove containers from site immediately they have been emptied or are no longer required. Operatives must hold a BASIS Certificate of Compliance, or work under the supervision of a Certificate holder. |  |
| 210 | NUISANCE: Take all necessary precautions to prevent nuisance from smoke, dust, rubbish, vermin and other causes. |  |
| 220 | FIRE PREVENTION: Take all necessary precautions to prevent personal injury, death, and damage to the Works or other property from fire. Comply with Joint Code of Practice ‘Fire Prevention on Construction Sites’ published by the Building Employers Confederation, the Loss Prevention Council and the National Contractors’ Group. |  |
| 230 | FIRE PREVENTION: Smoking will not be permitted on the site. |  |
| 240 | MOISTURE: Prevent the work from becoming wet or damp where this may cause damage. Dry out the Works thoroughly. Control the drying out and humidity of the Works and the application of heat to prevent: Blistering and failure of adhesion. Damage due to trapped moisture. Excessive movement. |  |
| 250 | INFECTED TIMBER: Where instructed to remove timber affected by fungal/insect attack from the building, do so in a way, which will minimise the risk of affecting other parts of the building. |  |
| 260 | WASTE: Remove rubbish, debris, surplus material and spoil regularly and keep the site and Works clean and tidy. Remove all rubbish, dirt and residues from voids and cavities in the construction before closing in. Ensure the non-hazardous material is disposed of at a tip authorised by a Waste Regulation Authority. Remove all surplus materials and their containers regularly for disposal off site in a safe and competent manner as approved by a Waste Regulation Authority and in accordance with relevant regulations. Retain waste transfer documentation on site. |  |
| 270 | ASBESTOS: Comply with Asbestos at Work Regulations and all associated Codes of Practice and amendments to the legislation. |  |
|  | PROTECT THE FOLLOWING: |  |
| 280 | WORK IN ALL SECTIONS: Adequately protect all types of work and all parts of the Works, including work carried out by others, throughout the Contract. Wherever work is of an especially vulnerable nature or is exposed to abnormal risks provide protection to ensure that damage does not occur. |  |
| 290 | EXISTING SERVICES: Notify all service authorities and adjacent owners of the proposed works not less than one week before commencing site operations. Before starting work check positions of existing services. Observe service authorities’ recommendations for work adjacent to existing services. Do not interfere with their operation without consent of the service authorities or other owners. If any damage to services results for the Works, notify CA and appropriate service authority without delay. Make arrangements for making good without delay to the satisfaction of the service authority or other owner as appropriate. Replace marker tapes or protective covers disturbed by site operations to the service authority’s recommendations. |  |
| 300 | ROADS AND FOOTPATHS: Adequately maintain roads and footpaths within the adjacent to the site and keep clear of mud and debris. Any damage to roads and footpaths caused by site traffic or otherwise consequent upon the Works must be made good to the satisfaction of the Local Authority or other owner. Bear any costs arising. |  |
| 310 | TREES/HEDGES/SHRUBS/LAWNS: Adequately protect and preserve, except those, which are to be removed. Replace to approval or treat as instructed any species or areas damaged or removed without approval. |  |
| 320 | EXISTING FEATURES: Prevent damage to existing buildings, fences, gates, walls, roads, paved areas and other site features, which are to remain in position during the execution of the Works. |  |
| 330 | EXISTING WORK: Prevent damage to existing property undergoing alteration or extension and make good to match existing any defects so caused. Remove existing work the minimum necessary and with care to reduce the amount of making good to a minimum. |  |
| 340 | BUILDING INTERIORS: Protect building interiors exposed to the weather during the course of alteration work with temporary closures of sufficient size to permit execution of the work and which will remain weathertight in severe weather. |  |
| 350 | ADJOINING PROPERTY: Prevent trespass of workpeople. Take all reasonable precautions to prevent damage to adjoining property. Obtain permission as necessary from the owners if requiring to erect scaffolding on or otherwise use adjoining property, and pay all charges. Clear away and make good on completion or when directed. Bear the cost of repairing any damage arising from execution of the Works. |  |
| 360 | EXISTING STRUCTURES: Provide and maintain during the execution of the Works all incidental shoring, strutting, needling and other supports as may be necessary to preserve the stability of existing structures on the site or adjoining, that may be endangered or affected by the Works. Support existing structure as necessary during cutting of new openings or replacement of structural parts in accordance with BRE Practice Note GBG 10, 15 and 20 or structural design. Do not remove supports until new work is strong enough to support the existing structure. Prevent overstressing of completed work when removing supports. |  |
| A36 | FACILITIES/TEMPORARY WORK/SERVICES |  |
| 100 | LOCATIONS: Inform CA of the intended siting of all spoil heaps, temporary works and services. |  |
| 120 | MAINTAIN, alter, adapt and move temporary works and services as necessary. Remove when no longer required and make good. |  |
| 130 | TEMPORARY FENCE(S), HOARDING(S) AND ROAD(S): The Contractor shall provide all necessary temporary fencing, scaffolding, screens, fans, planking, roofing, hoardings, footways, guardrails, gantries, etc for the protection of and access to the works, adjoining properties, and the public with suitable openings. The Contractor shall provide all necessary temporary roads, hardstandings, crossings etc that may be required. To be altered and adapted as required and all works cleared away on completion and existing surfaces reinstated. |  |
| 140 | NAME BOARD: Obtain approval for and provide a suitable temporary name board displaying: Title of project. Employers display board 1200 x 300mm. Names of Consultants. Names of Funding Agencies. If the Contractor wishes, names of Contractor and Sub-Contractors. No site advertisements are permitted. |  |
| 150 | LIGHTING: During finishing work and inspection provide temporary lighting, and intensity and direction of which closely resembles that provided by the permanent installation. |  |
| 160 | LIGHTING AND POWER: The Contractor shall provide artificial lighting and power for the works and sub-contractors, including lighting to hoardings, for testing and for temporary installations. The Contractor shall allow for testing all installations and permanent equipment upon completion and issue a Test Certificate prior to practical completion. |  |
| 170 | WATER for the Works will be supplied by the Contractor including all connections, plumbing and storage. Clear away upon completion and reinstate existing surfaces. |  |
| 180 | TEMPERATURE AND HUMIDITY: The permanent heating installation may be used for drying out the Works and controlling temperature and humidity levels, but: The Employer does not undertake that it will be available. The Contractor must take responsibility for operation, maintenance and remedial work, and arrange supervision by and indemnification of the appropriate Sub-Contractors, and pay costs arising. |  |
| 190 | METER READINGS: Where charges for service supplies need to be apportioned ensure that meter readings are taken by relevant authority at possession and/or completion as appropriate. Ensure that copies of readings are supplied to interested parties. |  |
| 200 | PROVISION OF WELFARE FACILITIES AT CONSTRUCTION SITES shall be in accordance with HSE Construction Information Sheet No 46 for Transient Sites and C1518 (revised) for fixed Construction Sites. |  |
| A37 | OPERATION/MAINTENANCE OF THE FINISHED BUILDING |  |
|  | To be read with Preliminaries/General Conditions |  |
| 100 | THE BUILDING MANUAL: The Building Manual (incorporating the Health and Safety File and subtitled accordingly) is to be a comprehensive information source and guide for the Employer and end users providing a complete understanding of the building and its systems and enabling it to be operated and maintained efficiently and safely. The Contractor is required to obtain or prepare all the information to be included in the Manual, produce the required number of copies of the Manual and submit them to the CA for checking by the Planning Supervisor and for delivery to the Employer. |  |
|  | The Manual is to consist of the following three parts: PART 1: GENERAL INFORMATION: Content as clause 120, the information being provided to the Contractor by the CA. PART 2: BUILDING FABRIC INFORMATION: Content as clause 130, plus certain as-built drawings and other information provided to the Contractor by the CA. PART 3: BUILDING SERVICES INFORMATION: Consent as clause 140. The presentation of the Manual is to be as clause 150. A complete draft of the Manual must be submitted to the CA for the comment not less than 2 weeks before the date for submission of the final copies of the Manual. Do not proceed with production of the final copies of the Manual until authorised to do so by the CA. Final copies of the Manual: Provide the CA with 2 copies not less than 2 weeks before Practical Completion. |  |
|  | 110 FORMATION: Content as clause 120, the information being provided to the Contractor by the CA. PART 2: BUILDING FABRIC INFORMATION: Content as clause 130, plus certain as-built drawings and other information provided to the Contractor by the CA. PART 3: BUILDING SERVICES INFORMATION: Consent as clause 140. The presentation of the Manual is to be as clause 150. A complete draft of the Manual must be submitted to the CA for the comment not less than 2 weeks before the date for submission of the final copies of the Manual. Do not proceed with production of the final copies of the Manual until authorised to do so by the CA. Final copies of the Manual: Provide the CA with 2 copies not less than 2 weeks before Practical Completion. |  |
| 110 | THE HEALTH AND SAFETY FILE is an information source and guide for the Employer and end users providing an understanding of the building and its systems and enabling it to be operated and maintained safely. Provide the Planning Supervisor, with 2 copies of the information required below not less than 2 weeks before Practical Completion. A full description to each of the building services installed written to ensure that the Employer’s staff fully understand the scope and facilities provided. Operating and maintenance instructions for all equipment and systems installed. Copies of manufacturers current technical literature and COSHH dated data sheets for all materials, plant and equipment selected by the Contractor. |  |
| 120 | THE BUILDING MANUAL PART 1: GENERAL INFORMATION must include: A description of the buildings. Details of ownership and all consultants and designers. Details of all Authorities plus copies of all consents and approvals obtained. Names, addresses, telephone and fax numbers of all contractors, sub-contractors, suppliers and manufacturers. The fire safety strategy for the building(s) including drawings showing emergency escape routes, location of emergency and fire fighting systems, services shut-off valves, switches, etc, valves, switches, etc. |  |
| 130 | THE BUILDING MANUAL PART 2: BUILDING FABRIC INFORMATION: Provide such information as is reasonably required by the Planning Supervisor including: Copies of manufacturers current literature for all products for which the particular proprietary brand has been chosen by the Contractor, including COSHH dated data sheets and manufacturers recommendations for cleaning and maintenance. Copies of all guarantees, warranties and maintenance agreements offered by sub-contractors and manufacturers. Copies of all test certificates and reports required in the specification. |  |
| 140 | THE BUILDING MANUAL PART 3: BUILDING SERVICES INFORMATION must include: A full description of each of the systems installed including their mode of operation, written to ensure that the Employer’s staff fully understand the scope and facilities provided. Diagrammatic drawings of each system indicating principal items of plant, equipment, valves, etc. The name, address and telephone number of the manufacturer of every item of plant and equipment together with catalogue list numbers. Manufacturers technical literature for all items of plant and equipment, including operating and maintenance instructions. A copy of the Test Certificates for all items and plant and equipment used in the installation. A copy of all manufacturers guarantees, warranties and maintenance agreements offered by sub-contractors and manufacturers. Emergency procedures, including telephone numbers for emergency services. |  |
| 150 | PRESENTATION OF BUILDING MANUAL: The Manual is to be contained A4 size, plastic in covered, loose leaf, four ring binders with hard covers, indexed, divided and appropriately cover titled. Selected drawings larger than A4 are to be folded and accommodated in the binders so that they may be unfolded without being detached from the rings. |  |
| 160 | TRAINING: Before Practical Completion explain and demonstrate the operation of the installation to the Employer’s representatives. |  |
| 170 | SPARE PARTS: At least 2 weeks before Practical Completion submit to the CA a schedule of spare parts that the Contractor recommends should be obtained and kept in stock by the Employer for maintenance of the services installations. State against each item the manufacturers current price, including packaging and delivery to site. |  |

| A38 | Execution of Work and Damages in the event of delay: |  |
| --- | --- | --- |
| 100 | On receiving possession of the site, the Contractor is to carry out the work with due diligence and expedition. The whole of the work is to be completed in all aspects and ready for occupation on the date agreed in the Form of Contract. Extensions of time may be agreed in writing if it can be proved that delays in the delivery of materials or shortage of local labour have been experienced. |  |
| A39 | Contingencies: |  |
|  | The amount indicated on the Form of Tender and or Tender Analysis is to be allowed in the Contractor’s tender sum for any contingencies or unseen work, which may arise during the course of the work as may be directed in writing. This sum will be deducted in whole or part at completion if not used. |  |

| Total For Preliminary Works = |  |
| --- | --- |

SCHEDULE OF WORKS

FOR

EXTERNAL DECORATION

OF RIVERBANK HOUSE, BIDEFORD

| LOCATION: | Riverbank House, Bideford – External Decoration and Works. |
| --- | --- |
| FACE NO: | DESCRIPTION OF WORKS | UNITS QUANTITY | £ P |
| General | To undertake redecoration of rendered walls and other surfaces, carry out minor repairs. |  |  |
| Note 1 | The majority of the work is to the first floor level between a height of 3 m and 8 m. |  |  |
| Note 2 | Access to the work surfaces shall be achieved using standard alloy tower scaffold equipment or similar access equipment. |  |  |
| Note 3 | Towers to be properly equipped with toe boards, guardrails fixed or trap door platforms, ladders and stability outriggers, to provide a safe working environment for the duration of the works. Security to be maintained at all times. |  |  |
| Note 4 | Due to the paved areas and tarmac hard standings surrounding the work areas, braked castors may be fitted to enable moving of the tower along the wall as work proceeds. |  |  |
| 100 | PREPARATION WORK |  |  |
| 101 | All rendered surfaces comprising first floor walls, parapet details above stone work, soffits, sides and risers to rear fire exit stairway on North end of building are to be cleaned down with water using low pressure washing (see notes below) Washing down to include walls of external store on southern elevation (Room G35) along with uPVC guttering. Make good to cracks with suitable external filler. Approx 720 sqm | Item |  |
| 102 | Landing and treads to north external stairway to be cleaned down using pressure washer, but shall be operated from a safe working distance to reduce the effect of the force of water. Working distance to be determined on site with the Supervising Office and will be strictly adhered to. Approx 30 sqm | Item |  |
| 104 | Remove remains of ivy growth to soffits of building, but not to front (west) elevation stonework (adjacent TDC logo) | item |  |
| 105 | When all rendered surfaces are dry, apply Dulux Weathershield Fungicidal Solution to walls including soffits, in strict accordance with manufacturers instructions. Allow 48 hour treatment time, and wash off with brushes to remove residual solution. Approx 675 sqm Note 1. Ensure provision and correct use of all P.P.E. Note 2. Extreme care is to be taken when operating in the vicinity of radio and microwave equipment, aerials, cables etc. Note 3. Ensure all windows and doors are closed in the vicinity of any wash down operations and consideration for passers by (staff or public) from any mist of drips generated. Note 4. Provide suitable cover for external lights, plaques, and signage. Note 5. Provide warning signs and divert staff and members of the public away from spraying and working area(s). | Item |  |
| 200 | RENDER BEADING |  |  |
| 201 | Allow to expose lightly rusting mild steel render beads around windows, (head sill, and reveals) and plinth course at first floor level where localised rust and water staining is observed. Employ hand or power tools to remove loose render and abrade metal surface to a bright finish dust off, and apply cold galvanised paint (i.e. Galvfroid) Allow to dry and make good to render edges with premixed Snowcem “Alpine” where required. | Item |  |
| 202 | On South elevation, remove the two existing grilles of air conditioning system, clean down and set aside for reuse. Replace old wood frame with new galvanised steel frame to match existing dimensions and fix in place. Reerect grilles.. | Item |  |
| 300 | DECORATION |  |  |
| 301 | To all rendered surfaces, comprising walls, parapet, (not soffits), sides and risers to rear stairway apply one full coat of Dulux Weathershield “All Seasons” Masonry Paint in Brilliant White. | Item |  |
| 302 | To undersides of Committee Room, apply one coat of Dulux Weathershield Smooth Masonry Paint Colour: Tideway (BS 18B21) | Item |  |
| 303 | Rub down, prepare and paint external door to top of first floor stairs One coat Dulux Trade High Gloss Colour Tideway (BS 18B21) | Item |  |
| 304 | Carefully wash down “Donkey Stone” on North East corner of building (adjacent external stairs) and Apply two coats Weathershield White Masonry Paint for the body with highlighting of edges and details in Dulux Tideway. | Item |  |
| 305 | Rub down and prepare doors, frame and two windows on G35. Apply one full coat Dulux Trade Undercoat and two coats Dulux Trade High Gloss paint in Brilliant White. Allow sufficient drying time between coats. | Item |  |
| 306 | Prepare and paint external walls of building G35 one coat Dulux Masonry Paint Colour: Orchard (BS 12C39) Approx 22 sqm | Item |  |
| 307 | Rub down, prepare and paint G35 Fascia and soffits one coat Dulux Trade Gloss colour: Conker. | Item |  |
| 308 | Using hand or power tools abrade steel lintel over first floor fire door (north elevation) and two first floor windows on east elevation, to remove flaking paint and surface rusting back to a sound base. Paint with Dulux Quick drying metal primer Zinc Phosphate, followed by one full coat Dulux Trade undercoat and two coats Dulux Trade High Gloss in Tideway. | Item |  |
| 400 | ELECTRICAL WORKS |  |  |
| 401 | Supply and install two No. Eterna SL226WPC floodlights complete wired from existing distribution board in FP200 cabling (or equivalent). The lights are to be positioned one on the East elevation the other on the North angled downwards facing the ground, to provide security lighting around the fire exit stair well for staff or members of the public who are entering or leaving the building during darkness hours. | Item. |  |
|  | Specification Total = |  |  |

|  | Total Carried Forward From Preliminaries = |  |
| --- | --- | --- |
|  | Specification Total = |  |
|  | Contingency @ 5%of Contract Sum = |  |
|  | Total Carried Forward To Form of Tender = |  |