King St Footbridge Refurbishment - Surfacing

Volume 2 – Specification

Scheme Ref: 1079541

Produced for

Oldham Council

Prepared by

Jawad Hashmat

The Unity Partnership

Henshaw House

Cheapside

Oldham

OL1 1NY

Web Site: www.unitypartnership.com

# Document Control Sheet

Project Title	King St Footbridge Refurbishment - Surfacing

Scheme Ref		1079541

Document Title		Specification

Revision		0.0

Status		Tender Issue

Control Date		28th April 2020

Record of Issue

| Issue | Status | Author | Date | Check | Date | Authorised | Date |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0.0 | Issue | S Hussain | 28/04/20 | A Shaw | 28/04/20 | N Molden | 28/04/20 |

Distribution

| Organisation | Contact | Copies |
| --- | --- | --- |
| Tenderers | Various | 1 |

King St Footbridge Refurbishment - Surfacing

## INDEX OF DOCUMENTS FORMING THE CONTRACT

| Tender Document (Contract) | See Volume 1 |
| --- | --- |
| Activity Schedule | See Volume 3 |
| Pre-construction Information | See Volume 4 |
| Designer’s Hazard Checklist and Hazard Elimination Management | See Volume 5 |
| TENDER DOCUMENT (Specification) - | Volume 2 |
|  | Page |
| Employer’s Requirements | 3 |
| Specification | 4 |
| Appendices 0/1 - Contract Specific Additional, Substitute and Cancelled Clauses, Tables and Figures Included in the Contract 0/2 - Contract-Specific Minor Alterations to Existing Clauses, Tables and Figures Included in the Contract 0/3 - List of Numbered Appendices Referred to in the Specification and Included in the Contract 0/4 - List of Drawings Included in the Contract 1/1 - Temporary Accommodation for the Contract Supervisor 1/5 - Testing to be Carried Out by the Contractor 1/7 - Site Extent and Limitations on Use 1/9 - Control of Noise and Vibration 1/13 - Programme of Works 1/14 - Payment Applications 1/16 - Privately and Publicly Owned Services or Supplies 1/17 – Traffic Safety & Management 1/19 – Routing of Vehicles 1/21 - Information Boards 1/23 - Risks to Health and Safety 1/70 – Inspection of Specific Works 2/1 – Site Clearance 2/3- Retention of Material Arising from Site Clearance 7/1 - Permitted Pavement Options 12/1 - Traffic Signs : General 12/3 - Traffic Signs : Road Markings And Studs 20/1- Form PWS Proprietary Waterproofing System Data Sheet & Annexe ‘A’ 23/1- Bridge Deck Expansion Joint Schedule | 10 16 17 24 26 27 37 39 42 44 45 48 50 51 52 53 54 55 57 58 59 62 63 |

Employer’s Requirements

Preamble

- The design and construction works and all temporary works shall comply with the Employer’s Requirements including:

The Specification

The Drawings (Listed in Appendix 0/4 to the Specification)

- The Specification referred to in these Employer’s Requirements shall be the “Specification for Highway Works”, published by The Stationery Office (formerly HMSO) as Volume 1 of the Manual of Contract Documents for Highway Works, as modified and extended as described in the Preamble to the Specification.

Introduction

- King St Footbridge is prominent pedestrian and cycle footbridge over the A62 Oldham Way, connecting residents from Werneth, Medlock Vale, Alexandra and surrounding areas with Oldham Town Centre. King Street Footbridge is a through truss steel bridge that was completed in 2000.  The length of the footbridge is approximate 33m in length.  A special bridge inspection carried out in 2017 identified defects to the existing surfacing and bridge joints. The brickwork block where found to be heavily weathered with washed out joints, 5% - 20% of the blockwork has lifted and is loose forming a tripping hazard, the movement joints rubber joint sealants are split across the length of the joints. To correct the defects identified to the existing surfacing and movement joints, the footway approach and footbridge deck are to be resurfaced (including waterproofing to the steel bridge deck) and the movement joints renewed.

Design and Works Requirements

- The employer’s requirements are described in detail in the Specification and the drawings listed in Appendix 0/4 to the Specification. The Contractor shall prepare and complete the specification appendices depending on his tender or detailed design in accordance with the used Appendices listed in Appendix 0/3.

- The outline design has been prepared based on the information contained in the drawings listed in Appendix 0/4. The Supervisor will consider any alternative design providing that the design criteria can be fulfilled and that the investigation of any alternative design does not result in an increase in resources, both in time checking and project costs. In addition, any alternative design check should not delay the proposed start date of the works.

Programme Requirements

- The Contractors’ method statement and outline programme is to be included with the Tender submission to demonstrate their understanding of the Works requirement.

Payment Requirements

- Payment is made via BACS credit transfer and is made in accordance with Appendix 1/14 of the Specification.

Health and Safety

- The successful Tenderer will be appointed as Principal Contractor.  A named person from this organisation will be appointed as CDM Co-ordinator who will be responsible for co-ordinating and monitoring health and safety standards during the construction stage.

Specification

Preamble

1	The Specification referred to in the Tender shall be the “Specification for Highway Works”, published by The Stationery Office (formerly HMSO) as Volume 1 of the Manual of Contract Documents for Highway Works, as modified and extended by the following:

(i)	Appendix 0/1: Contract-specific Additional, Substitute and Cancelled Clauses, Tables and Figures;

(ii)	Appendix 0/2: Contract-specific minor alterations to existing Clauses, Tables and Figures;

(iii)	The Numbered Appendices listed in Appendix 0/3;

(iv)	Appendix 0/4 contains a list of the Drawings.

2	The relevant publication date of each page of the Specification for Highway Works is given in the Schedule of Pages and Relevant Publication Dates.

3	An Additional Clause as indicated by a suffix ‘A’ and it is an alteration originating from the Overseeing Organisation of Scotland, Wales or Northern Ireland.  An Additional Clause as indicated by a suffix ‘AR’ in Appendix 0/1 is a Contract-specific alteration.

4	A Substitute Clause as indicated by a suffix ‘S’ is an alteration originating from the Overseeing Organisation of Scotland, Wales or Northern Ireland. A Substitute Clause as indicated by a suffix ‘SR’ in Appendix 0/1 is a Contract-specific alteration.

5	A Cancelled Clause as indicated by a suffix ‘C’ is an alteration originating from the Overseeing Organisation of Scotland, Wales or Northern Ireland.  A Cancelled Clause as indicated by a suffix ‘CR’ in Appendix 0/1 is a Contract-specific alteration.

6	Insofar as any of the Numbered Appendices may conflict or be inconsistent with any provision of the Specification for Highway Works the Numbered Appendices shall always prevail.  Additionally, Numbered Appendices 0/1 and 0/2 shall take precedence over any other Appendix.

7	Any reference in the Contract to a Clause number or Appendix shall be deemed to refer to the corresponding Substitute Clause number or Appendix listed in Appendix 0/1, 0/2.

8	Where a Clause is altered any original Table/Figure referred to in the Clause shall apply unless the Table/Figure is also altered. Where a Table/Figure is altered any reference in a Clause to the original Table/Figure shall apply to the altered Table/Figure.

9	Where a Clause in the Specification relates to work goods or materials which are not required for the Works it shall be deemed not to apply.

10	Any Appendix referred to in the Specification, which is not used, shall be deemed not to apply.

11	Where a Clause in the Specification is prefixed by an # this indicates that this particular Clause has a substitute National Alteration for one or more of the Overseeing Organisations of Scotland, Wales or Northern Ireland.  Substitute or additional National Clauses shall be used within countries to which they specifically apply and they are deemed to replace corresponding Clauses in the main text of the Specification as appropriate.  The substitute National Clauses are located at the end of the relevant Series together with the additional National Clauses of the Overseeing Organisations.

12	Other than where references to the Overseeing Organisation are made in the context of the Overseeing Organisation granting statutory or type approvals, the roles and functions of the Overseeing Organisation shall be undertaken by the Supervisor.

Where the Specification requires the provision of documentation to the Overseeing Organisation for statutory or type approval such documentation shall be provided to the Supervisor.

13	If the Specification is used in conjunction with a Contract under which the Contractor is responsible for the design of any part of the Permanent Works, the delegation of the roles and functions of the Overseeing Organisation as stated in paragraph 12 above shall be amended as follows:

(i)	If any agreement, consent or approval required to be obtained from the Overseeing Organisation impacts on the health and safety of the general public, the environment or any property or equipment not owned or operated by the Contractor or the Design Build Finance and operate concessionaire, such agreement, consent, approval shall be obtained from the Supervisor on behalf of the Employer.

(ii)	Where the Specification provides for the Overseeing Organisation to require a test, waive the requirement for a test or alter testing frequency, the party to whom the Overseeing Organisation’s roles and functions have been ascribed by paragraph 12 above shall exercise such decisions in accordance with the Employers requirements stated in the Contract.

# Specification for Highway Works

# Schedule of Pages and Relevant Publication Dates (05/06)

| Series/Appendix | Page Number | Publication Date |
| --- | --- | --- |
| 000 | 1 to 3, 7 to 8F | May 2014 |
| 000 | 4 to 6 | August 2014 |
| 100 | 1 to 29F, W1F, N1 to N11F | May 2014 |
| 200 | 1, 3F | May 2001 |
| 200 | 2 | May 2004 |
| 300 | 1 | May 2001 |
| 300 | 4 | November 2002 |
| 300 | 2 to 3, 5 to 6F | May 2008 |
| 400 | 1 to 6, 8, 10 to 13F | November 2007 |
| 400 | 7, 9 | November 2008 |
| 500 | 23 to 24, 26 | November 2004 |
| 500 | 28F | May 2005 |
| 500 | 3, 22, N1F | May 2006 |
| 500 | 2, 5, 27 | November 2006 |
| 500 | 6, 25 | November 2007 |
| 500 | 1, 4, 7, to 21 | November 2009 |
| 600 | 33 | November 2003 |
| 600 | 2, 27 to 28, 30 to 32, 34 to 36, N1 | November 2005 |
| 600 | 25 to 26 | November 2006 |
| 600 | 42 to 49, 51 to 68F | November 2007 |
| 600 | 37, 50 | November 2008 |
| 600 | 1, 3 to 24, 29, 38 to 41, S1 to S3F, N2 to N4F | November 2009 |
| 700 | 2 to 3, 5 to 6, N1, N3 to N5F | November 2006 |
| 700 | 33 to 34F | November 2007 |
| 700 | 4, N2 | August 2008 |
| 700 | 1, 7 to 32F | November 2009 |
| 800 | 1 to 25F | November 2009 |
| 900 | 2 to 5, 9 to 22, 24 to 26, 28 to 67F | August 2008 |
| 900 | 1, 6 to 8, S1F | November 2008 |
| 900 | 23, 27 | May 2009 |
| 1000 | 3, 5 to 6 | November 2005 |
| 1000 | 1 to 2, 4, 7 to 15, 19 to 33F | May 2006 |
| 1000 | 16 to 18 | November 2006 |
| 1100 | 1, 4F | November 2004 |
| 1100 | 2, N1F | November 2006 |
| 1100 | 3 | August 2008 |
| 1200 | 1, 14 to 16F | May 2004 |
| 1200 | 2 to 3, W1F | August 2003 |
| 1200 | 1, 14 to 16F | May 2004 |
| 1200 | 4, 9 to 11, 13 | May 2005 |
| 1200 | 5 | May 2001 |
| 1200 | 12 | November 2006 |
| 1200 | 6 to 7, N1 to N4F | November 2007 |
| 1200 | 8 | May 2008 |
| 1300 | N2F | November 2003 |
| 1300 | 3 to 4 | November 2004 |
| 1300 | 1, 5 to 10, 12F | November 2005 |
| 1300 | 2, 11 and N1 | May 2006 |
| 1400 | 2, N1F | May 2001 |
| 1400 | 1, 3 to 9F | May 2006 |
| 1500 | 7 | May 2001 |
| 1500 | 2 | February 2003 |
| 1500 | 3 to 4, 8 to 11, 13 | November 2004 |
| 1500 | 1, 5 to 6, 12 14 to 17F | November 2006 |

| Series/Appendix | Page Number | Publication Date |
| --- | --- | --- |
| 1600 | 1, 4 to 5, 9, 15, 17 to 18, 22, 24 to 26, 29 to 31, 35, 38, 49F | March 1998 |
| 1600 | 2, 6 to 8, 10 to 14, 16, 19, 27 to 28, 32 to 34, 36 to 37, 39 to 42, 44 to 48 | November 2003 |
| 1600 | 3, 20 to 23, 43 | November 2005 |
| 1700 | 2 to 7, 10 to 15 | May 2004 |
| 1700 | 8 to 9 | May 2005 |
| 1700 | 1, 16 to 22F | May 2006 |
| 1800 | 1 to 35F | August 2014 |
| 1900 | 1 to 35F, S1 to S2F | August 2014 |
| 2000 | 1, 3 to 4F | May 2001 |
| 2000 | 2 | November 2004 |
| 2100 | 1, 4F | March 1998 |
| 2100 | 2 | November 2003 |
| 2100 | 3 | November 2005 |
| 2300 | 1 | March 1998 |
| 2300 | 2 to 3F | May 2001 |
| 2400 | 1, 4, 7F | May 2005 |
| 2400 | 2 | May 2006 |
| 2400 | 3, 5 to 6 | May 2008 |
| 2500 | 1 | May 2001 |
| 2500 | 2, 8, 11F | November 2003 |
| 2500 | 6 to 7, 9 | May 2005 |
| 2500 | 10 | November 2004 |
| 2500 | 5 | May 2006 |
| 2500 | 3 to 4 | November 2006 |
| 2600 | 1 | March 1998 |
| 2600 | 2 to 4 | November 2003 |
| 2600 | 5 | November 2004 |
| 2600 | 6 | May 2005 |
| 2600 | 7F | November 2006 |
| 3000 | 1, 4 to 7, 10, 12 to 17, 19, 22 to 27F | May 2001 |
| 3000 | 20 | November 2004 |
| 3000 | 2 to 3 | May 2006 |
| 3000 | 8 to 9, 11, 18, 21 | May 2008 |
| 5000 | 1, 4 to 19F, S1F | May 2005 |
| 5000 | 2 to 3 | November 2008 |
| Appendix A | 1 to 4F | May 2014 |
| Appendix B | 1 to 3F | May 2014 |
| Appendix B | 1 to 2F | May 2014 |
| Appendix C | 1 to 2F | May 2014 |
| #Appendix D | 1F | May 2014 |
| Appendix D (NI) | 1F | May 2014 |
| #Appendix E | 1F | May 2014 |
| Appendix F | 1 to 51F | August 2014 |
| Appendix G | Not used |  |
| Appendix H | 1 | May 2004 |
| Appendix H | 2 | November 2005 |
| Appendix H | 3 | November 2006 |
| Appendix H | 4 to 9F | November 2008 |

# Appendices 000 Series

## Introduction

| Appendix | Title | Page |
| --- | --- | --- |
| 0/1 | Contract-Specific Additional, Substitute And Cancelled Clauses, Tables And Figures Included In The Contract | 10 |
| 0/2 | Contract-Specific Minor Alterations To Existing Clauses, Tables And Figures Included In The Contract | 16 |
| 0/3 | List of Numbered Appendices Referred To In The Specification And Included In The Contract | 17 |
| 0/4 | List of Drawings Included In The Contract | 24 |
| 0/5 | Not used | — |

# APPENDIX 0/1

# Contract Specific Additional, Substitute and Cancelled Clauses, Tables and Figures Included in the Contract

List of Additional Clauses, Tables and Figures

| Clause | Title |
| --- | --- |
|  | Series 100—Preliminaries |
| 150 AR | Access for Council's Safety Officer |
| 151 AR | Notification of Operations |
| 152 AR | Structures, Services, Drains and Road Surfaces |
| 153 AR | Access to site by other bodies |
| 154 AR 156 AR 157 AR 158 AR 159 AR 161 AR 163 AR 170 AR | Abatement of Nuisance Care of Public Highway Siting of Workshops and Depots Advertising, name boards & public information Non-Highway Work Affecting Highways Proprietary Materials Sampling and Testing Security of the Site |

List of Cancelled Clauses, Tables and Figures

| Clause | Title |
| --- | --- |

None

List of Substitute Clauses, Tables and Figures

| Clause | Title |
| --- | --- |
|  | Series 100—Preliminaries |
| 150 SR | Privately and Publicly Owned Services or Supplies |

Additional Clauses, Tables and Figures

Series 100—Preliminaries

150 AR Access for Council's Safety Officer

- The Contractor shall permit Oldham Metropolitan Borough Safety Officer, or other duly authorised representatives of Oldham M.B.C. to enter upon the construction site and/or site of operation of the work at any time during working hours and have free and unfettered access to each and every part of the area covered by the Contract work or affected thereby.

- The Contractor shall at all times observe and supply the provision of his Safety Policy and Safe Working System during the execution of the Works including where there is a Sub-Contractor ensuring compliance by such Sub-contractor.

- During his inspection Oldham Council.'s Safety Officer, or his authorised representative, may inform the Contractor, initially orally and subsequently in writing of any method of operation or other matter which in his opinion falls below the requirements of the Safe Working System and/or Statutory Requirements and that the matter will be reported to the Health and Safety Inspectorate should appropriate remedial action not be taken.

151 AR Notification of Operations

- The Contractor shall give the Engineer daily notification of work to be carried out on the following day and in any case not less than 24 hours' notice of his intentions, to enable the Engineer to make his arrangements for checking the setting out, taking measurements for valuation purposes and for the supervision of important operations in the Works. He shall also give the Engineer not less than 2 days' notice of the preparation or manufacture at a place not on the Site of any article or material, to be used in the Works, whether by himself or by Nominated Sub-Contractors stating the time and place of preparation or manufacture, so that the Engineer may arrange to make whatsoever inspection or tests he may require.

152 AR Protection of Existing Structures, Services, Drains And Road Surfaces

- The Contractor will be held responsible for any damage he may cause to any part of the existing highway infrastructure including pipes, services, drains, manholes, lighting and communications cables, structures, traffic signs and other highway furniture, landscaped areas, etc and all costs or repairs and/or renewal thereof shall be the responsibility of the Contractor.

- The Contractor's attention is drawn to the fact that diesel and other oils have a deleterious affect upon the road surface and the Contractor is to ensure that all vehicles are maintained in such a condition that the spillage of oil does not occur. Should the surface of the carriageway be damaged as a consequence of the Contractor failing to prevent the spillage of oil then the roadway will be repaired by the Local Authority and all costs appertaining to such repair shall be the responsibility of the Contractor.

- Particular care shall be taken to ensure that no mud or stones whatsoever are deposited on the carriageway or footpath and provision shall be made for the removal of any mud and stones inadvertently deposited, to the satisfaction of the Engineer. Provision shall be made for cleaning the wheels of all vehicles and this shall include the provision of sleeper or other type of track if required, at no additional charge. Works vehicles shall be loaded so that no loose material falls onto any highway. The Contractor will be held responsible for the consequence of any failure to observe these requirements.

- Any damage caused to the carriageway as a result of the establishment or removal of traffic safety and control measures is to be made good to the satisfaction of the Engineer.

- Prior to the introduction or reintroduction of traffic onto any carriageway, hardshoulder or hardstanding for traffic control or other purpose, the Contractor shall ensure the surface is swept clean.

- The Contractor will ensure that the above Clauses are strictly complied with at all times by his workmen or his Sub-Contractors and the Engineer may suspend the Works or part of the Works where such provisions are not being complied with, entirely at the Contractor's expense.

- Irrespective of the method of construction adopted, the Contractor shall be responsible for and ensure that the stability of existing structures affected by the execution of the Works remains unimpaired during the contract period.

153 AR Access to Site by Other Bodies

- All highway works within the Contract are to be adopted by the highway authority. Drainage works will be adopted by the Highway Authority or Water Authority as appropriate.

- The Contractor shall permit any authorised representative of the Highway Authority (Oldham MBC) to enter upon the construction site and/or site of operation of the work at any time during working hours and have free and unfettered access to each and every part of the area covered by the Contract work or affected thereby.

154 AR Abatement of Nuisance

Notwithstanding his obligations under the Conditions of Contract, the Contractor shall carry out the Works so as to cause the minimum of nuisance and inconvenience to the general public and to the owners and occupiers of property. In particular the Contractor shall comply with the following requirements:-

- Roads to be kept clean/Protection of Street Furniture. All roads which are being used by the Contractor's, Sub-Contractor's and supplier's vehicles and plant shall be kept clean and free from debris, dirt or mud arising from or due to the construction of the Works, and the Contractor shall take all necessary precautions to prevent grit, diesel oil and other contaminants being spilt onto verges and embankments. Should there be an occurrence of such spillage the Contractor shall take all necessary measures to make good the contaminated area immediately.

The Engineer shall have the right to stop the Works if, after consultation with the Police, it is considered that mud or other materials deposited by the Contractor's, sub-contractors' or suppliers' vehicles onto the carriageway is crating a hazard to passing traffic.

The Contractor shall take due care to avoid damage to traffic signs, lighting columns street furniture, carriageway surfacing, footways and verges on all parts of the structure not affected by the Works and shall not allow vehicles to run or stand on the footways and verges. Any damage caused by the Contractor shall be reinstated at his own expense to the satisfaction of the Engineer.

No unnecessary parking of vehicles will be permitted within restricted areas of trafficked highways.

To meet his obligations the Contractor shall provide, maintain and use as necessary suitable equipment including mechanical sweepers throughout the course of the Works.

- Dust Prevention. Precautions shall be taken to prevent dust nuisance arising from the Works and shall include watering, surface dressing haul roads or any other necessary measures, which may be required from time to time.

- Control of Weeds. All necessary steps shall be taken to curtail the growth on site of injurious weeds as prescribed under the Weeds Act 1959 and any other weeds which may be injurious or constitute a nuisance to land adjacent to the site.

- Burning of Waste. No waste materials shall be disposed of by burning within 200 metres of existing occupied buildings or at points outside the limits of the Works without approval of the Engineer.

- Siting of Workshops and Depots. The Contractor shall not site any workshops, mixing plants or depots for the storage of plant or materials:-

  - within 100 metres of any habitable property without the prior permission of the Engineer.

  - on, under or within 10 metres in plan of any part of any bridge or similar structure, without the prior permission of the Engineer.

  - within 2 metres of a traffic lane.

156 AR Care of Public Highways

- Subject and without prejudice to the Conditions of Contract the Contractor shall :-

  - Take all reasonable measures necessary to avoid damage to the public highway.

  - Be responsible for all repairs necessary as a consequence of his failure to comply with sub-clause (i) of this Clause and shall submit to the Engineer for approval his proposed method of repair.

- Sections of carriageway or hardshoulder closed during the course of the works shall be vigorously cleaned of all deposits, which have built up since the closure before they are re-opened to traffic.

- The Contractor shall take measures to ensure that no equipment or materials can fall onto trafficked lanes or areas used by pedestrians. Members of the public shall be protected at all times from the effects of abrasive blasting or any other operation necessary to the carrying out of the Works could result in injury to persons or damage to property.

- Protective sheeting shall be provided to adequately shield traffic and pedestrians from the effects of grit blasting. It shall be firmly secured along top and bottom edges and it is to be stiffened to prevent it being affected by the wind or passing traffic. Special attention shall be given to sealing gaps to ensure that no dust is allowed to escape. If plywood sheets are used for this purpose, they are to be securely fixed to prevent them being accidentally knocked out of position.

157 AR Siting of Workshops and Depots

- The Contractor shall obtain the written approval of the Engineer to the siting of any workshops, mixing plants, depots for the storage of plant or materials within the Work area. (Work Area is defined in Appendix 1/7). Approval will not be unreasonably refused provided that the proposed location:-

  - does not interfere with or limit existing sight lines

  - is over 3 meters from the nearest traffic lanes

  - does not pose a hazard to any existing structure

  - if within 4.5 metres of the nearest traffic lane, is protected by a safety fence which shall be erected in accordance with the 400 series of the Specification.

  - is not within the clearance zone of a safety fence, as defined in Departmental Standard TD 19/06.

  - does not have an unacceptably adverse impact on private or public interests in the opinion of the Unity Partnership.

The giving of such approval by the Engineer shall not relieve the Contractor of any obligation or responsibility under the Contract or outside the Contract.

158 AR Advertising, Name Boards and Public Information

- The Contractor shall obtain the written approval of the Engineer to the erection of any advertisement or name board on or about the Work area. Approval will not be unreasonably refused having regard to planning, traffic management and such other considerations as the Engineer may consider relevant.

Every such advertisement or name board shall prominently include the Contractors Site Agents' telephone number which shall be manned full-time whenever work is in progress and serviced by an answering machine at all other times.

159 AR Non-Highway Work Affecting Highways

- The Contractor shall not do any demolition or other non-highway work which encroaches on any part of any highway, whether adopted or unadopted, without first obtaining any necessary licenses or consents under the Highways Act 1980, the Road Traffic Regulation Act 1984 or any other requirements of the Highway Authority. Such licenses or consents may require four working weeks notice.

The Contractor shall consult the Group Engineer Traffic Management, Unity Partnership, Henshaw House, Cheapside, Oldham when contemplating any such work.

161 AR Proprietary Materials

- Where proprietary articles or materials are referred to in the Contract and are described by brand name or type followed by "or equivalent", the words "or equivalent" are to mean that the Engineer will decide whether any alternative proposal is suitable.

163 AR Sampling And Testing

- In this Clause "testing" includes in-situ measurement for checking compliance with dimensional design and tolerances.

Unless otherwise required by the Contract the Contractor shall be responsible for sampling and testing of all materials and workmanship and for proving compliance with every requirement of the Contract and shall include for all costs in his rates and prices.

Sampling and testing shall be at not less than the frequencies specified in the Contract and for every property or requirement of the Contract. Where no frequency is specified in the Contract it shall be at such reasonable frequency as the Engineer shall direct.

The Engineer may take additional samples or do additional testing and the Contractor shall be deemed to have given his consent for such sampling or testing and shall give the Engineer such assistance as he may require.

The Contractor shall give the Engineer adequate notice of his intention to sample or test materials or workmanship and the Engineer will give like notice to the Contractor. The Engineer may attend, and shall have power to supervise, any sampling or testing by the Contractor. All sampling and testing shall be to the approval of the Engineer. The Engineer will consider favourably any request by the Contractor to do sampling jointly.

All sampling of materials shall be done by competent experienced operatives from materials on site at the point of use. Samples shall be sent for testing within one week of sampling.

Testing of materials shall be done by a NAMAS - accredited laboratory which shall do the tests and deliver copies of all test results and reports to the Engineer promptly.

The laboratory shall be approved by the Engineer before use. Such approval may be withdrawn if the Engineer considers the service provided is not sufficiently prompt.

170 AR Security of the Site

- The Contractor shall take all reasonable measures to prevent trespass or unauthorised access to the works and theft from or malicious damage to the works.  The Contractor shall report details of any breach of security measures to the Overseeing Organisation.

The report shall initially be oral immediately on becoming aware of an incident.  Written confirmation of all such oral reports giving date, time and action taken shall be provided to the Overseeing Organisation within 24 hours after the initial oral report of any incident.  The Contractor shall maintain a log of all breaches of security which shall be available to the Overseeing Organisation on request.

1131 AR : FOOTWAYS AND PAVED AREAS : GENERAL

- Footways and paved areas shall be laid to smooth gradients and crossfalls, to jointing patterns approved by the Project Manager before work commences and shall be free of any trips, ponding or steps at joints.

- The finished levels of bituminous binder courses and surface courses shall not deviate from the proper levels by more than +6mm/-6mm. The tolerances at kerbs or drainage channels shall be +3mm/-0mm. The combination of tolerances shall not reduce the total thickness of the surfacing by more than 5mm, nor the thickness of surface course by more than 3mm.

- The finished levels of flagged or block-paved areas shall not deviate from the proper levels by more than +3mm/-3mm. The tolerances at kerbs or drainage channels shall be +2mm/-0mm.

- Sub-base materials shall be laid and compacted to S.H.W Clause 802.

The finished level of sub-base shall not deviate from the design level by more than +10mm/-30mm.

Appendix 0/2

Contract-Specific Minor Alterations to Existing Clauses, Tables and Figures Included in the Contract

| Clause No. | Alterations to be made |
| --- | --- |
|  | Series 000—Introduction |
| 002 110 803 | Delete the second paragraph of Clause 002.1 and replace with the following: “The term Overseeing Organisation means Oldham Metropolitan Borough Council, unless references to the Overseeing Organisation are made in the context of granting statutory or type approvals. In which case the term Overseeing Organisation means the Highways Agency, Scottish Office Development Department, Welsh Office or the Department of Environment for Northern Ireland as appropriate.” Delete four weeks and insert “two weeks”. Delete paragraph 1, and insert Type 1 granular material shall be crushed rock, crushed slag or crushed concrete. The crushed rock shall be confined to the types listed below: 1) Granite 5) Quartzite 2) Basalt 6) Hornfels 3) Gabbro 7) Limestone 4) Pophyry Add new sub-clause:- 6. The material shall be laid and compacted to the requirements of Clause 802 at a moisture content within the range 1% above tp 2% below the optimum percentage determined in accordance with the Vibrating Hammer Method test in BS 1377: Part 4 and without drying out or segregation. |

Appendix 0/3

List of Numbered Appendices Referred to in the Specification and Included in the Contract

Appendix 0/3 comprises two lists, A and B, of Numbered Appendices as follows:

List ‘A’ is a complete list of the Numbered Appendices referred to in the national Specification for Highway Works with those not adopted marked “Not Used”.  Those identified by the letter ‘T’ shall be completed by the Tenderer and included with the Tender.  Those identified by the letter ‘C’ shall be completed by the Contractor as part of his detailed design.  Those marked “If required” are to be completed by the Tenderer or Contractor as indicated, if they are required by the Contractors design.  Those with page numbers shown have been prepared by the Employers Representative but can be added to by the Tenderer or Contractor where identified by the letters ‘T’ or ‘C’ and if they are required by the Contractors design.

List ‘B’ gives the list of Contract-specific Numbered Appendices devised for the Contract.

List ‘A’:	List of Numbered Appendices Referred to in the Specification for Highway Works

| Page No. | Completed by | Appendix No. | Title |
| --- | --- | --- | --- |
|  |  |  | INTRODUCTION |
| 10 |  | 0/1 | Contract-specific Additional, Substitute and Cancelled Clauses, Tables and Figures Included in the Contract |
| 16 |  | 0/2 | Contract-specific Minor Alterations to Existing Clauses, Tables and Figures |
| 17 |  | 0/3 | List of Numbered Appendices Referred to in the Specification and Included in the Contract |
| 24 |  | 0/4 | List of Drawings included in the Contract |
| Not used |  | 0/5 | Special National Alterations of the Overseeing Organisation of Scotland/Wales/Northern Ireland |
|  |  |  | PRELIMINARIES |
| 26 |  | 1/1 | Temporary Accommodation and Equipment for the Overseeing Organisation |
| Not used |  | 1/2 | Vehicles for the Overseeing Organisation |
| Not used |  | 1/3 | Communication System for the Overseeing Organisation |
| Not used |  | 1/4 | Working & Fabrication Drawings |
| 27 | C | 1/5 | Testing to be Carried out by the Contractor |
| Not used |  | 1/6 | Supply and Delivery of Samples to the Overseeing Organisation |
| 37 |  | 1/7 | Site Extent and Limitations on Use |
| Not used |  | 1/8 | Operatives for the Overseeing Organisation |
| 39 | C | 1/9 | Control of Noise and Vibration |
| Not used |  | 1/10 | Structures to be Designed by the Contractor |
| Not used |  | 1/11 | Structural Elements and Other Features to be Designed by the Contractor |
| Not used |  | 1/12 | Setting Out and Existing Ground Levels |
| 42 | C | 1/13 | Programme of Works |
| 44 | C | 1/14 | Payment Applications |
| Not used |  | 1/15 | Accommodation Works |

List ‘A’:	List of Numbered Appendices referred to in the Specification for Highway Works (Continued)

| Page No. | Completed by | Appendix No. | Title |
| --- | --- | --- | --- |
| 45 | C | 1/16 | Privately & Publicly Owned Services & Supplies |
| 48 | C | 1/17 | Traffic Safety & Management |
| Not used |  | 1/18 | Temporary Diversions for Traffic |
| 50 |  | 1/19 | Routing of Vehicles |
| Not used |  | 1/20 | Recovery Vehicles for Breakdowns |
| 51 | C | 1/21 | Information Boards |
| Not used |  | 1/22 | Progress Photographs |
| 52 | C | 1/23 | Risks to Health and Safety |
| Not used |  | 1/24 | Quality Management System |
| Not used |  | 1/25 | Temporary CCTV for monitoring of Traffic |
| Not used |  | 1/26 | Temporary Automatic Speed Camera System for the Enforcement of Mandatory Speed Limits at Road Works (TASCAR) |
| Not used |  | 1/27 | Temporary Automatic Speed Camera System for the Enforcement of Mandatory Speed Limits at Road Works (TASCAR) – Particular requirements |
| 53 |  | 1/70 | Inspection of Specific Works |
|  |  |  | SITE CLEARANCE |
| 54 |  | 2/1 | List of Buildings, etc., to be Demolished |
| Not used |  | 2/2 | Filling of Trenches & Pipes |
| 55 |  | 2/3 | Retention of Material Arising from Site Clearance |
| Not used |  | 2/4 | Explosives & Blasting |
| Not used |  | 2/5 | Hazardous Materials |
|  |  |  | FENCING AND ENVIRONMENTAL BARRIERS |
| Not used |  | 3/1 | Fencing, Gates and Stiles |
|  |  |  | SAFETY FENCES, SAFETY BARRIERS AND PEDESTRIAN GUARDRAILS |
| Not used |  | 4/1 | Safety Fences and Safety Barriers |
| Not used |  | 4/2 | Pedestrian Guardrails |

List ‘A’:	List of Numbered Appendices referred to in the Specification for Highway Works (Continued)

| Page No. | Completed by | Appendix No. | Title |
| --- | --- | --- | --- |
|  |  |  | DRAINAGE AND SERVICE DUCTS |
| Not used |  | 5/1 | Drainage Requirements |
| Not used |  | 5/2 | Service Duct Requirements |
| Not used |  | 5/3 | Surface Water Channels and Drainage Channel Blocks |
| Not used |  | 5/4 | Fin Drains and Narrow Filter Drains |
| Not used |  | 5/5 | Combined Drainage and Kerb Systems |
| Not used |  | 5/6 | Linear Drainage Channel Systems |
| Not used |  | 5/7 | Thermoplastics Structural Wall Pipes and Fittings |
|  |  |  | EARTHWORKS |
| Not used |  | 6/1 | Requirements for Acceptability & Testing etc., of Earthworks Materials |
| Not used |  | 6/2 | Requirements for Dealing with Class U2 Unacceptable Material |
| Not used |  | 6/3 | Requirements for Excavation, Deposition, Compaction (Other than Dynamic Compaction) |
| Not used |  | 6/4 | Requirements for Class 3 Material |
| Not used |  | 6/5 | Geotextiles Used to Separate Earthworks Materials |
| Not used |  | 6/6 | Fill to Structures & Fill Above Structural Foundations |
| Not used |  | 6/7 | Sub-formation & Capping & Preparation & Surface Treatment of Formation |
| Not used |  | 6/8 | Topsoiling, Grassing Seeding and Turfing |
| Not used |  | 6/9 | Earthwork Environmental Bunds, Landscape Areas, Strengthened Embankments |
| Not used |  | 6/10 | Ground Anchorages, Crib Walling & Gabions |
| Not used |  | 6/11 | Swallow Holes & Other Naturally Occurring Cavities & Disused Mine Workings |
| Not used |  | 6/12 | Instrumentation & Monitoring |
| Not used |  | 6/13 | Ground Improvement |
|  |  |  | ROAD PAVEMENTS—GENERAL |
| 57 |  | 7/1 | Permitted Pavement Options Sheets 1, 2 & 3 |
| Not used |  | 7/2 | Excavation & Reinstatement of Existing Surfaces |
| Not used |  | 7/3 | Surface Dressing Sheets 1&2 |
| Not used |  | 7/4 | Bituminous Sprays |
| Not used |  | 7/5 | In Situ Recycling: The Remix and Repave Processes |
| Not used |  | 7/6 | Breaking Up or Perforation of Existing Pavement |
| Not used |  | 7/7 | Slurry Surfacing Sheets 1 & 2 |
| Not used |  | 7/8 | Microsurfacing Sheets 1 & 2 |
| Not used |  | 7/9 | Cold-Milling of Bituminous Bound Flexible Pavement |
| Not used |  | 7/10 | Worksheet Pro Forma for Results of Testing for Constituent Materials in Recycled Coarse Aggregate and Recycled Concrete |
| Not used |  | 7/11 | Overbanding and Inlaid Crack Sealing Systems |
| Not used |  | 7/12 | Arrester Beds |
| Not used |  | 7/13 | Saw-Cut and Seal Bituminous Overlays on Existing Concrete Pavements |
| Not used |  | 7/14 | Preparation of Jointed Concrete Pavements prior to Overlaying and Saw-Cutting and Seal of Bituminous Overlay |
| Not used |  | 7/15 | Saw-Cut and Seat Existing Jointed Concrete Pavements |
| Not used |  | 7/16 | Cracking and Seating of Existing Jointed Unreinforced Concrete Pavements and CBM Roadbases |
| Not used |  | 7/17 | Cracking Plant and Equipment Progress Record |
| Not used |  | 7/18 | Site Specific Details and Requirements for Cold Recycled Bitumen Bound Material |
| Not used |  | 7/19 | Site Specific Details and Requirements for Recylced Cement Bound Material |
| Not used |  | 7/20 | Site Specific Details and Requirements for Inducing Cracks |
| Not used |  | 7/21 | Surface Dressing – Recipe Specification ( Sheets 1 and 2) |
| Not used |  | 7/22 | Repairs to Potholes |
|  |  |  | ROAD PAVEMENTS—CONCRETE AND CEMENT BOUND MATERIALS |
| Not used |  | 10/1 | Plant and Equipment for the Construction of Exposed Aggregate Concrete Surface |

List ‘A’:	List of Numbered Appendices referred to in the Specification for Highway Works (Continued)

| Page No. | Completed by | Appendix No. | Title |
| --- | --- | --- | --- |
|  |  |  | KERBS, FOOTWAYS AND PAVED AREAS |
| Not used |  | 11/1 | Kerbs, Footways & Paved Areas |
| Not used |  | 11/2 | Access Steps |
|  |  |  | TRAFFIC SIGNS |
| 58 |  | 12/1 | Traffic Signs: General |
| Not used |  | 12/2 | Traffic Signs: Marker Posts |
| 59 |  | 12/3 | Traffic Signs: Road Markings & Studs |
| Not used |  | 12/4 | Traffic Signs: Cones, Cylinders, FTD’s & Other Traffic Delineators |
| Not used |  | 12/5 | Traffic Signs: Traffic Signals |
| Not used |  | 12/6 | Traffic Signs: Special Sign Requirements on Gantries |
|  |  |  | ROAD LIGHTING COLUMNS AND BRACKETS |
| Not used |  | 13/1 | Information to be Provided When Specifying Lighting Columns & Brackets |
| Not used |  | 13/2 | Column & Bracket Data Sheets 1 & 2 |
| Not used |  | 13/3 | Instruction for Completion of Column & Bracket Data Sheet |
| Not used |  | 13/4 | Information to be Provided When Specifying CCTV Masts |
| Not used |  | 13/5 | (Specification for Highway Works) Typical CCTV Mast Data Sheet |
| Not used |  | 13/6 | Instruction for Completion of CCTV Mast Data Sheet |
| Not used |  | 13/7 | Information to be Provided when Specifying Cantilever Masts |
| Not used |  | 13/8 | (Specification for Highway Works) Typical Cantilever Mast Data Sheets 1 and 2 |
| Not used |  | 13/9 | Instructions for Completion of Cantilever Mast Data Sheets |
|  |  |  | ELECTRICAL WORK FOR ROAD LIGHTING AND TRAFFIC SIGNS |
| Not used |  | 14/1 | Site Records |
| Not used |  | 14/2 | Location of Lighting Units & Feeder Pillars |
| Not used |  | 14/3 | Temporary Lighting |
| Not used |  | 14/4 | Electrical Equipment for Road Lighting |
| Not used |  | 14/5 | Electrical Equipment for Traffic Signs |
|  |  |  | MOTORWAY COMMUNICATIONS |
| Not used |  | 15/1 | Motorway Communications |
| Not used |  | 15/2 | Cable Duct Requirements |
|  |  |  | PILING AND EMBEDDED RETAINING WALLS |
| Not used |  | 16/1 | General Requirements for Piling and Embedded Retaining Walls |
| Not used |  | 16/2 | Precast Reinforced and Prestressed Concrete Piles and Precast Reinforced Concrete Segmental Piles |
| Not used |  | 16/3 | Bored Cast-in-Place Piles |
| Not used |  | 16/4 | Bored Piles Constructed using Continuous Flight Augers and Concrete or Grout Injection through Hollow Auger Stems |
| Not used |  | 16/5 | Driven Cast-in-Place Piles |
| Not used |  | 16/6 | Steel Bearing Piles |
| Not used |  | 16/7 | Reduction of Friction on Piles |
| Not used |  | 16/8 | Non-destructive Methods for Testing Piles |
| Not used |  | 16/9 | Static Load Testing of Piles |
| Not used |  | 16/10 | Diaphragm Walls |
| Not used |  | 16/11 | Hard/Hard Secant Pile Walls |
| Not used |  | 16/12 | Hard/Soft Secant Pile Walls |
| Not used |  | 16/13 | Contiguous Bored Pile Walls |
| Not used |  | 16/14 | King Post Walls |
| Not used |  | 16/15 | Steel Sheet Piles |
| Not used |  | 16/16 | Integrity Testing of Wall Elements |
| Not used |  | 16/17 | Instrumentation for Piles and Embedded Walls |
| Not used |  | 16/18 | Support Fluid |
|  |  |  | STRUCTURAL CONCRETE |
| Not used |  | 17/1 | Concrete—Classification of Mixes |

List ‘A’:	List of Numbered Appendices referred to in the Specification for Highway Works (Continued)

| Page No. | Completed by | Appendix No. | Title |
| --- | --- | --- | --- |
| Not used |  | 17/2 | Concrete—Impregnation Schedule |
| Not used |  | 17/3 | Concrete—Surface Finishes |
| Not used |  | 17/4 | Concrete—General |
| Not used |  | 17/5 | Buried Concrete – Sulphate Attack |
| Not used |  | 17/6 | Grouting and Duct System for Post Tensioned Tendons |
|  |  |  | STRUCTURAL STEELWORK |
| Not used |  | 18/1 | Requirements for Structural Steelwork |
|  |  |  | PROTECTION OF STEELWORK AGAINST CORROSION |
| Not used |  | 19/1 | (Specification for Highway Works) Form HA/P1 (New works) Paint System Sheet |
| Not used |  | 19/2 | Requirements for Other Works |
| Not used |  | 19/3 | (Specification for Highway Works) Form HA/P3 Paint Data Sheet |
| Not used |  | 19/4 | (Specification for Highway Works) Form HA/P3 Paint Sample Despatch List, Sheets 1 & 2 |
| Not used |  | 19/5 | General Requirements |
|  |  |  | WATERPROOFING FOR STRUCTURES |
| 62 |  | 20/1 | Form PWS Proprietary Waterproofing System Data Sheet & Annexe ‘A’ |
| Not used |  | 20/2 | Waterproofing for Concrete Structures |
|  |  |  | BRIDGE BEARINGS |
| Not used |  | 21/1 | Bridge Bearings Schedule |
|  |  |  | PARAPETS |
| Not used |  | 22/1 | Parapet Schedule |
|  |  |  | BRIDGE EXPANSION JOINTS AND SEALING OF GAPS |
| 63 |  | 23/1 | Bridge Deck Expansion Joint Schedule |
| Not used |  | 23/2 | Sealing of Gaps Schedule |
|  |  |  | BRICKWORK, BLOCKWORK AND STONEWORK |
| Not used |  | 24/1 | Brickwork, Blockwork and Stonework |
|  |  |  | SPECIAL STRUCTURES |
| Not used |  | 25/1 | Requirements for Corrugated Steel Buried Structures |
| Not used |  | 25/2 | Requirements for Reinforced Soil and Anchored Earth Structures |
| Not used |  | 25/3 | Requirements for Pocket Type Reinforced Brickwork Retaining Wall Structures |
| Not used |  | 25/4 | Environmental Barriers |
| Not used |  | 25/5 | Requirements for Buried Rigid pipes for Drainage Structures |
|  |  |  | MISCELLANEOUS |
| Not used |  | 26/1 | Ancillary Concrete |
| Not used |  | 26/2 | Bedding Mortar |
| Not used |  | 26/3 | Cored Thermoplastic Node Markers |
|  |  |  | LANDSCAPE AND ECOLOGY |
| Not used |  | 30/1 | General sheet 1, 2 & 3 |
| Not used |  | 30/2 | Weed Control |
| Not used |  | 30/3 | Control of Rabbits and Deer |
| Not used |  | 30/4 | Ground Preparation |
| Not used |  | 30/5 | Grass Seeding, Wildflower Seeding and Turfing |
| Not used |  | 30/6 | Planting, sheets 1 & 2 |
| Not used |  | 30/7 | Grass, Bulbs and Wildflower Maintenance |
| Not used |  | 30/8 | Watering |
| Not used |  | 30/9 | Establishment Maintenance for Planting |
| Not used |  | 30/10 | Maintenance of Established Trees and Shrubs |
| Not used |  | 30/11 | Management of Waterbodies |
| Not used |  | 30/12 | Special Ecological Measures |

List ‘A’:	List of Numbered Appendices referred to in the Specification for Highway Works (Continued)

| Page No. | Completed by | Appendix No. | Title |
| --- | --- | --- | --- |
|  |  |  | MAINTENANCE PAINTING OF STEELWORK |
| Not used |  | 50/1 | (Specification for Highway Works) Form HA/P1 (Maintenance) Paint System Sheet |
| Not used |  | 50/2 | Requirements for Other Work |
| Not used |  | 50/3 | (Specification for Highway Works) Form HA/P2 Paint Data Sheet |
| Not used |  | 50/4 | (Specification for Highway Works) Form HA/P3 Paint Sample Despatch List, sheets 1 & 2 |
| Not used |  | 50/5 | General Requirements |

List ‘B’:	List of Contract-Specific Numbered Appendices Devised for the Contract

| Page No. | Appendix No. | Title |
| --- | --- | --- |
|  |  | PRELIMINARIES |
| 53 | 1/70 | Inspection of Specific Works |

Appendix 0/4

List of Drawings Included in the Contract

1	Contract-specific Drawings Supplied to Each Tenderer

| Drawing No. | Title | Volume No. |
| --- | --- | --- |
| 1079541-0100-U-101 | Location Plan | - |
| 1079541-1100-U-1101_Rev A | Proposed Footbridge Kerbs, Footways And Paved Areas Layout | - |
| 1079541-0100-U-0801 | Scheme Sign Board | - |

2 Standard Drawings

2(i) Supplied to Each Tenderer

| Drawing No. | Title | Volume No. |
| --- | --- | --- |
| HC 1207-1 | Oldham Bollard Standard | - |

2(ii) Inspected by Tenderers

During the Tender period the following drawings and documents shall be available for inspection (by prior arrangement) between 10 a.m. and 4 p.m., Monday–Friday, at Level 1, Henshaw House, Cheapside, Oldham, OL1 1NY:

| Document | Title | Aspect required if not whole Drawing |
| --- | --- | --- |
| N/A | N/A | N/A |

2(iii) Brought Into the Contract by Reference

HCD published by The Stationery Office (formerly HMSO) as Volume 3 of the Manual of Contract Documents for Highway Works contains the following drawings brought into the Contract by reference.  Unless otherwise stated below the whole drawing is brought into the Contract.

| Drawing No. | Title | Aspect/Alternative(s) required if not whole Drawing |
| --- | --- | --- |
| N/A | N/A | N/A |

3 Additional Documents

3(I) Supplied to each Tenderer.

| Document Name | Produced By | Title | Date |
| --- | --- | --- | --- |
| N/A | N/A | N/A | N/A |

Appendix 1/1

Temporary Accommodation for the Contract Supervisor.

1	No Accommodation required for the Contract Supervisor.

Appendix 1/5

1.	Tests comparable to those specified in the following table of this appendix will be necessary for any work, goods or materials supplied under this contract, this shall include any reasonable additional acceptance testing where the Project Manager directs. The contractor is responsible for arranging and bearing the cost of carrying out the tests.

2.	Testing must be carried out by a NAMAS accredited laboratory and paid directly by the contractor.

3.	The Contractor is to supply the Project Manager with a NAMAS test report or certificate for each test.

4.	Unless otherwise shown in this Appendix tests for work, goods or materials as scheduled under any one Clause are required for all such work, goods or materials in the works.

APPENDIX 1/5: TESTING TO BE CARRIED OUT BY THE CONTRACTOR (cont.)

| Clause | Work, Goods or Material | Test | Frequency of Testing | Test Certificate | Comments |
| --- | --- | --- | --- | --- | --- |
| Series 500 |  |  |  |  |
| 501 | Pipes for drainage and service ducts |  |  |  |  |
|  |  | Asbestos-cement |  |  |  | Product certification |
|  |  | Vitrified clay |  |  |  | scheme applies |
|  |  | Concrete PC/SRC | not exceeding |  |  |  |  |
|  |  | Concrete Pre-stressed | 900 mm dia |  |  |  |  |
|  |  | Iron—cast |  |  |  |  |
|  |  | Iron—ductile |  |  |  |  |
|  |  | UPVC |  |  |  |  |
|  |  | GRP |  |  |  |  |
|  |  | Plastics |  |  | Required |  |
|  |  | Corrugated steel |  |  | (AASHTO) |  |
|  |  | Corrugated steel bitumen protection | (Manufacturer’s tests) |  |  |  |
|  |  | Concrete PC/SRC exceeding 900 mm dia | Proof load Maximum load Chloride ion Cube strength (Manufacturer’s tests) | Sub-Clause 509.9 | Required (AASHTO) |  |
|  |  | Other materials |  |  |  | BBA certification applies |
| 503 | Pipe bedding | Grading | 1 per 500 tonnes (min of 3) * |  |  |
|  |  | Soluble sulphate content (N) | 1 per source * |  |  |
|  |  | 10% fines value (N) |  |  |  |
| 505 | Filter medium backfill | Plastic index (N) | 1 per source * |  |  |
|  |  | 10% fines value (N) |  |  |  |
|  |  | Soluble sulphate content |  |  |  |
|  |  | Grading | 1 per 500 tonnes |  | Washing and sieving method to be used |
|  |  | Permeability (N) | 1 per source * |  |  |
| 506 | Sealing existing drains |  |  |  |  |
|  |  | Concrete |  | Not required |  |  |
|  |  | Grout |  | Not required |  |  |

Testing to be Carried Out by the Contractor (continued)

| Clause | Work, Goods or Material | Test | Frequency of Testing | Test Certificate | Comments |
| --- | --- | --- | --- | --- | --- |
| Series 500 (continued) |  |  |  |  |
| 508 | Gullies and pipe junctions |  |  |  | Product certification scheme applies |
|  |  | Precast concrete |  |  |  |  |
|  |  | Clay |  |  |  |  |
|  |  | Cast iron and steel |  |  |  |  |
| 509 | Watertightness of cells | Air test | All pipelines with watertight joints |  |  |
| 512 | Backfill to pipe bays | Grading | 1 per 500 tonnes (min of 3) |  |  |
|  |  | Soluble sulphate content (N) | 1 per source |  |  |
| 513 | Permeable backing to earth retaining structures | Plastic index (N) | 1 per source |  |  |
|  |  | Soluble sulphate content (N) |  |  |  |
|  |  | 10% fines value (N) |  |  |  |
|  |  | Grading | 1 per 200 tonnes (min of 3) |  |  |
|  |  | Permeability (N) | 1 per source |  |  |
|  |  | Precast hollow concrete blocks | Manufacturer’s tests |  | Required |  |
| 515 | Narrow filter drains—granular fill | Plastic index (N) | 1 per source |  |  |
|  |  | 10% fines value (N) |  |  |  |
|  |  | Soluble sulphate content (N) |  |  |  |
|  |  | Grading | 1 per 200 tonnes (min of 3) |  |  |
|  |  | Permeability (N) | 1 per source |  |  |
| 517 | Linear drainage systems | Load test | A minimum of 1 and not less than 1 test per 1000 m for each type and source | Required | Certification that the systems comply with Clause 517 is required |

Testing to be Carried Out by the Contractor (continued)

| Clause | Work, Goods or Material | Test | Frequency of Testing | Test Certificate | Comments |
| --- | --- | --- | --- | --- | --- |
| Series 600 |  |  |  |  |
| 601 631 to | Acceptable material |  |  |  |  |
| 637 640 | Class | General Description |  |  |  |  |
|  | 1 | General granular fill | Grading/uniformity coefficient | Twice a week |  |  |
|  |  |  | mc/MCV (N) | 2 per 1000 m³ up to max. of 5 per day |  |  |
|  |  |  | SMC of chalk (N) | Twice a week |  |  |
|  |  |  | 1C only | 10% of fines value (N) | Weekly |  |  |
|  | 2 | General cohesive fill | Grading | Twice a week |  |  |
|  |  |  | mc/MCV/PL Undrained shear strength (N) | 2 per 1000 m³ up to max. of 5 per day |  |  |
|  |  |  | SMC of chalk (N) | Twice a week |  |  |
|  |  |  | Bulk density (PFA) (N) | 2 per 1000 m³ up to max. of 5 per day |  |  |
|  | 3 | General chalk fill | mc (N) | 2 per 1000 m³ up to max. of 5 per day |  |  |
|  |  |  | SMC (N) | Daily |  |  |
|  | 4 | Landscape fill | Grading/mc/MCV (N) | Daily |  |  |
|  | 5 | Topsoil | Grading | Daily |  |  |
|  | 6 | Selected granular fill | Grading/uniformity coefficient | 1 per 400 tonnes |  |  |
|  |  |  | PI/LL (N) | Daily |  |  |
|  |  |  | 10% fines value/SMC (N) | Weekly |  |  |
|  |  |  | omc/mc, mc or MCV (N) | 1 per 400 tonnes |  |  |
|  |  |  | Organic matter/water soluble or total sulphate content (N) | Weekly |  |  |
|  |  |  | pH/chloride ion content (N) | Weekly |  |  |
|  |  |  | Resistivity (N) | Not Required |  |  |
|  |  |  | Undrained and drained shear parameters (N) | 1 per 400 tonnes |  |  |

Testing to be Carried Out by the Contractor (continued)

| Clause | Work, Goods or Material | Test | Frequency of Testing | Test Certificate | Comments |
| --- | --- | --- | --- | --- | --- |
| Series 600 (continued) |  |  |  |  |
|  | Class | General Description |  |  |  |  |
|  | 7 | Selected cohesive fill | Grading/mc/MCV/ bulk density (N) | 1 per 400 tonnes |  |  |
|  |  |  | SMC of chalk | Twice a week |  |  |
|  |  |  | PI/LL (N) | Daily |  |  |
|  |  |  | Organic matter/total or water soluble sulphate content (N) | Twice a week or daily where sulphates are expected |  |  |
|  |  |  | pH/chloride ion content (N) | Weekly |  |  |
|  |  |  | Resistivity (N) | Not Required |  |  |
|  |  |  | Undrained and drained shear parameters (N) | 1 per 400 tonnes |  |  |
|  |  |  | Permeability (N) | 1 per 400 tonnes |  |  |
|  | 8 | Miscellaneous fill | mc/MCV (N) | Daily |  |  |
|  | 9 | Stabilised | Pulverisation | 1 per lane width |  |  |
|  |  | materials | mc/MCV (N) | per 200m length |  |  |
|  |  |  | Bearing ratio (N) |  |  |  |
|  | Pulverised fuel ash | Chemical analysis | 1 per consignment |  |  |
|  | Furnace bottom ash | Grading | 1 per 300 tonnes |  |  |
|  | Fill adjacent to cementitious material or metallic items | Soluble sulphate content (N) | 1 per 400 tonnes or per location if less than 400 tonnes |  |  |
| 602 | Earthworks material beneath surface of a road or paved central reserve (i) Off site source (ii) On site source | Frost heave (N) | 1 every four months 1 per location |  |  |
| 609 | Geotextiles | Tensile load | 1 per 400 square |  |  |
| 621 |  | Permeability | metres |  |  |
|  |  | Pore size |  |  |  |

Testing to be Carried Out by the Contractor (continued)

| Clause | Work, Goods or Material | Test | Frequency of Testing | Test Certificate | Comments |
| --- | --- | --- | --- | --- | --- |
| Series 600 (continued) |  |  |  |  |
| 612 | Compaction of fills |  |  |  |  |
|  |  | Method compaction | Field dry density (N) | 1 per 400 tonnes |  |  |
|  |  | End product compaction | Optimum mc (2.5 kg rammer/vibrating hammer method) (N) | Each class or sub class of material |  |  |
|  |  |  | Field dry density (N) | 1 per 400 tonnes |  |  |
| 614 | Cement stabilisation to form capping | Rate of spread of cement | 1 per 500 square metres of cement spread |  |  |
| 615 641 | Lime stabilisation to form capping | Rate of spread of lime | 1 per 500 square metres of lime spread |  |  |
|  |  | Available lime content | Each source of lime weekly during stabilisation operation |  |  |
| 618 | Topsoiling and grass seeding | Rate of spread of fertiliser | 1 per 1000 square metres |  |  |
|  |  | Rate of spread of seeding |  |  |  |
|  |  | Chemical analysis of fertiliser | 1 per source |  |  |
|  |  | Grass seed germination and purity (Manufacturer’s test) | 1 per source and mix variety | Required prior to sowing |  |
| 622 638 639 | Earthworks for reinforced earth and anchored earth structures | Redox potential | 5 locations within the affected area |  |  |
|  |  | Drainage layers | Grading | 1 per 400 tonnes |  |  |
|  |  |  | Chemical analysis |  |  |  |
|  |  | Reinforcing elements | Coefficient of friction | Each type of element with each type of fill |  |  |
|  |  | Anchor elements | Adhesion |  |  |  |
| 624 | Ground anchors | Proof loading | As required in Appendix 6/10 |  |  |
| 626 | Gabions |  |  |  |  |  |
|  |  | Fill | Grading | 1 per 400 tonnes |  |  |
|  |  |  | 10% fines value (N) |  |  |  |
|  |  | Geomesh |  | 1 per 400 square metres |  |  |
|  |  | PVC coated wire |  |  | Required (ASTM G23) |  |
| 642 | Earthworks materials adjacent to structures | Constrained soil modulus (M*) | 3 on each side of structure |  |  |

Testing to be Carried Out by the Contractor (continued)

| Clause | Work, Goods or Material | Test | Frequency of Testing | Test Certificate | Comments |
| --- | --- | --- | --- | --- | --- |
| Series 700 |  |  |  |  |
| 705 | Sub-base and roadbase material beneath surface of a road or paved central reserve | Frost heave (N) | 1 every four months |  |  |
| Series 900 |  |  |  |  |
|  | All material in series. | Confirmation of plant | Weekly. |  |  |
|  |  | OCL Level A |  |  |  |
|  |  | CE Certification |  |  |  |
| Series 1100 |  |  |  |  |
| 1101 | Precast concrete kerbs, channels, edgings and quadrants | Transverse strength | Minimum of 3 per 1000 units of each product (BS 7263: Part 1) |  |  |
|  |  | Water absorption |  |  |  |
| 1102 | In situ asphalt kerbs | Grading | 1 test per 500 |  |  |
|  |  | Binder content | metres laid |  |  |
| 1104 | Precast concrete flags | Transverse strength | Minimum of 3 per |  |  |
|  |  | Water absorption | 1000 units of each product (BS 7263: Part 1) |  |  |
|  | Bedding | granular material | As for clauses 803 and 804 | As for clauses 803 and 804 |  |  |
|  |  | mortar | As for Series 2400 | As for Series 2400 |  |  |
| 1107 | Concrete block paving | Compressive strength | 16 per 5000 blocks (BS 6717: Part 1) |  |  |
| 1108 | Clay pavers | Transverse breaking load | Minimum of 10 per 10000 pavers (BS 6677: Part 3) |  |  |
|  |  | Skid resistance | Minimum of 5 per 10000 pavers (BS 6677: Part 3) |  |  |
| Series 1200 |  |  |  |  |
| 1202 | Permanent traffic signs |  |  | Required | Quality management scheme applies. Certification that the traffic sign is capable of passing tests in BS 873: Part 1 is required |
| 1212 | Road markings | Tests specified in BS EN 1824 |  | Required | National quality management sector scheme applies. Procedures are given in BS EN 1824 |
|  |  | Glass Beads | Arsenic trioxide content. Lead content and antimony content (N) | One per contract and / or per specific source of supply | Required |  |

Testing to be Carried Out by the Contractor (continued)

| Clause | Work, Goods or Material | Test | Frequency of Testing | Test Certificate | Comments |
| --- | --- | --- | --- | --- | --- |
| Series 1700 |  |  |  |  |
|  | Aggregates | Grading | 1 per delivery (min 1 weekly per source) |  | Results of routine control tests by the manufacturer/ |
|  |  | Shell content (N) | Monthly |  | supplier to be |
|  |  | Flakiness index (N) | Monthly |  | provided |
|  |  | 10% fines value (N) | Monthly |  | Product certification |
|  |  | Drying shrinkage (N) | Monthly |  | scheme applies |
|  |  | Chloride content (N) | Daily or as otherwise agreed |  |  |
|  |  | Sulfate content | Monthly |  |  |
|  |  | Blastfurnace slag | Bulk density (N) | 1 per 500 tonnes |  |  |
|  |  |  | Stability (N) | 1 per 500 tonnes |  |  |
|  |  |  | Sulphur content (N) | 1 per 500 tonnes |  |  |
|  | Water | Tests specified in BS 3148 | Monthly |  | Not required if provided from a water company supply |
|  |  | Chloride content | Monthly |  |  |
|  |  | Sulfate content | Monthly |  |  |
|  |  | Acid-soluble alkali content | Weekly |  |  |
|  | Admixtures |  |  | Required | Product certification |
|  |  | Chloride content | 1 per consignment | (BS 5075) | scheme applies |
|  |  | Sulfate content | 1 per consignment |  |  |
|  |  | Acid-soluble alkali content | 1 per consignment |  |  |
| 1707 | Concrete | Cube strength (N) | Prestressed concrete—two cubes from 10m³ or 10 batches whichever represents the lesser volume |  | Contractor to cast and test sufficient additional cubes to demonstrate cube strength before transfer |
|  |  |  | Reinforced concrete—two cubes from 20m³ or 20 batches whichever represents the lesser volume |  |  |
|  |  |  | Mass concrete—two cubes from 50m³ or 50 batches whichever represents the lesser volume |  |  |
|  |  |  | Additional cubes for special purposes |  | Particular requirements as detailed in Appendix 17/4 |
|  | Concrete | Cube strength—special testing as described in Appendix 17/4 (N) | 2 cubes from each of two samples of each batch |  | To determine transfer strength. Cubes to be stored in accordance with Clause 1724.3 |
|  |  | Density | Not required |  |  |
|  |  | Modulus of elasticity |  |  |  |
|  | Fresh concrete | Workability (slump or compacting factor or Vebe (N) | Each batch |  |  |
|  |  | Air content | Each batch |  |  |
|  |  | Cement content | Not required |  |  |
|  |  | Water/cement ratio |  |  |  |
| Clause | Work, Goods or Material | Test | Frequency of Testing | Test Certificate | Comments |
| 1709 | Silane |  |  | Required for each delivery | Certification that the silane complies with Clause 1709 is required |
| 1710 | Concrete packing Mortar packing Epoxy resin bonding agent | Not required |  |  |  |
|  | Precast concrete manufactured off site | Cube strength (Manufacturer’s tests) |  |  | Contractor to make available records of tests by the manufacturer |
| 1711 | Grout | Bleeding | 1 per mix |  |  |
|  |  | Free expansion | 1 per mix |  | Only applicable if an expanding agent is used |
|  |  | Cube strength | 3 cubes from each batch |  |  |
|  |  | Admixtures |  |  | Required (BS 5075) |  |
| 1712 | Reinforcement |  |  |  |  |
|  |  | Steel bars |  |  | Required (BS 4449) | Product certification scheme applies |
| 1726 | Stainless steel bar |  |  | Required (BS 6744) |  | 1726 |

Testing to be Carried Out by the Contractor (continued)

| Clause | Work, Goods or Material | Test | Frequency of Testing | Test Certificate | Comments | Clause |
| --- | --- | --- | --- | --- | --- | --- |
| Series 2400 |  |  |  |  |
| 2401 | Masonry cement |  |  | Required (BS 5224) | Quality management scheme applies |
|  |  | Chloride content | Monthly |  | Test to be carried out by the manufacturer and results included on the test certificate |
| 2402 | Sand |  |  | Required per consignment (BS 1199 and 1200) |  |
|  |  | Chloride content | Monthly |  | Test to be carried out by the manufacturer and results included on the test certificate |
| 2403 | Water | Tests specified in BS 3148 | Monthly |  | Not required if provided from a water company supply |
| 2404 | Mortar admixtures |  |  | Required (BS 4887) (BS 5075) | Product certification applies |
| 2406 | Bricks |  |  |  |  |
|  |  | Clay | (Soluble salt content Efflorescence Compressive strength Water absorption Initial rate of suction) (BS 3921) | Not required |  |  |
|  |  | Calcium silicate |  |  | Required (BS 187) |  |
|  |  | Concrete |  |  | Required (BS 6073: Part 1) |  |
| 2407 | Blocks |  |  |  |  |
|  |  | Clay | (Soluble salt content Efflorescence Compressive strength Water absorption Initial rate of suction) (BS 3921) | Not required |  |  |
|  |  | Concrete |  |  | Required (BS 6073: Part 1) |  |
| 2408 | Reconstituted stone |  | Not required |  |  |
| 2404 | Mortar |  |  |  |  |
|  |  | Ready mixed mortars |  |  | Required (BS 6744) | Testing laboratory to be agreed |
|  |  | Mortars | Tests specified in Appendix A1 of BS 5628: Part 1 (1985) | 1 set of tests per mix |  |  |

Appendix 1/7

Site Extent and Limitations on Use

1	General

  - The extent of the Site is shown on Drawing No.1079541-0100-U-0101, “Working Area & Site Compound Location”.

- Limitations on the Use of the Site

  - Limitations concerning the use of the site are contained in Appendices 1/17 and 1/23.

  - The Contractor shall obtain the approval of the Project Manager for the siting of all huts, workshops, messes, stockpiles, access towers etc and shall keep all access tracks and gateways clear of obstruction at all times.

  - The Contractor shall be responsible for the watching and lighting of his plant, equipment, material and works and in particular plant and stockpiles parked or deposited in the working area adjacent to trafficked areas.

  - The Contractor shall, at all times during the progress of the works, afford facilities to accredited Agents of any public or Statutory Authority for access to all or any of their apparatus situated in, over or under the site, as may be necessary for inspecting, reporting, maintaining, removing, renewing or altering such apparatus in connection with the construction of the works or for any other purpose whatsoever.

  - All lighting used by the Contractor for illuminating the works area shall be fully screened from traffic.

  - At all times, the Contractor shall take measures to ensure that no equipment or material can fall into areas used by pedestrians. Members of the public shall be protected at all times from the effects of the works.

  - Except for the periods of closure of any lane in accordance with Appendix 1/17, the Contractor shall keep the highway free of all obstructions.

  - The Contractor shall take precautions to ensure that no materials or debris are allowed to enter the highway drainage system.

  - The Contractor shall ensure that there is a safe access for pedestrians through or past the works at all times.

  - The Contractor shall take all due care to avoid damage to traffic signs, lighting columns, street furniture, carriageway surfacing, footways and all parts of the structure not affected by the Works and shall not allow vehicles to run or stand on the footways and verges. Any damage caused by the Contractor shall be reinstated at his own expense to the satisfaction of the Project Manager.

  - The burning of waste and the tipping of debris or surplus materials on the site shall not be permitted.

  - The Contractor shall take all due care to avoid damage to the grassed verges and French drains. Any damaged areas of verge will be reinstated by reforming the surface to at least 100mm of approved topsoil trimming and sowing.

  - The Contractor shall be responsible for ensuring that none of his or his sub-contractors personnel cross live traffic lanes with any equipment or materials.

  - Care must be taken not to damage the existing boundary fences, guard rails, safety fences and equipment on the road. No section of fence or barrier must be removed. Should any topsoil have been rendered unsuitable for cultivation this shall be replaced from a source to be approved by the Project Manager.

  - No unnecessary parking of vehicles will be permitted on lengths of the road subject to restriction. The Contractor must make arrangements for collective transportation of his personnel and those of his sub-contractor to and from site.

3	Limits of Working Hours

3.1	The limits of normal working hours on site shall be as follows:

- Monday to Friday, 08.00 to 18.00 hours.

- Overnight working Monday to Friday, 22:00 to 05:30 hours.

- Sunday and Public Holiday working shall not normally be allowed without prior agreement in writing.

- Working may be allowed outside those times given subject to the Supervisor’s approval providing that the Contractor shall have sought such approval no less than seven days prior to his intent to carry out such working.  Approval shall not be unreasonably withheld by the Supervisor subject to any provision to the contrary contained in the Contract.

4	Site Security

4.1	The Contractor shall ensure that the site is secure using an approved fencing; the site compound shall be protected using similar approved fencing and/or patrolled by competent security staff as required, at all times outside working hours.

4.2	Working areas shall be separated from areas of public access by see-through barriers, such as Heras fence or similar.  The barriers shall fully enclose all plant, equipment, materials and spoil deposits.  The barriers shall be fitted with suitable gates appropriate to the works being undertaken in the working area enclosed.

Appendix 1/9

Control of Noise and Vibration

Noise and Vibration

1	The Contractor’s attention is drawn to the requirements contained in the following applicable documents:

(a)	Sections 60 and 61 of the Control of Pollution Act 1974;

(b)	BS 5228: 1984 “Noise Control on Construction and Open Sites”;

(c)	The Noise at Work Regulations 1989, Statutory Instrument No. 1790.

The provisions of both the Control of Pollution Act 1974 and the Noise at Work Regulations 1989 shall be fully complied with.  The guidelines given in BS 5228 : 1984 shall also be followed unless a specific waiver has been agreed with the Supervisor.

3	The normal working hours within the Site shall be Monday to Friday between 08.00 hours and 18.00 hours and overnight working with closures along the A62 Oldham Way 22:00 and 05:30. No weekend working or Public Holidays, without prior agreement.  Exceptionally, consent for work outside these hours may be given by the Supervisor after all necessary consultation. Temporary carriageway closures during these times will require consent from the Project Manager and 14 days’ notice is required.

4	Without prejudice to the generality of the Contractor’s obligations, the Contractor shall comply in particular with the following requirements:

(a)	All vehicles, plant and machinery used for the purposes of the Works shall be fitted with effective exhaust silencers and all parts shall be maintained in good and efficient working order so as to minimise noise emissions;

(b)	All compressors, pumps, power units and diesel engines shall be “sound reduced” models fitted with properly lined and sealed acoustic covers which shall be kept closed whenever the machines are in use, and all ancillary pneumatic percussive tools shall be fitted with mufflers or silencers of the type recommended by the manufacturers.  “Sound reduced” means emitting a sound pressure level not exceeding 75 dB(A) at 10 metres between 07.00 and 19.00 hours, or 70 dB(A) outside these hours.

(c)	Machines in intermittent use shall be shut down in the intervening periods between work or throttled down to a minimum.  The engines or motors of machines which will be out of use for a period exceeding 15 minutes shall be turned off.

5	The Contractor will not be permitted to carry out works as stated below, except where consent has been given for exceptional working or such works are required under the terms of the Contract or is absolutely necessary for the saving of life or property or for the safety of the Works:

(a)	Piling, including sheet piling, by percussive methods on Sundays or Public Holidays or outside the hours of 9.00 to 13.00 on Saturdays or outside the hours of 08.00 to 18.00 on Mondays to Fridays inclusive.

(b)	Any other permanent or temporary works (including the operation and maintenance of mechanical or other construction plant on or adjacent to the site) on Sundays or outside the hours of 08.00 to 18.00, or when notified by the Supervisor of any special Church Services during the working day.

(c)	The Contractor shall furnish such information as may be requested by the Supervisor in relation to noise levels likely to be emitted by any plant which the Contractor is using or intends to use and shall afford all reasonable facilities to enable the Supervisor to carry out such investigations as he may consider necessary.

6	The noise levels scheduled in Clause 9 for periods outside the normal working hours will only be permitted when the Supervisor and the Assistant Director (Environmental Health and Trading Standards) have given consent to exceptional working.

7	The noise level from all sources when measured 2·0 m above the ground at any residential property not insulated against noise shall not exceed the appropriate level given in Clause 9 or not exceed by more than 3 dB(A) the ambient equivalent continuous noise level, LAeq at that control station measured over the same period, whichever level is the greater.  Exceptionally, the Contractor may be given permission to carry out works which exceed the noise levels in Clause 9 provided that 28 days notice of the date and time of these works is given to the Supervisor, and the Contractor demonstrates that he intends to take all reasonable measures to mitigate the noise nuisance.  After consultation with the Local Authority and any other interested bodies, the decision of the Supervisor will be given within 14 days of receipt of the notice.

8	Static plant left running outside the normal working hours within the site will only be permitted if prior approval is obtained from the Supervisor after any necessary consultations.  Suitable screening, such as approved acoustic enclosures, must be provided as directed by the Supervisor. Temporary lights shall be powered from a supply obtained from an adjacent street lighting column.

9	The noise levels scheduled (dB(A)) below must not be exceeded at any point one metre in front of the windows of any occupied building:

| Period | Hours | Noise level LAeq | Period of hours over which LAeq is applicable | Maximum Noise Lpa maximum |
| --- | --- | --- | --- | --- |
| Mondays to Fridays | 00.00 to 08.00 * 08.00 to 19.00 18.00 to 21.00 * 21.00 to 24.00 * | 40+ 65+ 55+ 40+ | Any 1 hour Any 1 hour Any 1 hour Any 1 hour | 55 91 75 55 |
| Saturdays | 00.00 to 08.00 * 08.00 to 13.00 13.00 to 21.00 * 21.00 to 24.00 * | 40+ 65+ 55+ 40+ | Any 1 hour Any 1 hour Any 1 hour Any 1 hour | 55 91 75 55 |
| Sunday | 00.00 to 24.00 * | 40+ | Any 1 hour | 55 |

+ or 3 dB(A) above the noise level with no construction works in progress whichever is the higher

* only if work is permitted

10	The Contractor shall so order his method of working that no excessive vibrations are caused.  In all cases, the maximum measured vibrations at occupied property shall not exceed a peak particle velocity of 1 mm per second unless written consent has been obtained from the Supervisor.  Consideration will only be given if it can be shown conclusively that alternative methods of working are impractical.

11	The Supervisor and the Assistant Director (Environmental Health and Trading Standards) shall be notified immediately of any Works carried out in emergency.

12	A telephone number for emergency use shall be notified to the Assistant Director (Environmental Health and Trading Standards) prior to the commencement of operations and the Contractor shall submit a working schedule, in writing, so that any necessary protection measures can be checked or noise monitoring carried out.

13	Before commencement of Works or any significant phase thereof, or immediately any change in method of working not previously notified is effected, the Contractor shall inform the Local Authority by contacting the Environment Department, Environmental Health, Civic Centre, West Street, Oldham, OL1 1UT.  Telephone: 0161 770 3000.

- The Local Authority has informally agreed that the above measures would be acceptable and they are given as a guide; however it is for the Contractor to decide whether to seek the Local Authority’s formal consent to his proposed methods and to the steps he proposes in order to minimise noise and vibration.

Appendix 1/13

Programme of Works

1     The Contract period shall run from the Date for Commencement of the Works as notified in Writing by the Supervisor.  The Contractor shall provide the Programme of Works in the form of a Bar Chart produced as a result of a ‘critical path analysis’ which shall also be provided and must abide by the constraints below.  It shall show the level of detail appropriate to each stage of the Works and all activities and restraints, each of which shall be given a short title.  All events shall be numbered and annotated with earliest and latest event dates.

2     A schedule of output and resources shall be provided to support all activities shown in the programme.

3	A schedule of output and resources shall be provided to support all activities shown in the programme. The contractor shall give at least 48 hours’ notice (i.e. 2 working days) of the commencement of     the various stages of construction as listed below. Such notice is to be repeated subsequent to any period when work has been temporarily suspended. No further work covering up these stages may be undertaken until approval has been obtained:

Working Constraints

The following working constraints apply:

- The Contractor is responsible for making arrangements with all Undertakers and Public Authorities concerned for the phasing into his Programme of Works of all work, which needs to be done by them or their contractors concurrently with the Works. The Contractor shall allow sufficient flexibility and float-time in his Programme to accommodate amendments arising from uncharted services to individual premises. Particulars of the Undertakers service diversions are contained in Appendix 1/16.

- Drawings and calculations, as requested in Appendix 1/4, are to be approved by the Project Manager prior to works commencing on site.

- Working Hours:

See Appendix 1/7

For Full Road Closure (Lanes 1 to 4):-

Please refer to Contract Drawings for temporary departure from above working hours.

The following restrictions apply as defined in Appendix 1/17.

- Noise and Vibration Requirements - See Appendix 1/9.

- Work to Privately and Publicly Owned Services -

The Contractor's attention is drawn to the requirements of Clauses 150AR, 151AR, 152AR and 153AR which must be taken into account when programming the works.

- Traffic Orders -

The Contractor must obtain the necessary traffic orders for which at least 3 weeks’ notice will be required for completion of necessary statutory procedures - see Appendix 1 /18/17.

Schedule of Constraints

In programming the Works, the Contractor shall take note, inter alia, of the following constraints and requirements which shall be incorporated into his programming.

(i)	The requirement to comply with Traffic Safety and Management measures as set out in Clause 117 and Appendix 1/17.

(ii)	The requirement to comply with Temporary Diversions of traffic measures as set out in Clause 118 and Appendix 1/18.

(iii)	The requirement to comply with Routing of Vehicles restrictions as set out in Clause 119 and Appendix 1/19.  The need to maintain vehicular and pedestrian access to properties adjacent to the site.

(v)	The requirement to test for the classification of excavated unacceptable material prior to disposal.

Level of Detail

The level of detail shall not be less than that given in sample Appendix 1/13 within the Notes for Guidance on the Specification for Highway Works.

Appendix 1/14

Payment Applications

1	The monthly statements submitted to the Project Manager in accordance with Clause 50 of the Conditions of Contract by the Contractor shall, whenever dealing with matters covered by the Bills of Quantities, be set out under Part and Section headings similar to those in the Bills of Quantities and shall separately identify each item and specify quantity, unit, rate and value.  Items not described in Bills of Quantities but appropriate for inclusion as measured work shall be shown at the end of the relevant section or under new section headings as appropriate indicating quantity, unit, rate and value.  In respect of all other matters referred to in Clause 50 the Contractor shall separately show in the statement, quantities, units and rates of goods and/or materials and also details of any other matters to which he considers himself entitled.

## Appendix 1/16

Privately and Publicly Owned Services or Supplies

1	Details of preliminary arrangements that have been made with Statutory Undertakers and others for the alteration or protection of services affected by the Works are listed in this Appendix.

2	The Contractor shall make arrangements with the Statutory Undertakers and others concerned, for the co-ordination of his work with all work which needs to be done by them or their Contractors concurrently with the Works.  Compliance with the periods of notice given in this Appendix does not relieve the Contractor of his obligations.

3	Private Services to individual properties have not generally been listed or shown on the Drawings.  The Contractor shall make arrangements with the Statutory Undertakers and others concerned for the phasing of all necessary disconnections and diversions of private services affected by the Works.

4	Disconnected apparatus can be removed by the Contractor only with the prior approval of the Authority concerned.

5	The names, addresses and telephone numbers of the authorities serving in the locality are listed on the following pages;

| Statutory Undertakers |
| --- |
| Name | Address | Contact |
| Statutory Undertakers |  |  |
| Electricity (1) | Electricity North West Ltd (was UU Electricity Services Ltd) Electricity Service Desk Hartington Road Preston PR1 8LE | Tel: 0800 195 4141 |
| Gas (2) | Plant Protection National Grid plc Block 1 Floor 2 Brick Kiln Street Hinckley Leicestershire LE10 0NA | Tel: 0800 688 588 24hr Tel: 0800 111 999 |
| Telecommunications (1) | Repayments Project Engineer BT Openreach PP100B Dial House 21 Chapel Street Salford M3 7BA | Tel: 0800 023 2023 |
| Telecommunications (2) | Cable & Wireless Comms Atkins Telecoms PO Box 290 The Hub 500 Park Avenue Aztec West Almondsbury Bristol BS32 4RZ | Tel: 01454 662881 Fax: 01454 663330 |
| Name | Address | Contact |
| Statutory Undertakers (cont.) |  |  |
| Water Mains | United Utilities Clean Water Diversions Team Haweswater House Lingley Mere Business Park Lingley Green Avenue Great Sankey Warrington WA5 3LP | Tel: 0800 330 033 E-mail: cleanwaterdiversionsteam@uuplc.co.uk |
| Main Drainage | United Utilities plc Warrington North Wastewater Treatment Works Gatewarth Industrial Estate Off Liverpool Road Sankey Bridges Warrington WA5 1DS | Tel: 01925 428237 Fax: 01925 428125 |
| Street Lighting | PFI Lighting Manager Oldham and Rochdale Street Lighting PFI Unit 2 John Boyd Dunlop Drive Kingsway Business Park Rochdale OL16 4NG | Tel: 0300 303 8881 |
| Virgin Media | Virgin Media Diversionary Works/New Development 1 Dove Wynd Strathclyde Business Park Bellshill ML4 3AL | Tel: 0800 408 0088 Option 2 |

Appendix 1/17

## Traffic Safety and Management

1	Responsibility for Traffic Management

The Contractor shall appoint a Traffic Safety Officer and a deputy, who shall be direct staff employees, to be exclusively responsible for all traffic safety, traffic management and associated work as described in Clause 117 and this Appendix.  The Contractor shall supply to the Supervisor and the Police the names and telephone numbers of these officers for use in case of emergencies outside normal site working hours.

2	Traffic and Management Requirements

2.1	The Contractor shall undertake all traffic management measures as described in the contract.  These measures include signing to Clause 117.9, together with other traffic management measures.  The traffic management measures for each works area shall be fully operational whilst the permanent works are undertaken in that area.

2.2	A full closure of A62, Oldham Way (carriageway closed in one direction at any one time) with a diversion route has already been applied and it will be in effect throughout the works.

2.3	In accordance with Clause 117.6, the Contractor shall submit to the Supervisor for his consent, a traffic management programme, which should include details of the following:

(i)	location and position of all signs, cones, lamps and barriers etc., to be shown in schedule form and/or on a location plan;

(ii)	positions of temporary traffic signals;

(iii)	temporary road closures;

(v)	protection arrangement for the temporary diversion route;

(vi)	working areas;

- safety zones;

- pedestrian safety;

- provision of emergency vehicles;

- phasing of works.

This requirement shall apply to all measures affecting the use of the public highway including site accesses, plant crossings and temporary diversions.

Oldham BC has the right to insist on alternative traffic control methods should the proposed arrangements cause consistent problems with traffic flows. Any changes required by Oldham BC shall be carried out within 24 hours of instruction.

2.4	In accordance with Clause 117.9 the following Department of Transport publications shall apply to traffic management requirements:

Departmental Advice Note TA 47/85

Departmental Advice Note TA 5/80 (includes Addendum)

Departmental Advice Note TS 2/79 (Revision No. 2)

Departmental Standard TD 21/85

Departmental Standard TD 14/83

Trunk Road Management and Maintenance Notice TRMM/9/85.

2.5	All temporary signs located on the existing roads shall be:

(i)	erected on both nearside and offside verges;

(ii)	mounted a minimum of 1·5 m from ground level to the underside of the sign except where erected on or near a footpath where the minimum height shall be 2·1 m.

2.6	All temporary triangular Warning Signs located on existing roads shall comply with the following:

Route	Minimum Height

All roads	750 mm with appropriate supplementary distance plates

3	Highways, Private Roads and other Ways affected by the Work

3.1	Details of Highways, Private Roads and other Ways affected by the Work are as follows:

| Description | Predicted 24-hour Annual Average Daily Traffic AADT | Eighty-five Percentile Speed of Cars (mph) | Speed Limit (mph) | Type of Traffic Control | Special Facilities | Whether to be Kept Open or Closed |
| --- | --- | --- | --- | --- | --- | --- |
| King Street Roundabout | Unavailable | Unavail-able | 30 mph | None | None | Open |

Highways including footpaths, cycle tracks and bridleways, described above or listed in Appendix 1/19 are the responsibility of:

Authority:	Oldham Borough Council

Address:	Oldham Borough Council

Civic Centre, West Street
OL1 1UT
Oldham

Telephone:	0161 770 3000

Appendix 1/19

Routing of Vehicles

- The Contractor will not be permitted to use tracked vehicles on existing or finished road surfaces. This does not relieve the Contractor of his obligations under Clause 14(3) of the Conditions of Contract.

- The Contractor must ensure that delivery vehicles and his own site vehicles communicating with the site use main routes whenever possible.

- The Contractor will not be permitted to use tracked vehicles on existing or finished road surfaces. This does not relieve the Contractor of his obligations under Clause 14(3) of the Conditions of Contract.

- The Contractor must agree with the Project Manager and the Police the locations of works entrances.

- The Contractor must erect temporary road signs on the main routes in the vicinity of the site directing delivery vehicles to the site works entrances and delivery points.

- Contractors vehicles shall enter and leave coned off areas at the ends in the direction of the traffic flow at all times. No U-turns will be permitted at any time on any trafficked carriageways.

- Loading and unloading of vehicles shall be carried out without encroaching onto the running lane of any carriageway.

- Permitted access routes to and from the site are to be via King St Roundabout to King St Footbridge.

Appendix 1/21

Information Boards

- Two Information Boards shall be provided by the Contractor, one to be located at each end of the works and erected in the first week of work on site.

- The location shall be agreed with the Project Manager. The information boards shall be as detailed on Drawing No. 1079541-2600-U-801.

- The Contractor shall remove the information board(s) within 7 days of the date of the Certificate of Completion.

## Appendix 1/23

Risks to Health and Safety

- Restrictions in Relation to Traffic Management Measures

  - Where site operations are carried out adjacent to or near to lanes open to traffic care should be taken to ensure that no dust, spray or other material is transferred to the lanes open to traffic by any means.

  - Additional safety zones may be required locally if the above is likely to occur.

- Restrictions in Relation to Working Practices

- As an alternative to the provision of additional safety zones where any dust, spray or other material could be deposited onto lanes open to traffic the contractor may so arrange his operation, or stop his operations for short periods, when:-

    - the wind direction would propel material onto traffic in the lanes open to traffic;

    - slow moving or standing traffic would be contaminated by site operations.

(Note: for the purpose of this appendix only, "slow moving traffic" is defined as traffic travelling at less than 20mph).

- Measures to be taken to protect members of the Public

- During road works and bridgeworks operations care should be taken to protect members of the public from their effects, particularly during:-

    - Grit blasting operations to bridge decks;

    - Any other operation likely to generate dust, or result in hazardous or unhealthy substances being released.

- Monitoring to be Undertaken by the Contractor

- No specific monitoring will be required but the Contractor should consider Sections 2 and 3 above and his general obligation under the COSHH Regulations and take action to eliminate or reduce problems that occur due to his site operations.

- The Contractor is required to keep records of all materials taken from the site and must record the location of the tips and the nature of the material deposited in them from the site. These records shall be available for inspection by the Project Manager on demand.

Appendix 1/70

Inspection of Specific Works

- The specific items of work to be inspected in accordance with the requirements of Clause 174 AR are as follows:

(a)	Removal of all existing 50mm block pavers and 12/25mm screed/sand bedding on footbridge approaches and footbridge.

(b)	Removal and application of waterproofing on footbridge deck.

(c)	Removal and construction of footbridge movement joints.

(d)	Surface dressing of existing footbridge central concrete upstand.

(e)	Construct new footbridge pavement on footbridge approaches and footbridge.

Appendix 2/1

Site Clearance

- Site clearance items to be Take Up or Down and Set Aside for Re-use or Remove to Store or

Tip off Site are shown on drawings 1079541-1100-U-1101_Rev A.

## Appendix 2/3

Retention of Material Arising from Site Clearance

- Statutory Undertakers apparatus which is made redundant by the Works and requires removal for the construction of the works shall be dealt with in a manner which the Contractor shall agree with the relevant Statutory Undertaker.

- There is no requirement to retain any materials arising from site clearance, unless required by clause 1 above or the table below.

- All trees are to be retained as far as possible. Lopping is to be attempted as the first stage and if in the opinion of Overseeing Organisation this is unsatisfactory they shall be removed. Provision is made in the landscaping to replace these if they are to be removed.

- All voids left by items of site clearance are to be treated appropriately.

- The following list of materials arising from site clearance shall be re-used in the permanent works:

| Description | Location | Delivered To: | Requirements |
| --- | --- | --- | --- |
| Existing bollards. | Refer to drawing 1079541-1100-U-1101_Rev A | Site | To be re-used as shown on drawing 1079541-1100-U-1101_Rev A. |

## Appendix 7/1

Permitted Pavement Options

- Grid for checking surface levels of pavement courses (Clause 702.4)

Longitudinal dimension : 10.0m

Transverse dimension  : 2.0m

- Surface regularity (Clause 702.7) Table 7/2.

- Flexible Pavement materials shall comply with Clause 701 and the following table.

Proposed Foot Bridge Approach Pavement Option

Refer to drawing 1079541-1100-U-1101_Rev A, Section B-B

- Surface treatment to be 2/3mm Anti skid surface treatment consisting of;

      - Decorative aggregate.

      - Bonding coat to be Leeson Grip 3-1 (PU4490/20)2.5-­‐3kg/m2 or similar approved.  Refer to drawing 1079541-1100-U-1101_Rev A.

- Decorative aggregate finish to be quartz (black, grey, white and blue) . Refer to drawing 1079541-1100-U-1101_Rev A, Section B-B.

| Material ref | Clause | Description | Special Requirements |  |
| --- | --- | --- | --- | --- |

| SC/AC 2 | 912 | AC10 Close Surf |  |  |
| --- | --- | --- | --- | --- |
|  |  | 100/150 |  |  |
|  |  | Thickness : | 30 mm |  |
|  |  | Minimum declared PSV xx: | PSV60 [PSV 55 ] |
|  |  | Maximum Aggregate Abrasion Value | AAV12 | [12 ] |
|  |  | Binder Penetration grade: | 100/150 pen |
|  |  | Aggregate Colour: | Subject to source approval |
|  |  | Composition: | PD 6691 Table B14 |

| BC/AC | 906 | AC 20 dense bin |  |  |
| --- | --- | --- | --- | --- |
|  |  | 100/150 |  |  |
|  |  |  | Thickness: | 50mm |
|  |  |  | Composition: | PD 6691 Table B11 |
|  |  |  | Grade of binder : | 100/150 pen paving grade |

Proposed Bridge Deck Pavement Option

Refer to drawing 1079541-1100-U-1101_Rev A, Section A-A

- 5mm Surface treatment to consist of;

- Seal (Trazcon® C22 or similar approved).

- Basecoat (Trazcon® C68V resin and filler broadcast with colour quartz, size 0.7-1.2, or similar approved).

- Membrane (Trazcon® C10V resin or similar approved).

- Primer (Trazcon® P17U priming resin or similar approved).

- 55mm Polymer modified granolithic wearing screed to BSEN13813.

Appendix 12/1

Traffic Signs : General

- The locations of existing bollards that are to be taken down and set aside for re-use are shown on drawing 1079541-1100-U-1101_Rev A.

- The locations of existing bollards that are to be reinstated are shown on drawing 1079541-1100-U-1101_Rev A.

- Bollards are to be reinstated as per Oldham Council Standard Detail HC 1207/1.

Appendix 12/3

Traffic Signs : Road Markings And Studs

- The location, colour and type of permanent road markings are shown on drawing 1079541-1100-U-1101_Rev A.

- Permanent road markings shall be one of the following materials:

  - thermoplastic road marking material or paint in accordance with BS EN 1871;

  - permanent preformed road markings in accordance with BS EN

1871.

- Prefabricated temporary road markings shall only be allowed for use with temporary traffic management after approval from the Engineer.

Durability

- The line marking shall be firmly adhered to the underlying surface. The minimum thickness of a new marking shall be 3mm.

- The Wear Index at any position in the works shall not exceed 1.6 when assessed in accordance with Annex G of BS EN 1824.

Performance

- Road marking shall have the following minimum standard of performance as defined in BS EN 1436 for a period of 1 year from the date of application.

| Property | BSEN 1436 | Requirements Value |
| --- | --- | --- |
| Colour | Table 6 | White | x, y co-ordinates |
|  |  |  | given |
|  |  | Yellow | x, y co-ordinates |
|  |  |  | given |
| Luminance | Table 5 | Class B3 | 0.40 |
| Skid |  |  |  |
| Resistance | Table 7 | Class S2 | 45 |

| Retroreflectivity | Table 2 |  |
| --- | --- | --- |
|  | Classes of RL |  |
|  | for dry markingsClass R4 | 200 |
| Retroreflectivity | Table 3 |  |
|  | Classes of RL |  |
|  | for wet markingsClass RW1 | 25 |

Dimensional tolerances

- The width tolerances and thickness for screed, spray, pre-formed and extrusion white or yellow lines shall be in accordance with the current Traffic Signs Regulations and General Directions. With the exception of Raised Rib edge-line markings, in no case shall any materials be laid more than 6mm thick.

Reflectorisation

- Unless specified all white markings shall be reflectorized with solid glass beads in accordance with BS 6088 by incorporation (except for pre-formed markings) into the road marking mixture and to the wet surface of the marking.

Retro-reflectivity

- Retro-reflectivity shall be measured by means of an approved retrometer such as the LTL 2000 Retrometer.

Yellow material

- Yellow material shall comply with Table 5 and Table 6 of BSEN 1436. Quality Assurance schemes

- All materials and solid glass beads shall be obtained from manufacturers who operate Third Party QA Schemes under ISO 9002, EN 29002.

- The Contractor shall operate a Quality System complying with Scheme No. 7 of the Sector Schemes for Quality Management in Highway Construction – "Application of Road Marking Materials".

Permanent removal of existing road markings

- Where existing road markings are to be permanently removed from bituminous running surfaces this shall be by mechanical means or forced air abrasive (shot blasting). Hot compressed air (HCA) lance shall not be used on concrete pavements and not on other surfaces without the consent of the Engineer. Obliteration of road markings using bituminous, resinous paint or prefabricated materials will not be permitted.

Temporary obliteration of road markings

- Where existing road markings on bituminous pavements are to be temporarily obliterated for traffic management or any other purpose the markings shall be completely covered by black tape or covering which shall be able to withstand the traffic load upon it for the required period. Upon removal of the black tape or covering the original markings are to be upgraded to the standard apparent before the temporary obliteration. Temporary covering of road markings on concrete surfaces shall not be permitted.

Reflecting road studs

- The cutting of the surface course for installation of reflecting road studs shall be by milling or diamond cutting methods only.

.

## Appendix  20/1

## Form PWS Proprietary Waterproofing System Data Sheet & Annexe ‘A’

- Proposed bridge deck water proofing system to be as shown on drawing 1079541-1100-U-1101_Rev A.

Proposed Bridge Deck Water Proofing System

Refer to drawing 1079541-1100-U-1101_Rev A, Section A-A

- Proposed water proofing  to consist of;

- Coating resin (FloorTech International Ltd - Coating Resin C 68 V or similar approved).

- Resin (SILIKAL® RU 320 resin or similar approved).

- Priming resin with additive (FloorTech International Ltd - Priming Resin P 17 U or similar approved, FloorTech International Ltd  - Additive M  & Additive A 51 I or similar approved).

## Appendix  23/1

## Bridge Deck Expansion Joint Schedule

- Proposed bridge deck expansion joint locations are shown on drawing 1079541-1100-U-1101_Rev A.

- The proposed bridge deck expansion joints are to be BD33/94  type 3 joints (Nosing with preformed compression seal).