ALLIANCE ENVIRONMENTAL SERVICES LIMITED

Gully Cleansing and Related Services

THE SPECIFICATION

Contents

Definitions

- Background

- Introduction

- Service Requirements and Outputs

- Waste Disposal

- Data Capture and Defect Reporting

- Performance Monitoring

- Payment & Contact Arrangements

Appendix A - Data Capture requirements for Gully Cleansing

Appendix B - Data Capture requirements for Drainage systems

Appendix C - Gully Cleansing Calendar

Appendix D - Suppliers Street List – see separately attachment spreadsheet

DEFINITIONS

Expressions in the left-hand column of the following interpretation table shall be construed in accordance with the definitions indicated adjacent to them in the right-hand column.

Interpretation Table

| Term | Definition |
| --- | --- |
| AES | Means Alliance Environmental Service Ltd, a joint venture organisation owned and controlled by High Peak Borough Council, Staffordshire Moorlands District Council and Ansa Environmental Services Ltd |
| Contract Standard | The removal of all silt, debris and detritus from the gully pot and any fitted grating, checking for free flow and clearing obstructions in the connections to the mains |
| County Council | Means Derbyshire County Council |
| Contract | Means the resulting Contract for Gully Cleansing and Related Services consisting of all schedules listed within the ITT Guidance and Response Documents and Agreement |
| Contract Term | Means 1 August 2021 until 31 July 2022, unless extended by a maximum of one additional year in accordance with the relevant Contract clause. |
| District | Means the High Peak Borough Council local authority area |
| District Council | Means High Peak Borough Council |
| Drainage Systems | A gully, channel or slot drain |
| Disposal | The deposit of waste at a suitable transfer location or final destination authorised to accept such deposits. |
| Environment Agency | The Environment Agency or its successor in function. |
| Environmental Permit | Means an operating consent issued by the Environment Agency in accordance with the Environmental Permitting Regulations (England and Wales) 2010 |
| Gully / Gullies | A "Gully" is defined as a chamber, pot, pipe, covered channel or proprietary kerb/channel specifically designed for the purpose to collect surface water run-off and transfer it to a drainage system or soak-away and including any such systems leading to any gully or catch-pit in the public highway, to include gullies on the footpath or road/street. |
| Gully Calendar | Calendar of works submitted by the Supplier detailing the time of year when specific regions will receive Gully Cleansing services |
| Gully Cleansing | Shall include the removal of all silt, debris and detritus from the Gully and any fitted grating, checking for free-flow and clearing obstructions in the connections to the mains |
| Gully Cleansing and Related Services | The full and comprehensive service described within the Specification, herein |
| Health & Safety Executive | Means the national independent UK watchdog for work-related health, safety and illness (www.hse.gov.uk). |
| Highway Authority | Means Derbyshire County Council |
| HMSO | Means Her Majesty's Stationary Office |
| Inlet Kerbs | An aperture in kerb allowing access to gully pot through a vertical throat opening |
| Landfill Tax | Landfill tax applies to all waste disposed of by way of landfill, at a licensed landfill site unless the waste is specifically exempt. All Landfill Tax payments and payments due at the Waste Disposal Site shall be made by the County Council. |
| Road Hierarchy | A national system for identifying classification of roads administered by the Dept. of Transport |
| Schedule | Means the schedule as attached at Appendix D - Gully Calendar |
| Supervising Officer | A nominated officer of AES with delegated authority to enforce all Contract terms and manage the Supplier’s performance |
| Supplier | The successful tenderer entering into a contract in accordance with the Agreement |
| Waste Carriers Licence | A Licence issued by the Environment Agency following registration which permits organisations or individuals to transport waste, buy, sell or dispose of waste, or arrange for someone else to buy, sell or dispose of waste. |
| Waste Disposal Site | The nominated Waste Disposal Site is the waste transfer station of Sita UK at Waterswallows Household Waste Recycling Centre, Waterswallows Industrial Estate, Waterswallows Road, Green Fairfield, Buxton, SK17 7JB |
| Waste Transfer Note | A document issued in accordance with the Waste Duty of Care Code of Practice (Environmental Protection Act 1990) that details the transfer of waste from one person to another, as issued by a registered Waste Carrier. |
| Water Authority | Means Severn Trent Water or United Utilities who are involved in water treatment and supply, sewage disposal, land drainage, river pollution and fisheries with the High Peak borough. |
| Weighbridge Ticket | A ticket that incorporates the information required to comply with the Duty of Care Regulations. |

- Background

- AES is a joint venture organisation wholly owned and controlled by High Peak Borough Council, Staffordshire Moorlands District Council and Ansa Environmental Services Ltd.

- AES is responsible for the cleansing of highway Gullies within the High Peak borough on behalf of the District Council and County Council.

- AES is seeking to appoint a single Supplier to carryout Gully Cleansing and Related Services in accordance with the Contract.

- The cleansing of Gullies should be undertaken according to a predetermined Schedule as directed by the County Council.

- AES has a duty to comply with Environmental Health legislation which requires interventions to safeguard public health. These are one off events and can occur anywhere within the boundaries of the Council(s). The scale of these works will vary given the nature of the drainage and specific attributes of the risk once identified.

- Introduction

2.1	The Supplier is required to provide Gully Cleansing and Related Services commencing on the 1 August 2021 for an initial one-year period up to 31 July 2022. The Contract includes an option of an extension for up to one additional year.

2.2	This Contract will be for a period of two years with the option to extend for two further one-year terms. This will take the overall contract length to potentially 4 years subject to performance and requirements.

3.       Service Requirements and outputs

3.1	The Gully Cleansing service requires the complete cleansing of all Gullies on the public highway, and connections checked for free flow, in accordance with the frequency laid out in Appendix D.

3.2	Operations should be programmed between the hours of 06.30 hours and 21.00 hours, Monday to Friday. AES reserve the right to alter the time of operations should the be reasonable concerns.

3.3	Unless otherwise requested by the Supervising Officer. A minimum of 24 Weeks a maximum of 28 Weeks should elapse between each Gully Cleansing visit scheduled to be cleansed twice annually. A minimum of 48 Weeks and a maximum of 56 Weeks should elapse between each Gully Cleansing visit scheduled to be cleansed once annually.

3.4	The Schedule as detailed in Appendix C - Gully Cleansing Calendar, is indicative and reflects the level of works and productivity expected from the Supplier.

3.5	The Supplier will submit a detailed Work Programme each Contract year outlining how the Supplier will complete the required works in accordance with the Street List at Appendix D. The Work Programme will be submitted to the Supervising Officer for approval prior to the commencement of the Contract Year. The Work Programme should be adhered to at all times to ensure performance meets the criteria at 3.3.

3.6	The Supplier is able to request changes to the Work Programme which should be submitted to the Supervising Officer for approval. Changes to the Work Programme will be accepted at the sole discretion of the Supervising Officer

3.7	The Supplier should be aware that the cleansing of all footway Gullies in the borough is also required under the terms of this Contract. These may not be itemised at Appendix D - Supplier’s Street List but are included in the overall number of Gullies.  Footway Gullies are often in place as the sole means of drainage for low areas of footway that would otherwise flood property if not drained.

3.8	Gullies may only be cleansed using specialist Gully emptying machines.  Care should be taken at all times by the Supplier during performance of the contract duties so as not to create undue noise, nuisance or obstruction to other road users or residents.  The Supplier should install guards where necessary around the Gully opening when cleansing is being performed.

3.9	Vehicles should as a minimum be equipped with: -

- Sludge tank and separate freshwater tank of adequate capacity.

- Suction equipment capable of clearing heavy or consolidated silt and debris from Gully pots.

- Clean water high pressure hose for cleaning Gullies and obstructions from connections to the main sewer.

- Hand tools, rods and container for manual cleansing of Gullies and clearance of obstructions.

- Provision of a high pressure jetting unit shall have the capacity of producing a water pressure of up to 2000 P.S.I. with a minimum rate of flow of 65 litres/min, and a self aligning hydraulic hose reel with a run of 100 m of high pressure hose and retro-acting nozzle.

- The provision of a GPS vehicle tracking system with the ability to monitor operational status and generate reports

- The means of displaying identifying signage on vehicles to show that they are working on behalf of the Client i.e.  magnetic placards that can be attached to the doors of the cab. The Client logo will be made available to the successful Supplier. The Supplier is responsible for all costs associated with a suitable means of displaying the identifying signage.

3.10	Gully Cleansing shall include the removal of the entire contents of the Gully without any of the contents being spilled onto the street.  The area around the Gully should be washed down after cleansing.  The Supplier is required to “dig out” any compacted, consolidated or any other material that cannot be lifted by the mechanical process.  When a ‘dig-out’ is required it will be paid at the rate entered in the submitted Tender and the standard cleansing emptying payment will not be paid.

3.11	After emptying, Gullies shall always be flushed and refilled with clean water and checked to ensure that water drains freely out of the Gully via the connection and to provide a water seal to the main sewer connection.  The Supplier shall ensure that any rodding eye is checked, cleansed and plugs refitted where appropriate.  The Gully grating must be cleansed of any obstruction and securely replaced leaving the surface in a clean and tidy condition.

3.12	In the event of the Gully connection not allowing free flow or flow at all, the Supplier shall take reasonable steps to clear minor blockages in connections to include the use of high pressure hoses and / or rods where appropriate for a distance of one metre from the Gully pot.

3.13	The Supplier shall report defects to the County Council using

CONFIRM CONNECT TM on site using the respective defect codes that

have been configured by the County Council. Payment for the attempted clearance of a blockage (i.e. jetting) will be payable at the “jetting” rate entered in the Tender submission.

3.14	When vehicles are prohibited or access is restricted, manual cleansing using scoops and, if necessary, rodding, will be required.

3.15	Where manual cleansing is necessary this shall be performed as in above, but contents will be placed into a suitable receptacle and immediately disposed of in a manner approved in writing by the Supervising Officer.  It is not acceptable for the material removed from the Gully or any receptacle to be stored at any time or disposed of on the highway.

3.16	The Supplier shall ensure that upon lifting of any Gully cover (including kerb inlets), the hinge points are free of detritus or any other material which may impede its opening, and should cutback any vegetation which may impede the lifting of the Gully cover or surface water flow into that Gully.  The Supplier should allow for such within the Tender.

3.17	The Supplier shall report defects to the County Council using CONFIRM CONNECT TM system.  If in the opinion of the Supplier, a defect may present a particular danger (e.g. a broken or missing grid) this must be reported immediately to the County Council. The Supplier shall ensure that the vehicle is equipped with a minimum of four number traffic cones at any given time, cones to BSEN 13422.2004 specification. The cones are to be used in the event of a missing or broken Gully/drainage system grate being identified by the operatives, or any other defects considered presenting a risk to users of the highway. The Gully must be made safe with the use of the cones. The cones are to have the Suppliers identifying marks so that they can be returned to them once the County Council have attended to the defect.

3.18	Should the Supplier damage any Gully during the Gully Cleansing process the Gully shall be made safe, and this shall be reported to the Supervising Officer at the beginning of the following Working Day.  Any costs of repair where such damage is attributable to the actions of the Supplier will be deducted from Tender in accordance with the Conditions of Contract.

3.19	The Supplier shall ensure that in carrying out Gully Cleansing and/or dig outs, traffic safety measures are employed in accordance with Chapter 8 of the “Traffic Signs Manual” issued by the Department of Transport, SSD 12C Mobile Lane Closures and/or any other legislative or regulatory requirements. Payments for traffic control measures will be made to the Supplier in accordance with the rate submitted in the Tender. The Supplier shall notify the Supervising Officer of locations and dates when traffic control is to be used to enable the Client to make use of the safety measures put in place by the Supplier. The Supplier shall submit proposals for temporary traffic signal control to the County Council for formal written authorisation by the Highway Authority.  A minimum of 7 Working days notice is required by the County Council for authorisation. If the Client and County Council have a road closure in place the Supervising Officer may direct the Supplier to deviate from the Work Program and move onto the road closure to reduce costs.

3.20	It may be more practical in certain circumstances for Gullies to be emptied / cleansed during periods of reduced traffic activity (e.g. early mornings in shopping areas or cleansing Gullies on roads near schools during school holidays). Notwithstanding the constraints of Paragraph 3.2, if the Supplier requests permission to cleanse Gullies in any particular location outside ‘normal working’ hours for this or any other reason considered valid by the Supervising Officer then permission will not be unreasonably withheld. County Council road closures should be used where possible to afford safer Gully Cleansing, particularly on major roads. Scheduled road closures can be viewed at (http://www.derbyshire.gov.uk/transport_roads/roads_traffic/roadworks/road_closures/default.asp).The Supplier should allow for any additional expenses in which he may be involved as a result of road closures in his Tender.

3.21	Any Gullies to be cleansed outside normal frequencies as instructed by the Supervising Officer and which, with the exception of emergencies, shall be performed unless notified otherwise.  Emergency emptying will be carried out immediately upon request and shall include Gullies that require emptying to alleviate localised flooding.  Within the Contract Term emergency call out is required.  Payment will be at day-work rates as detailed in the Tender.

3.21	The Suppliers Tender should take account of delays which maybe encountered as a result of parked vehicles in many areas. Costs associated with such should have been considered within the Tender.

3.22	The Supplier shall be required when instructed by the Supervising Officer to make provision for the cleansing of Gullies that are continually obstructed by such vehicles.  The Supplier is responsible for the distribution of leaflets and posting of notices to restrict parking to enable Gully Cleansing duties to be undertaken as scheduled.  The Supplier shall revisit such locations at the date and time specified in the notice and empty all Gullies previously obstructed, no additional payment shall be made for such instances.

3.23	The Supplier shall supply on the CONFIRM CONNECT TM System, a list of all the Gullies cleansed and reasons why Gullies were missed i.e. (vehicle over) from the previous Week.  The Supplier may be asked to revisit certain Gullies not emptied again within the following 4 Weeks of the Scheduled visit and will be deemed to have included for this within the Tender.  Payment will only be paid for Gullies that have been cleansed.

3.24	If the Supplier fails to notify the Supervising Officer of any Gullies which have not been emptied and which are subsequently found not to comply with the Contract Standard then these will be deducted from the payment of services received in accordance with the Tender and must be revisited and cleansed at the expense of the Supplier. Repeated failure to report accurately such incidents may result in Termination of the Contract.

3.25	The Supplier shall be responsible for securing a suitable water supply for his use, and shall be responsible for all costs associated with the use of this supply.  The Supplier shall at all times comply with the requirements of the Environment Agency and the Water Authority, as appropriate.  The Supplier shall inform the Client of the authorised points where he intends to obtain the water for these operations.

3.26	The Supplier shall verify and confirm the number and locations of all Gullies encountered and shall report all anomalies to the Client.  All payments shall be based on the actual number of Gullies cleansed as identified by the data submitted in the CONFIRM CONNECT TM System.

3.27	The Supplier should be aware of their duty under the Health and Safety at Work Act 1974 and its relation to this Contract.  The Supplier shall comply with relevant Acts of Parliament and Codes of Practice associated with Gully Cleansing works and the subsequent transportation and disposal of its resultant wastes. Sources for this information are the Health and Safety Executive, Environment Agency, British Standards Institute and/or HMSO.

- Waste Disposal

4.1	The Supplier shall clear any hazardous material found in any Gully in accordance with the Special Waste Regulations 1996 or any other relevant legislation or Code of Practice.  This will include, for example, the removal of hypodermic syringes and forms part of the normal Gully Cleansing service.

4.2	No additional payment will be made unless additional Gully Cleansings outside of normal frequencies are required in which case the full provisions of Paragraph 3.19 will apply.

4.3	The Supplier is responsible for making suitable arrangements for the transport and depositing of all wastes arising from the Gully Cleansing service at the nominated Waste Disposal Site. The material should be de-watered sufficiently to be accepted.  Any costs incurred in de-watering are the responsibility of the Supplier. The Supplier will be required to supply copies of its Waste Carriers Licence, all Waste Transfer Notes and details of all tonnages disposed of at this site.

The operating times of the Waste Disposal Sites are 08.00 until 17.00 Monday to Friday and 08.00 until 13.00 on Saturdays. The Supplier will ensure arrival at the site no later than 30 minutes prior to the stated closing times. The Supervising Officer reserves the right to alter the operating times and will provide appropriate notice should this be necessary.

4.4	The Supplier shall at all times comply with the provisions of Paragraph 4.3 and shall be fully responsible for the liaison with the operators of the Waste Disposal Site, the collection of all Waste Transfer Notes or Weighbridge Tickets and will comply with the conditions of the Environmental Permit of the Waste Disposal Site. The Supplier shall be deemed to have included for this in the Tender.

4.5	All Landfill Tax payments and payments due at the Waste Disposal Site shall be made by the County Council.

4.6	The Supplier shall not mix Gully Cleansing wastes with any other loads or materials and shall ensure that all wastes resulting from Gully Cleansing duties are delivered solely for Disposal at the Waste Disposal Site unless approved by the Supervising Officer. The Supplier may be expected to divert to another disposal facility in the event of an emergency but will be notified of such arrangements by the Supervising Officer.

- Data Capture/Defect Reporting

5.1 	The County Council utilises CONFIRM (Pitney Bowes Solutions) as a

single asset management system, for highways. The County Council will

provide the Supplier with access to CONFIRM CONNECT TM mobile

software. The software provides the ability to capture in the field data

including functionality to update feature condition data, defect recording,

and identification of new assets. The County Council will configure

CONFIRM CONNECT TM to provide known positions of highway gullies

within the designated area. The Supplier shall be responsible for

provision and maintenance of suitable devices to operate / send and

receive live condition data from CONFIRM CONNECT TM in the field. As a minimum the devices shall have the following functionality;

• Android (Preferred) / IOS

• GPS

• Camera

• Data / SIM enabled (The Supplier will be responsible for all data

charges for duration of Contract)

Where required the Supplier shall fully complete and return to the County Council a “Memorandum of Understanding”, in relation to use and access of CONFIRM CONNECT TM prior to commencing any works.

5.2	The Supplier shall use CONFIRM CONNECT TM to capture intelligent data regarding:

i. The condition of the asset when visited.

ii. The operation undertaken / defect reported on the asset.

Please refer to Appendix B and C, which shows the fields that the

County Council will configure CONFIRM CONNECT TM in line with, and

requires information to be provided against.

5.3	The Supplier will report on the visual content within the gully

chamber/drainage system prior to any other operation, this shall be the

level of arising not level of water.

5.4	The Supplier will report up to three defects on any given gully. In the event that a gully/catchpit requires to be attended to more than once in a

week, then records of each visit are to be provided on CONFIRM

CONNECT TM

5.5	 The Supplier will relocate the gully positions if the position provided within CONFIRM CONNECT TM incorrect.

5.6	 The Supplier will delete any gullies/drainage systems which are

identified incorrectly within CONFIRM CONNECT TM

5.7	The Supplier will identify new drainage assets within the Contractual

District Area not identified within CONFIRM CONNECT TM .The Supplier shall ensure that any new gully/drainage system is attributed with the attributes listed as per Appendix B and CONFIRM CONNECT TM user guide issued and updated by the County Council.

5.8	The Supplier will ensure that if a gully position has been created or relocated then its position and Co-ordinates have a tolerance error no

greater than + / - 1m of the position on site.

5.9	The Supplier shall ensure that the vehicle is equipped with a minimum of four number traffic cones at any given time, cones to BS EN

13422.2004 specification. The heights of which must be in accordance

with Chapter 8 of the Traffic Signs Manual published by Her Majesty’s

Stationary Office for the Department of the Environment and any

amendments thereof. The cones are to be used in the event of a missing or broken gully/drainage system grate being identified by the

operatives, or any other defects considered too present a risk to users

of the highway. The gully must be made safe with the use of the cones.

The cones are to have the Suppliers identifying marks so that they can be returned to them once the County Council have attended to the defect. Once the Supplier has made safe the defect they are to contact Call Derbyshire on 01629 533190 and report the defect immediately.

5.10	The Supplier will provide to the County Council upon request, GPS Tracking Information which identifies the vehicle registration details or other identification. Location of the vehicle when stopped, cleaning

operations and the time when the Jet Vac unit was in operation.

- Performance Monitoring

6.1	During the Contract Term the Supplier shall perform the services in a manner consistent with the terms and conditions of this Contract and to the satisfaction of the Supervising Officer or person authorised by the Supervising Officer.

6.2	If, in the opinion of the Supervising Officer, the Supplier is unlikely to complete the Work Program, the Supervising Officer will require the Supplier to supply a proposal in writing detailing how they propose to “catch up” with the Work Program.  The Supplier shall provide this proposal in writing, within seven Working Days.  The Supervising Officer will advise the Supplier within seven Working Days, in writing, of the acceptance or otherwise, of the proposals.  If accepted the Supplier will execute the revised programme within 48 hours.  In the event of the Supervising Officer not responding, the proposals will be deemed to be sufficient and shall be executed as above.

6.3	In the event of the Supplier not supplying a written proposal within seven Working Days or failing to provide an adequate proposal, the Supervising Officer will make arrangements as deemed necessary to fulfil the Work Plan to the end of the Contract Term or the 6 or 10 month cycle, as appropriate.  The costs involved in these arrangements and the supervision of any works will be deducted from any monies due to the Supplier.

6.4	If, in the opinion of the Supervising Officer, the Supplier is not performing its duties in accordance with the Contract or Work Program, this may result in the termination of the Contract.

6.5	There will be a monthly monitoring programme to ascertain the expected expenditure of the contract.  If the projected outturn is likely to exceed the available expenditure, or the County Council reduce available finance allocated for Gully Cleansing, the Client reserves the right to alter the frequencies or negotiate with the Supplier an agreed alteration to the work programme to ensure that the works DO NOT exceed the bid price or the amount allocated to the service by the County Council.

6.6	The Supplier will be required to attend an initial contract mobilisation meeting and one further meeting after six months of contract operation (unless more often is required due to contractual issues) to discuss compliance with the Specification, Contract Terms and Conditions. The Supplier may also be required to attend additional meetings if and when issues arise throughout the Contract Term. The Supplier must attend all contract monitoring meetings at their own expense.

6.7	The following Key Performance Indicator’s will be monitored through the Contract Term and will be reported by the Supplier as detailed in the table below:

| KPI no. | KPI | Frequency |
| --- | --- | --- |
| 1 | Timely provision of the Data Capture information via CONFIRM CONNECT TM System. | Daily |
| 2 | Gully Cleansing duties undertaken in accordance with the Work Program and evidence that the Work Program is adhered to. | Monthly |
| 3 | Timely provision of the monthly invoice. | Monthly |
| 4 | Inspections of Gully Cleansing work completed according to the Work Program will be conducted by the Client. | Monthly |

7. 	Payment and Contract Arrangements

7.1	Upon completion of the service to the satisfaction of AES, the Supplier will submit an invoice for payment. Electronic invoices are permitted; the Client will provide an e-mail address to the awarded Supplier. Invoices should be submitted monthly no later than 10 working days after the end of the previous calendar month.

7.2	Invoices will be paid within 30 days of receipt of the correct documentation received by AES. These timescales are consistent with Government Regulations provided that the work completed is accepted by the Supervising Officer. Retentions may apply if works are not completed or resolved to the satisfaction of the Supervising Officer.

7.3 	The Form of Agreement is provided at Guidance Document Appendix 3.

7.4 	A Performance Bond or Company Guarantee (equal to 10% of the contract value) is requested for this contract. AES will not bear any costs relating to the Performance Bond.

APPENDIX A – Data Capture requirements for Gully Cleansing

| Central Asset ID – Char (20) | Information provided in CONFIRM CONNECT TM SYSTEM |
| --- | --- |
| USRN – Char (10) | Information provided within CONFIRM CONNECT TM SYSTEM |
| Plot Number | Information provided in CONFIRM CONNECT TM SYSTEM |
| Street Name | Information provided within CONFIRM CONNECT TM SYSTEM |
| Town | Information provided within CONFIRM CONNECT TM SYSTEM |
| District | Information provided within CONFIRM CONNECT TM SYSTEM |
| Cleanse Frequency | Information provided in CONFIRM CONNECT TM SYSTEM |
| Gully Type | GU01 – Surface GU02 – Side Entry OTH – Other | Data to be captured by the Contractor for new Assets created by the Contractor |
| Gully Trapped | YES NO NA - Not Assessed NAP - Not Applicable | Data to be captured by the Contractor |
| Visual Gully Inspection | GUFU - Full Gully GU50 - 50% Arisings GU10 - 0-10% Arisings NA - Not Assessed | Data to be captured by the Contractor |
| Rodding Eye Accessible | YES NO | Data to be captured by the Contractor |
| Gully Access | GUAC - Accessible GURW - Road Works GUVO - Vehicle Over GUJL - Jammed Lid NA - Not Assessed | Data to be captured by the Contractor |
| Gully Dig Out | YES NO NA - Not Assessed | Data to be captured by the Contractor. |
| Gully Cleansed | YES NO NA - Not Assessed | Data to be captured by the Contractor |
| Slow Runner | YES NO NA - Not Assessed | Data to be captured by the Contractor |
| Gully Jetted | YES NO NA - Not Assessed | Data to be captured by the Contractor |
| Gully Defect Lid | DR3 - dr-gully lid missing DR3B - dr-gully lid damaged GU4 - dr-jammed gully lid NONE - No Defect Found DR3C – dr Gully lid cracked | Data to be captured by the Contractor |
| Gully Defect Blockage | GU1 - dr-blocked gully connection GU2 - dr-gully dig out required NONE - No Defect Found | Data to be captured by the Contractor |
| Gully Defect Damage | GU3 - dr-gully pot cracked/damaged GU5 - dr-damaged road surface GU6 - dr-no gully rodding eye NONE - No Defect Found | Data to be captured by the Contractor |
| Date / Time – Float Format. | Date/time captured within CONFIRM CONNECT TM system when data is input |
| Comments/Remarks | When a defect code has been selected the Contractor MUST ensure this field is populated with a location description i.e. Outside 23/ Opposite 1 |
| (X) Easting | CONFIRM CONNECT TM system will capture the eastings. |
| (Y) Northing | CONFIRM CONNECT TM system will capture the northings |

Appendix B - Data Capture requirements for Drainage Systems / INLET KERBS

| Central Asset ID – Char (20) | Information provided in CONFIRM CONNECT TM system |
| --- | --- |
| USRN – Char (10) | Information provided within CONFIRM CONNECT TM system |
| Plot Number | Information provided in CONFIRM CONNECT TM system |
| Street Name | Information provided within CONFIRM CONNECT TM system |
| Town | Information provided within CONFIRM CONNECT TM system |
| District | Information provided within CONFIRM CONNECT TM system |
| Cleanse Frequency | Information provided in CONFIRM CONNECT TM system |
| Hierarchy Category | Information provided within CONFIRM CONNECT TM system |
| Gully Type | KB03 – Drainage Kerbs LD01 – Linear Drainage System OTH – Other | Data to be captured by the Contractor for new Assets created by the Contractor. |
| Visual Inspection | GUFU - Full Gully GU50 - 50% Arisings GU10 - 0-10% Arisings NA - Not Assessed | Data to be captured by the Contractor |
| System Access | GUAC - Accessible GURW - Road Works GUVO - Vehicle Over GUJL - Jammed Lid NA - Not Assessed | Data to be captured by the Contractor |
| System Cleansed | YES NO NA - Not Assessed | Data to be captured by the Contractor |
| Length of Drainage System/Inlet Kerbing (Lin m) – Float Format | Data to be captured by the Contractor for new Assets created by the Contractor | Data to be captured by the Contractor for new Assets created by the Contractor |
| Defect Lid | LD1 – Catch-pit lid missing LD2 – Catch-pit lid damaged LD3 – Catch-pit jammed lid NONE - No Defect Found | Data to be captured by the Contractor |
| Defect Blockage | LD4 - Blocked connection/Outfall LD5 - System dig out required NONE - No Defect Found | Data to be captured by the Contractor |
| Defect Damage | LD6 – Catch-pit cracked/damaged LD7 - Damaged NONE - No Defect Found | Data to be captured by the Contractor |
| Date / Time – Float Format. | Date/time captured within CONFIRM CONNECT TM system when data is input |
| Comments/Remarks | When a defect code has been selected the Contractor MUST ensure this field is populated with a location description i.e. Outside 23 to 37. |
| (X) Easting | CONFIRM CONNECT TM system will capture the eastings. |
| (Y) Northing | CONFIRM CONNECT TM system will capture the northings |

|  |  |  |  |  | Every 2 years |  |  |  |  |  |  |  |  |  | Once annual |  |  |  |  |  |  |  |  |  |  | Twice annual |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | JUL |  |  | AUG |  |  | SEP |  |  | OCT |  |  |  | NOV |  |  | DEC |  |  | JAN |  |  |  | FEB |  |  | MAR |  |  |  | APR |  |  |
| Week | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 |
| Two Years |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2 year |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Once |  |  |  |  |  |  |  |  |  |  |  |  | GLOS. | HV. | NM. | HF. |  |  |  |  |  |  |  |  |  |  |  |  |  |  | WB. | CH. | BUXTON |  |
| Twice | GLOSSOP | CENTRAL | BUXTON |  |  |  |  |  |  |  |  |  |  |  | GLOSSOP | CENTRAL | BUXTON |  |  |  |  |  |  |  |  |  |

appendix c – GULLY CLEANSING CALENDAR

Based on approximately 140 cleanses per day

Note:

The above calendar is indicative and subject to change.

Weeks 43 on wards are left as contingency “catch-up” weeks.

APPENDIX D – Supplier’s STREET LIST

See separately attachment spreadsheet