# ARCUS APPOINTMENT & QUALITY ASSURANCE

This report provides the Pre-Construction Information for the Replacement of Ventilation System and Associated Works at Crundale Tower.

The report was:

Prepared by:	A.Greenwood ……………………………………………….

Name:		Andrew Greenwood

Title:		Partner

Approved by:	D. Handforth..................................................................

Name:		David Handforth

Title:		Associate Partner.

Revision Ref: 	Ver 01

Date:  		18th August 2018

## CONTENTS

1.	INTRODUCTION

2.	DESCRIPTION OF THE PROJECT

3.	CLIENT CONSIDERATIONS & MANAGEMENT REQUIREMENTS

4.	ENVIRONMENTAL RESTRICTIONS & SITE RISKS

5.	SIGNIFICANT DESIGN & CONSTRUCTION HAZARDS

6.	HEALTH & SAFETY FILE

APPENDICES

Appendix A	-	Construction Phase Plan Evaluation Form

Appendix B	-	Designer Risk Assessment

Appendix C	-	Building Maintenance Manual Requirements

Appendix D	-	Health & Safety File contents

Appendix E	-	Designers Assessment CDM 2015

Appendix F	-	Principal Contractors CDM Assessment 2105

Appendix G	-	Contractors Parking Exclusion Zone

Appendix H	-	NASC Scaffold-Spec

1.0	INTRODUCTION

1.1	Unless otherwise stated, the Regulations referred to hereunder are the Construction (Design and Management) Regulations 2015, effective from 6 April 2015. The HSE ‘Managing Health & Safety in Construction’ booklet Ref L153 provides guidance to the regulations.

Pre-Construction Information submitted in this document has been prepared to enable Principal Contractors and/or Principal Designers to submit a Construction Phase Plan, indicating the general Principals to be employed and the resources required to complete the project in a safe manner.  It should not be assumed that all relevant information is currently available, any known further investigations required will be highlighted in this document and the Principal Contractor is in the development of their Construction Phase Plan to make clear any other further investigations needed for the safe execution of the works.

In Appendix A, there is a Construction Phase Plan Evaluation Form which will be used by the Client and/or their CDM Consultant, Arcus, to assess initial contents of the plan provided by the Principal Contractor to see if works can proceed in a way to satisfy the Regulations.  The Contractor is urged to ensure their document will satisfy this check prior to submission for approval.

The Principal Contractor must also ensure that all contractors employed are competent and have the resources in place as required by the Regulations.  Demonstration of progress/systems and processes will be necessary.

Assessments and statements so far supplied by the Designer(s) in terms of risk assessments and related detail are incorporated in this Pre-Construction Information.  Procedures for further liaison between designers and contractors are to be stated in the Construction Plan.

1.2	The Pre-Construction Information and its Aims

This Pre-Construction Information is intended to focus attention on communication of information that Designers and Contractors need to plan to do their work and to provide initial Health and Safety information to the Principal Contractor for the project indicated. It is to be viewed in the context of the duties established in the Construction (Design & Management) Regulations 2015.

The document provides specific site information, to enable the Principal Contractor and their Contractors to develop suitable, safe working methods.

It identifies any known other relevant factors, such as, operating restrictions placed by the Client, Designer or Principal Designer, which should be incorporated into the safe working methods developed by the Contractor.

The information is not considered to be exhaustive and as such the Principal Contractor should visit the site and familiarise themselves with the health and safety aspects of the site and surrounding site.

1.3	Development of the Pre-Construction Information for Evaluation

The Principal Contractor is expected to develop this plan, as a Construction Phase Plan as far as is reasonably practicable, for the purpose of evaluation to allow the Client and their CDM Consultant to confirm that the Principal Contractor will fulfil the requirements under the regulations ahead of the start on site.

The degree and depth of development expected will be dependent upon the specific project, the associated hazards and the information available to the contractor. On many sites the Construction phase plan evolves as information becomes available and as such the Principal Contractor is to ensure an issue register is incorporated in to the plan to allow for its update and reissue to be recorded.

1.4	Construction Phase Plan

The approved Construction Phase Plan may be modified only with the agreement of both the Principal Contractor and the Client/CDM Consultant. This agreement should be in writing and the document shall have an issue and amendment sheet at the front to regard this.

In the event of unforeseen works, the Principal Contractor shall immediately notify the Client/CDM Consultant and Principal Designer of the implications and update the Construction Phase Plan accordingly. Ongoing risk assessments of all construction work shall be included in the Construction Phase Health & Safety Plan.

A copy of the Construction Phase Plan shall be retained on site/at the place of work at all times.

The CDM Consultant will also carry out performance monitoring on behalf of the Client. The Client’s Representative on site will be under instruction to report any failure in the plan or safety procedures to the relevant authority.

The Principal Contractor has responsibility for vetting the competence of Sub-Contractors and will be responsible for ensuring the Sub-Contractors follow safe procedures. The Construction Phase Plan should contain all relevant method statements, risk assessments and COSHH sheets from all Sub-Contractors. The Client/Principal Designer may ask to view Sub-Contractor’s method statements prior to appointing the organisation as ‘Principal Contractor’.

The Principal Contractor will ensure that any relevant information is passed onto the Principal Designer to be incorporated into the Health & Safety File on completion of the project. The Principal Contractor is to provide all necessary manuals, list of manufacturers, stockists of spares etc. and copies of the site modified drawings used for the construction to the Principal Designer for inclusion with Designer’s drawings within the Health & Safety File if required. The Principal Contractor is also to arrange for the Sub-Contractors and other Contractors to provide copies of their arrangement drawings for the inclusion in the Health and Safety File. This information is to be submitted in a structured format, suggested format is shown in Appendix B.

Attention is drawn to the Guidance document L153 Schedule 5 Appendix 4, which provided guidance on the preparation of the Health & Safety File.

1.5	Continuing Liaison

Procedure for considering Health and Safety implications of the design elements for the Principal Contractor and/or other contractors.

Detail design and final as built drawings should preferably include appropriate comments on Health and Safety implications, together with advice on maintenance, dismantling and alterations.

Where ever practical, consideration must be given to designing out Health & Safety Risks within the works. Should this be in conflict with contract documentation, alternative proposals must be highlighted and agreement reached with the Contract Administrator, Principal Designer and Client/CDM Consultant as to the action to be taken. Procedures for circulation and management of design information from all designers must be established and agreed to ensure that all works are considered for Health and Safety.

Procedures for dealing with unforeseen eventualities and conditions during the construction phase resulting in substantial design change, which might affect resources.

Should unforeseen eventualities or conditions change during the construction phase which may affect the agreed procedures in respect of Health and Safety matters, this must be brought to the attention of the Contract Administrator, Principal Designer & Client/CDM Consultant immediately these become apparent. Details to include know Health and Safety implications, risk assessments and method statements where appropriate.

2.	DESCRIPTION OF THE PROJECT

2.1	Project Title

Project Admiral

# 2.2	Project Description

The refurbishment of four occupied 11 storey high rise flat blocks. The extent of the works is as follows:

•	New windows and doors

•	New external cladding and external wall insulation

•	Decoration of flats and communal areas

•	Balcony works

•	Design and installation of new heating system

•	New Lighting and electrical rewire to communal areas

•	General repair and maintenance works

•	New insulated flat roof covering

•	Communal area upgrades

•	Construction of new front entrances

•	Landscaping and environmental works

# Location/Works

Nelson Court, 9 Lagland Street, POOLE, BH15 1RT

Drake Court, 1 Lagland Street, Poole BH15 1RP

Grenville Court Grenville Court, South Road, POOLE, BH15 1PZ

Rodney Court Whatleigh Close, Poole, Dorset, BH15 1RL

Location of Blocks

  - Existing use of Site and Buildings

Crundale Towers is located on the Ramsden Estate, an estate in Orpington, which is part of the London Borough of Bromley. It was built in the 1950s is made up of a large number of semi-detached houses built in the 1950s. The Tower block was built in newer central area built in the 1970s which consisted of three high rise blocks and 48 maisonettes.

All the blocks are eleven storey high. The blocks are concrete framed building with brick infill and render.   All of the surrounding buildings in the areas are residential in nature.

Drake Court						Rodney Court

Grenville Court 					Nelson Court

2.5	Project Programme Details

# 2.5.1	Commencement Date:

# The project is due to start Summer 2019. This was subject to the Client being satisfied that suitable welfare arrangements are in place and a suitable construction phase plan in place prior to commencement.

The Contractor shall provide a programme of works as part of the Construction Phase Plan including phasing of the works to each floor level. The programme proposed for the construction works must illustrate adequate and competent resources and consider partial handover to the client in stages where residents will begin to occupy the building whilst works are ongoing.

It is envisaged that the works will be undertaken during usual recognised working hours i.e. 08:00 – 17:00 hours Monday to Friday, excluding Bank Holidays. Notwithstanding this, should the Contractor feel it is prudent to work extended hours to comply with the contract programme such will be acceptable subject to prior notification/approval of the PM and will be at the Contractor’s expense.

# 2.5.2	Completion Date/Timescale for the works

The approximate duration 36 month from June 19.

# 2.5.3	Lead in time

The minimum time allowed between the appointment of the Principal Contractor and the Instruction to commence work on site is, as advised by the client, 6 weeks. The Contractor must provide a Construction Phase Plan (‘The Plan’) for the works, this should be detailed appropriately to the scale and complexity of the works proposed No works will be permitted to start on site without prior approval of ‘The Plan’ by the client/PD.. A copy of the Construction Phase Plan evaluation form is included in Appendix A

# 2.6	Details of Main Parties

# 2.6.1	Client

# Name:	Poole Housing Partnership Ltd (Borough of Poole)

Address:	Beech House,

28-30 Wimborne Road,

POOLE, BH15 2BU.

Client Project 	David J Hood

Tel: 		01202 264461

Email: 	d.hood@poole.gov.uk

2.6.2	Designers

Name:	Arcus Consulting LLP

Address:	Suite 309

CBX Cobalt Business Exchange

Cobalt Business Park

Cobalt Park Way

Newcastle upon Tyne NE28 9NZ

Telephone:	(0)20 8742 2512

Email:	b.chakarvarty@arcus.uk.com

Contact:	Bobby Chakravarty

2.6.3	Project Manager/Contract Administrator

Name:	Arcus Consulting LLP

Address:	1st Floor

10-11 Heathfield Terrace

Chiswick

London

W4 4JE

Telephone:	(0)20 8742 2512

Email:	a.greeenwood@arcus.uk.com

Contact:	Andrew Greenwood

2.6.3	Principal Designer

Name:	Arcus Consulting LLP

Address:	1st Floor

10-11 Heathfield Terrace

Chiswick

London

W4 4JE

Telephone:	(0)20 8742 2512

Email:	d.hadforth@arcus.uk.com

Contact:	David Handforth

2.6.4	Principal Contractor

Name:		TBC

Address:

Email:

Name:

2.6.5	Contractor

Name:

Address:

2.6.6	Health & Safety Executive:

Address:	14 Stinsford Rd,

Poole BH17 0NF

Telephone: 01202 634400

2.6.7	Local Authority:

Borough of Poole, Civic Centre, Poole BH15 2RU

2.6.8    Emergencies:

Accident and Emergencies

Name:	Poole Hospital

Address:	Longfleet Rd, Poole BH15 2JB

Telephone:	01202 665511

Various dependant on scheme, PC’s are to identify this where required in their CPP

Name:	British Gas Transco	Tel:	0800 111999

Name:	MEB/Scottish Power 	Tel:	0845 272 2424

Name:	British Telecom	Tel:	100

Name:	Environment Agency	Tel:	0800 807060

Name:		Police/Fire/Ambulance Emergencies	Tel: 	999

Name:		Regional Water Board			Tel: 	0800 330 033

Name:		Regional Gas Office			Tel: 	0800 111 999

Name:		Smoke free Law Enforcement 		Tel: 	0800 587 1667

Name:	Local H.S.E Office	Tel: 	0151 951 4000

Name:	HSE Info line  	Tel:	0845 272 2424

(free advice on health and safety matters)

Name:	Environment Agency	Tel: 	0845 933 3111 (Gen. Enquiries)

0800 807 060   (Emergencies)

Name: 	R.I.D.D.O.R.

(Central Accident Reporting Centre)	Tel: 	0845 300 99 23

2.7	Workplace (Health, Safety and Welfare) Regulations 1992

The structure/homes are not be used as a workplace upon completion of the project. The finished design therefore will not need to take account of the relevant requirements of the Workplace (Health, Safety and Welfare) Regulations 1992.

# 2.8	Notification

Under Regulations the Client and the Principal Designer agree that this project is notifiable to the Health and Safety Executive (HSE).

At the time of issuing the Pre Construction Information, an initial F10 has not been prepared and issued.

2.9	Extent and Location of Existing Records and Plans

# The client has confirmed they have issued specifications for the works to the Principal Contractor

# 2.9.1	Existing Health & Safety File

# The client has confirmed that an existing Health & Safety File and Operations and Maintenance Manual(s) does not exist for some of the buildings or the site but other are available by request from the client.

# Contractor Skill, Knowledge, Experience and Training

The client has confirmed that they are happy with the Principal Contractor’s skill, knowledge experience and training in respect of Health and Safety in accordance with the Regulations and the works to be completed.

In the Construction Phase Plan, the Principal Contractor will be expected to demonstrate the processes they will put in place to ensure competency of their own Contractors with whom they may work in execution of this works package.

# 3.	CLIENT CONSIDERATIONS & MANAGEMENT REQUIREMENTS

3.1	Structure and Organisation

The Client’s representative for the project is David Hood

Contact details are as per Section 2.7.1

3.2	Health and Safety Goals for the Project

The project works are to be undertaken within the contract time scale, and to the specification and drawings, which are set out in the contract documents. Full regard is to be made to the Health, Safety and Welfare of the construction staff and that of residents and their visitors as well as the general public and other residents in the immediate vicinity of the site.

The client aims to achieve:

- Zero complaints in relation to health, safety and welfare matters.

- A project which is to have Health and Safety controlled to avoid the occurrence of reportable accident.

- Capture, by the contractor, of all near misses to inform future Health and Safety improvements.

- Full compliance with all Health and Safety legislation to avoid the issue of any prohibition or similar notices by the HSE.

- Safeguarding of all residents on or near the works

3.3	Arrangements for Assessing Training

The Principal Contractor is to ensure that all site personnel (including visitors) are provided with sufficient training for their needs, including on site training where required. The Principal Contractor is also to ensure that adequate health and safety information is provided to site personnel and that a site safety induction is undertaken. Records of personnel who have undertaken a site safety induction are to be kept on site and handed to the Principal Designer upon completion of the project.

3.4	Communication and liaison between client and others

3.4.1	Exchange of Health & Safety Information between Contractors

The Principal Contractor is to implement a system for the exchange of health and safety information between Contractors not only for this contract but if any construction works of any nature are undertaken on or in the immediate vicinity of these works. This may result in the need to meet with other contractors. Details of any meetings or other relevant information are to be copied to the Principal Designer for information and possible inclusion within the Health & Safety file.

3.4.3	Tenant /Client Liaison

The Contractor shall employ or allocate a responsible member of the site team the responsibility to act as a Resident Liaison Officer (RLO) who shall be responsible for communications with the Residents including advising and arranging access or providing details of the work or arrangements for areas to be segregated etc.

3.5	Permits and Authorisation Requirements

The client has indicated that Permits will be required for ‘Hot Works’ and ‘removal of non-licenced asbestos’.

3.6	Security of the Site

The Principal Constructor must provide arrangements for security to comply with the Regulations and as required by the Contract Preliminaries include reference to fencing, barricades clear CDM demarcation and appropriate signage where required. Although unlikely, the Contractor must provide arrangements for Residents evacuation from the properties if particular exits have to be blocked as a result of the works.

- The Contractor will be responsible for maintaining total security to the individual flats as a whole, all work areas, temporary accommodation and storage areas throughout the duration of the works, in and out of working hours.

- The Contractor shall keep an up to date key record book on site. Keys must be individually coded and not to be left in locks under any circumstances.

- All Contractors undertaking work must possess identification badges, wear ‘T’ shirts with Contractor’s logos and sign in and out individually prior to and following each works period (group signing not acceptable).

- Identification Badges: The Contractor shall allow to provide all operatives, either employees or sub-contractors, with identification badges bearing the company logo and picture of the operative which must be worn at all times. The identification badge should be produced by the operative when requesting access to each property or on demand by an officer of the client. The format of the identification badge shall be agreed with the CA, but should include the following details:-

- Name and address of Constructor

- Constructors site and head office telephone number

- Name of the member of staff

- Signature of the member of staff

- Position held by member of staff

- Colour photograph of member of staff

- Signature of issuing officer

- Authorisation of the Client

A record for each operative shall be handed to the Client prior to commencement of the contract for verification of operatives at any time during the contract. Spot checks will be undertaken. Any operative found without a badge will be asked to leave site immediately. The Client will not be held responsible for any disruption in work procedures/contract programme.

- The Principal Contractor must provide arrangements for security to comply with the Regulations and as required by the contract preliminaries including reference to fencing, barricades, clear CDM demarcation and appropriate signage

# 3.7	Welfare Facilities

Suitable and sufficient welfare facilities shall be provided by the Principal Contractor located at readily accessible places. The set-up shall have regard to HSE requirements in relation to distance from the workforce.

# 3.7.1	Sanitary Conveniences

Suitable and sufficient sanitary conveniences should be provided in readily accessible locations (the contractor shall ensure that access to toilet facilities is within a 5 minute walk of the work area), to be adequately ventilated and adequately lit. Sanitary conveniences are to be kept in a clean and orderly condition. Separate provision to be made for male and female conveniences, unless each convenience is in a separate room with a door, which is capable of being locked from the inside.

# 3.7.2	Washing Facilities

Washing facilities are to be provided in the immediate vicinity of the Sanitary Conveniences and in close proximity to any changing rooms if provided. Washings facilities are to include:

- A supply of hot and cold, or warm water.

- Soap or other suitable means of cleaning.

- Towels or other suitable means of drying.

Rooms containing washing facilities are to be sufficiently ventilated and lit and kept in a clean/tidy condition.

# 3.7.3	Drinking Water

The Principal Contractor is to ensure that an adequate supply of drinking water is provided or made available at readily accessible and suitable places. Drinking water supplies are to be marked by an appropriate sign. A sufficient number of cups or other drinking vessels should be provided where a supply of drinking water is provided unless the supply is in a jet form from which persons can drink easily.

# 3.7.4	Changing Rooms and Lockers

Suitable and sufficient changing rooms are to be provided or made available at readily accessible places, if  a worker has to wear special clothing for the purposes of his work and he cannot for reasons of health & safety or propriety, be expected to change elsewhere. Changing rooms shall:

- Be provided with seating

- Include where necessary, facilities to enable a person to dry any special clothing and his own clothing and personal effects.

Suitable and sufficient facilities shall, where necessary, be provided or made available at readily accessible places to enable persons to lock away:

- Any special clothing which is not taken home

- Their own clothing which is not worn during working hours

- Their personal effects

# 3.7.5	Facilities for Rest

Suitable and sufficient rest rooms or rest areas shall be provided or made available at readily accessible places.

Rest rooms/areas shall:

- Be equipped with an adequate number of tables and adequate seating with backs for the number of persons at work likely to use them at any one time

- Include suitable arrangements to ensure that meals can be prepared and eaten.

- Include the means for boiling water.

Be maintained at an appropriate temperature.

3.8	Smoking

Smoking is not permitted anywhere on the site or residents homes.

3.9	Access/Egress

The Principal Contractor shall identify arrangements for separation of the residents/public and the work force operatives

3.10	Accident and Emergency Procedures

The Principal Contractor is to describe in the Construction Phase Plan, the accident and emergency procedures to be implemented. All accident and emergency procedures are to take account of persons in the vicinity of the site as well as on the site itself.

3.11	Arrangements for Reporting & Investigation of Accidents & Incidents

The Principal Contractor is to ensure that procedures and arrangements for the reporting and investigating of accidents and incidents, including near misses, are included in the Construction Phase Plan. This is all to be in accordance with the Reporting of Injuries, Diseases and Dangerous Occurrences Regulations 2013 (RIDDOR).

3.12	Fire Prevention and Fire Safety Plan

A Fire Safety Plan shall be prepared and regularly updated and to be incorporated within the Construction Phase Plan showing escape routes, evacuation procedures and outlining proposed arrangements to prevent fire arising and the spread of fire during the construction works.

3.13	Site Transport or Vehicle Movement

Vehicular access and vehicular movement to the site is to be highlighted by the Contractor. The Principal Contractor is advised that access roads form part of the adopted highway. No temporary accommodation /storage areas shall be located on or at the side of access roads. The Contractor shall liaise with and observe the specific requirements of the Highways Department all times.

For the purpose of undertaking the works use of vehicular access will be limited to that agreed by the Contractor at commencement. Loading/deliveries operations are to be provided in the plan with a demonstration of how theses will reduce risk of interaction with residents and the public. All vehicular and pedestrian thoroughfares must be maintained clear and free from obstructions at all times except where secured off in the immediate vicinity of the works.

Parking within the vicinity of the four blocks is restricted/limited therefore the contractors site personnel may unload tools and equipment close to the blocks/site but then must park outside of the exclusion zone shown below (also see Appendix G of this Pre construction Information)

3.14	Separation of works

Contractor is to make proposals for separation of the works from the general public as work proceeds.

3.15	Site Hoarding

In the event hoardings are deemed necessary the Principle Contractor is to provide a safe design.

3.16    Site Specific Rules

- The Contractor shall ensure that the provisions of the ‘Joint Code of Practice’ for Fire Prevention on Construction Sites’ are implemented and strictly adhered to throughout the duration of the contract. ‘Fire Safety in Construction Work’ HS (G) 168 is to be adhered.

- The storage of hazardous and highly flammable materials is to be in strict accordance with Health and Safety Executives latest requirements and recommendations.

- All materials to be delivered onto the site via a pre-agreed route to a position wholly within the works area. A full method statement is to be agreed with the PM and before commencement.

- The position of the Contractors compound will be as indicated by drawings within the tender documents. The Contractor must ensure effective barriers are provided to prevent unauthorised access and maintain segregation between operatives and residents/visitors of blocks.

- Specific storage requirements will be agreed with the successful Contractor.

- The contractor will be responsible for providing all necessary temporary hard standings, footings, etc. required to locate cabins on grassed areas and shall allow for the making good of all disturbed landscaping upon completion of works.

- The cabins provided by the Contractor shall be suitably secure to prevent unauthorised access.

- All steps or staircases to cabins shall be properly constructed and maintained.

4.0	ENVIRONMENTAL RESTRICTIONS & SITE RISKS

4.1	Safety Risks and Hazards

# 4.1.1	Site Conditions

The sites are located within an existing residential area.

4.1.2	Works Near The Public Highway

High visibility garments are to be worn at all times, by all personnel when working on site.

Suitable protective barriers are to be installed between the working area and public areas.

A minimum clear width of 900mm is to be provided for access and egress. If there are going to be periods of time when the width is restricted below this then arrangements to make residents aware and to assist them, need to be put in place.

Consideration for Traffic Management and Pedestrian Management will need careful consideration in the Construction Phase Plan as it will be necessary to maintain traffic and pedestrian flow throughout the contract period.

The Principal Contractor is to include details of the measures to be implemented to ensure the safety of pedestrians within the Construction Phase Plan.

Consideration for Traffic Management and Pedestrian Management will need careful consideration in the Construction Phase Plan as it will be necessary to maintain traffic and pedestrian flow throughout the contract period.

# 4.1.3	Boundaries and Access

The site boundary is to be made secure and kept secure at all times. The following safety hazards are noted in relation to boundaries and access:

- Emergency escape from the site area.

- Refuse Disposal.

- Dogs.

- Children

# 4.1.4	Maintenance of Access for Emergency Services

Clear access routes must be maintained at all times for fire appliances, refuse vehicles, police vehicles and ambulances.

# 4.1.5	Location of Existing Services

The nature of the works do not necessarily highlight any need for disturbance of buried mains services but will as the works are being carried out within ducts inevitably it will impact upon rising mains and distribution pipework for gas and water services and internal drainage system.

# 4.1.6	Previous Structures

No information is available about any structures on or around the site. However, given the nature of the works, this is not considered to be a problem.

# 4.1.7	Access for Residents

During the works it is essential that the contractor maintains level access into the building for the residents and that they segregate the work from the residents. Additionally a number of residents struggle to get access to upper floors and so the contractor is to ensure that access to the lift is maintained

4.1.8	Resident Liaison Officer:

It will be the Contractor’s responsibility to provide an RLO for the scheme. The Construction Phase Plan is to demonstrate a safe environment for residents, the general public and construction operatives.

# 4.2	Health Hazards

# 4.2.1	Asbestos

Asbestos containing material have been identified. The client is to provide the contractor with access to their register of ACM’s and the contractor is to cross reference this to the works and identify any additional surveys considered necessary.

The contractor will be required to confirm this has been received and demonstrate in their plan how they will work based on the presence of any ACM’s. If the contractor or any of their operatives come across any material which he suspects to contain asbestos, then works are to cease immediately and a R&D type survey is to be undertaken to test the materials. This is to be undertaken by a licensed contractor. The contractor needs to include in their plan their policy for asbestos awareness training.

# There may be additional items of ACM present within the site, over and above those identified in the asbestos survey. The Contractor’s attention is drawn to those parts not specifically accessed by the surveyor for the purposes of producing the asbestos register, in particular such concealed spaces as may exist within the structure and those items of plant or equipment which for any reason the surveyor was unable to examine e.g. live mechanical, electrical or similar installations.

# The following information MUST be provided to the PDF/Client upon completion of the works:

# i)	An updated asbestos register together with details of any additional ACM’s found during the 	works.

# ii)	Certificate of ‘clearance for reoccupation’ issued by an independent UKAS accredited 	laboratory engaged to inspect and air test the asbestos works areas.

# iii)	All consignment notes from the licensed waste hauliers and all certificates issued by the 	licensed waste transfer station and/or disposal site.

# iv)	Details of any encapsulation

# d)	Where asbestos is to be left in situ the material should be correctly labelled and documented in an updated asbestos register. This should be referred to in the Health and Safety file, together with steps that ensure the person responsible for the site needs to take to ensure that they are maintained in a safe condition.

# 4.2.2	Dust and Fumes

Dust and fumes are potentially hazardous to the health of Contractors personnel and visitors/members of the public who may be in close proximity to the works. The Principal Contractor is required to take steps generally to control the emission of dust and fumes which should be detailed in the Construction Phase Plan.

# 4.2.3	Storage of Hazardous Materials

The Principal Contractor is to provide details of the methods to be implemented for the storage of paints and/or any hazardous materials, within the Construction Phase Plan.

# 4.2.4	Noise

Noise must be controlled in accordance with statutory requirements. In addition, every effort must be made to ensure that noise does not disrupt the residents, passers-by or the public at large. Noise should be kept to a minimum at all times. As the building will be occupied then World Health Organisation limits are not op be exceeded and if operations lead to this works will be suspended immediately and will only be allowed to continue when safe working methods have been identified and agreed, the cost of which will be met by the contractor

5.0	SIGNIFICANT DESIGN & CONSTRUCTION HAZARDS

# 5.1	Hazard Checklist

Information on specific hazards associated with the construction and future maintenance will need to be established by the designers.

Having reviewed the works with the client, the extent of the works are not considered to include any significant risks which a competent contractor would not be aware of, however the following are provided for consideration following consideration of the design by the Principal Designer:-

- Works on and adjacent to other occupied properties

- Control of traffic on narrow residential roadways

- Vehicle and pedestrian movements

- Close proximity to the general public

- Possible presence of ACM’s on the site

- Works adjacent to live services

- Location and control of adequate welfare facilities

- Compound & Materials storage area

- High level works

- Site Fire Precautions

- Exposure to the sun

- Violence towards construction operatives

- Dangerous dogs

- Discarded hypodermic syringes

- Works to gas appliances – Gas Safe Register

- Works on electrical Services

5.2	Additional Risks & Requirements

# 5.2.1	Statutory Regulations

Contractor to confirm all work should be carried out in accordance with the relevant Health and Safety Regulations – these may include:

1) 	Workplace (Health, Safety and Welfare) Regulations 1992.

2) 	The Management of Health and Safety at Work Regulations 1999.

- Pollution Prevention and Control Act 1999.

- The Control of Noise at Work Regulations 2005.

- COSHH Regulations 2002.

- RIDDOR Regulations 2013.

- The Construction (Head Protection) HSE ref. CIS 70.

- The Personal Protective Equipment at Work Regulations 1992.

- The Provision and Use of Work Equipment Regulations 1998.

10)	Environmental Protection Act 1990

11)	Road traffic Act 1991

# 5.2.2	General Principals

The Contractor will be required to include within the Construction Phase Plan method statements and risk assessments relating to the safe management and operation of these and all other relevant areas:

1)	Exposure to electric, gas, water and data installation

2)	Falls from height/temporary platforms

3)	Falling materials

4) 	Contact with residents/visitors

5)	Safety of the public where footways are in the vicinity of the works and/or any 			offloading operations.

6)	Handling and use of hazardous materials

7)	Work on gas services

# 5.2.3	Protection of Operatives

As contractors will sometimes be entering properties to complete lone working operations the contractor is to demonstrate how they will provide training on situations where operatives feel at risk.

5.2.4 	Roof and Plant Room Works

The work also involve works to the roof and plant room. Access to these areas is via the main stairs, as can be seen on the photographs below there are a number of steps within the roof structure and numerous cables running across the roof. Contractor shall take these in to consideration and the impact of winds with the blocks being in excess of 11 storeys high

5.2.5 	Work with the Ducts

The work involves removal of ductwork and installation of new duct within a small service duct. Although this is not strictly a confined space the area available to work within is restricted means for entry or exit and is not suitable for continuous occupancy. The contractor shall provide method statements for working within these areas

6.0	THE HEALTH & SAFETY FILE

###### 6.1	Responsibilities & Arrangements

All relevant information which is required to be included in the Health & Safety File should be collected by the Contractor and issued to the Principal Designer in duplicate by final Handover of the scheme. This shall include all guarantees, certificates of testing, material types any suppliers, all subcontractor details and information on maintenance/servicing of any installations.

###### Format and Information to Be Provided

The Health and Safety File will take the form of A4 lever arch files and the Principal Contractor should provide the following information in the sections listed in Appendix B.

In addition an electronic copy on disk or memory stick shall also be provided.

# Text boxes

PRE CONSTRUCTION INFORMATION

FOR

PROJECT ADMIRAL TOWER BLOCK REFURBISHMENT

FOR

POOLE HOUSING PARTNERSHIP

Prepared By

Arcus Consulting LLP

1st Floor

10-11 Heathfield Terrace

Chiswick, London

W4 4JE

T: 0208 742 2512

AUGUST 2018