# Expressions of Interest for removal of asbestos from the roof and part demolition of Torrington Swimming Pool

Torridge District Council is seeking expressions of interest from suitably qualified demolition contractors to be included on a short list to tender. The work comprises the safe removal and disposal of the cement asbestos roofing panels, sprayed limpet asbestos roof insulation lining and the part demolition of the pool hall at Torrington Swimming Pool, Great Torrington EX38 7AJ, pending reconstruction.

Torrington swimming pool is a single storey structure, built and converted between 1974 – 1975.  The building comprises of an entrance hall with reception serving both male and female changing rooms with associated showers and giving access to a viewing gallery over the pool hall. The pool hall encompasses a 25m long swimming pool, with a small purpose built sauna in one corner and access to the boiler room located to back and side of the building. There are two sets of double doors to the side of the pool hall which give access to the rear car park area.

To the South of the building is a parking area for the general public, with additional parking and staff parking area to the East (behind the building).There is an access road through the site to an adjoining depot (the road will be closed for the contract period). Limited on site car parking will be available for the duration of the contract only, please see block plan for further details.

Works

The following is an outline of work to be undertaken at the premises:-

- Removal of roof insulation and roof covering to the pool area, which contain asbestos

- Exposing elements of the steel frame to the pool area for inspection purposes

- Enabling access for investigation of the pool tank and structural elements of the building

- Securing the remaining building pending reconstruction of the pool roof

Due to the location of the building adjacent a highway and the extent and difficult location of the material to be safely removed it is anticipated that the successful contractor will be able to demonstrate extensive experience of carrying out similar demolition work.

Expressions of Interest

If you wish to express an interest in this contract, you must do so via the Southwest Procurement Portal, at www.supplyingthesouthwest.org.uk before 12 noon on Tuesday 28th June 2011

Those contractors registering interest will be emailed a link to a Pre-Qualification Questionnaire (PQQ) that must be obtained and returned electronically through www.supplyingthesouthwest.org.uk by 12 noon on Thursday 30th June 2011

In order to complete the PQQ, it must be downloaded to your system, completed and then uploaded to www.supplyingthesouthwest.org.uk. It is not possible to complete the PQQ document on-line.

Submission of the completed PQQ should not be left to the last minute as it may take some time to upload the document. The server time stamps the documents (GMT) when they are submitted. Any PQQ submitted after the closing date will not be considered. Any PQQ that is posted, emailed or faxed to Torridge DC may not be considered.

It is expected that the short list to be invited to tender will consist of five contractors. Tenders will be evaluated on a ‘Value for Money’ basis in terms of criteria as stated in the tender documents.

Contact Information

The administrative officer in connection with the contract is:

Andrew Champion BSc(Hons) MRICS. Building Surveyor

Torridge District Council

Riverbank House

BIDEFORD
EX39 2QG

Tel: 01237 428753 	Email: andy.champion@torridge.gov.uk