# Appendix A

# SCHEME ADDRESS:  PLAY AREAS

| AREA | TASK | PERFORMANCE STANDARD | FREQUENCY |
| --- | --- | --- | --- |
| RUBBER SAFETY SURFACE AREAS, PLAY AREA PATHWAYS, PLAY AREA FURNITURE, ACCESSORIES. | Jet washing | Draw water supply from wash out using low pressure inlet to tank. Set up high pressure wash system using trailing hose as required to reach site. Manually scrape/brush the majority of arising before washing, remove and dispose of debris away from site. Jet wash all floor surfaces throughout the perimeter border of the site working to natural edges with grass. Ensure any benches, bins, signs, play equipment and entrance path are adequately cleaned. Rinse the entire site ensuring that there is no surface debris remaining, final rinse ok to grassed areas. No chemical treatments on site unless specific prior instruction has been received and authorized. | Annually as required –weather dependent. |
| COMPLETED WORKS | Photographs | Before & After photographs to be supplied to Parks and Open Spaces Officer. | Annually as required –weather dependent. |
| See attached list of ALL PLAY AREAS owned or managed by MDDC. Monthly inspections determine the requirement for pressure washing each site as per specification. PLEASE NOTE that not all play areas are cleaned annually and we require a price for cleaning per sqm, to include travel costs, machinery and water. |

Please note the following: -

- The contractor shall provide, run and maintain suitable machinery & tools in accordance with the manufacturer’s instructions and health and safety recommendations for safe use, for cleaning services, at no additional cost.

- The contractor shall provide appropriate cleaning products and consumables.

- The contractor will be required to submit Health and Safety monitoring sheets for each visit which will be submitted with  monthly invoices for works undertaken, each equal to 1/12th of the annual contract value ( + the cost of any additional works approved by the Property Services Team).

- Appropriate protection and signage to be in place whilst works are in progress to ensure the health and safety of staff, contractor’s operatives and the general public where applicable.

- Fuel for machinery should be included in the quotation figure, and the contractor will ensure safe storage and transport of any fuels in accordance with health and safety guidelines.

- All additional work is to be authorised in advance by the Property Services Department and the Estate Management Department, invoiced separately along with the normal monthly charge.

- All chemicals used must be non-hazardous to animals and people and used according to manufacturer’s instructions, COSHH documentation and control measures must be provided prior to any works being undertaken.

- All work is to be carried out in accordance with the Mid Devon District Council Code of Conduct.

# Text boxes

STANDARD SPECIFCATION FOR CLEANING SERVICES