## SCHEDULE OF WORKS

FOR

WESTWARD HO! PROMENADE SURFACING

|  | DESCRIPTION OF WORKS | UNITS QUANTITY | £ p |
| --- | --- | --- | --- |
| A 1.0 | SECTION A: SITE PREPARATION SURVEY: Before starting work, carry out a survey and submit a report and Method Statement covering all relevant matters listed below and in Health & Safety Executive Guidance Note GS29/1 paragraph 32: Removal methods of arisings Type and location of adjoining or surrounding premises which may be adversely affected by the Works | Item |  |
| B 1.0 B 1.1 B 1.2 B 2.0 B 2.1 B 2.2 B 2.3 B 3.0 | SECTION B: WORKS Promenade Carry out planing of Promenade footpath to depth 12mm, in preparation of receiving final surfacing Dispose of arisings Overlay final surface of Addagrip 3mm aggregate resin bound surfacing in Autumn Gold to 12mm depth Village Green Installation of 5 no. bronze commemorative plaques in locations as shown on drawing C446/001. Dimensions: 300mm dia x 10mm, 2 fixing lugs to rear of plaque – plaques to be provided by TDC Removal of cold-lay tarmac around raised kerb edges, and dispose of material Overlay final surface of Addagrip 3mm aggregate resin bound surfacing in Yellow Cream to 12mm depth Overlay infants play space in Addagrip (Addacolour) colour resin bound surfacing in colours and pattern as drawing C446/001 Clean legs and bases of street furniture | item item item Item Item Item Item item |  |
|  | DESCRIPTION OF WORKS | UNITS QUANTITY | £ p |
|  | WORKMANSHIP GENERALLY: Operatives must be appropriately skilled and experienced for the type of work and hold or be training to obtain relevant CITB Certificates of Competence Site staff responsible for supervision and control of the work are to be experienced in the assessment of the risks involved and in the methods of demolition to be used COMPLETION: Clear away all debris and leave the site tidy on completion NOTICES: The contractor shall be responsible for the issue of any relevant Notices and approvals required for working adjacent to or temporary closure of the footpath. | Item Item |  |
| TOTAL FOR SCHEDULE OF WORKS |  |
|  | Total Carried Forward From Preliminaries |  |
|  | Total Schedule of Works |  |
|  | Sub Total |  |
|  | Add Contingency @ 5% of contract sum |  |
|  | Total Carried Forward To Form of Tender |  |