Alvaston Park Lake – Habitat improvement works

TD 1318

Section D

# Health & Safety Pre - Construction Information Pack

Issue Date: January 2018

| Document status |
| --- |
| Revision | Date | Status or comment | Prepared by | Checked by | Authorised by |
|  | Jan. 2018 | Final | Brown |  |  |

DISCLAIMER

This document and its contents have been prepared and are intended solely for the Client’s information and use in relation to Alvaston Park Lake - Habitat improvement works.

Derby City Council assumes no responsibility to any other party in respect of or arising out of or in connection with this document and/or its contents.

COPYRIGHT

The copyright of this document is vested in Derby City Council only. This document may not be reproduced in whole or in part without their express written permission.

## PRE-CONSTRUCTION INFORMATION DEVELOPMENT

The purpose of this document is to act as a record of pre-construction information that has been communicated to the necessary and relevant appointed parties within the project team.  This information has been provided by Derby City Council in relation to Alvaston Park Lake – Habitat improvement works.  By conveying this information, Derby City Council is assisting in ensuring the client discharges their duties under the Construction (Design and Management) Regulations 2015 by providing relevant pre-construction information to designers and contractors.

1     PROJECT DETAILS

Introduction

This pre-construction information has been developed to provide information to tendering contractors on the health, safety and welfare matters they need to take into account when undertaking habitat improvement works at Alvaston Park, Derby.

This document provides details of the nature of the project, the project organisation and information relating to general and specific health and safety issues. It also provides details of the project health and safety management and the information that is required to be provided by the Contractor in order to demonstrate that they have taken appropriate account of all necessary health and safety arrangements.

The Contractor should review the information included or referenced in this document and provide the relevant information requested. Failure to provide the required information or inadequate consideration of the information contained or referenced in the document may result in delays to the approval of the construction phase health and safety plan. Any conflict between the details contained in this document and any other contract document should be brought to the attention of the author for resolution.

The Contractor will be required to develop a Construction Phase Plan before work commences and to then fully implement, monitor and review the plan throughout the life of the project. The Principal Designer will facilitate the flow of design information pertaining to health and safety for the duration of the project and the Contractor will need to take this into account and update or amend the Construction Phase Plan accordingly.

Project description

1.1	A Brief description of the works

Undertake habitat improvements to the lake including:

•	Repairs to edges of concrete lined lake.

•	Removal of areas of Norfolk Reeds.

•	Selective tree removal on island.

•	Formation of marginal planting areas around the perimeter and island, supported by re-distribution of silt and aggregate in the lake.

•	Supply and planting of pre-planted coir rolls, marginal plants and reeds.

•	Supply and install bird netting to protect planting areas.

•	Supply and commission solar powered oxygenating pump.

•	Renewal of ornamental shrub planting around lake.

•	Reduce numbers of Canada Geese by preventing eggs hatching.

•	Supply and installation of interpretation boards.

1.2 Drawings:

Location plan P5-7-1

Lake Improvement Works P5-7-2

Base Plan P5-7-3

Ornamental shrub planting P5-7-4

1.3 Dates

The contract period is to run from early 2018 to 30th. September 2019. The contract period shall be agreed with the contractor and is dependent on the optimum seasons for different aspects of the work and achieving the objectives of the project.

Time is to be allowed between appointment and start on site for surveys, design and obtaining environmental permit.

1.4 F10 Notification

N/A The project is not notifiable.

2.      PROJECT DIRECTORY

Name of Client

Derby City Council

Director of Communities and Place

Representative Contact Name: Angie Brown

Designer

Derby City Council

Director of Communities and Place

Representative Contact Name: Angie Brown

Health & Safety Executive

City Gate West,

Level 6 (First Floor)

Toll House Hill

Nottingham NG15AT

Tel 0845 345 0055

3.    CLIENT’S CONSIDERATIONS AND MANAGEMENT REQUIREMENTS

3.1 Planning for and managing construction work, including any health and safety goals for the project

IMPORTANT: regular liaison/communication with the Client will therefore be of key importance for the duration of the construction works.

The Contractor must aim to deliver the project with a zero accident or injury rate. They must set out within their Construction Phase Plan the systems, methods of work and management techniques they will employ to ensure this Client requirement.

The following items will require particular consideration, planning and management (not an exhaustive list):-

• Ground conditions (including contamination).

• Existing services (especially underground), i.e. water, gas, electricity etc.

• Traffic management: deliveries/waste collection to and from site, segregation, transportation of materials/plant/tools around the site, banksman etc.

• Delivery and positioning of site cabins, welfare unit and storage containers etc.

• Site (including site compound) security/segregation.

• Noise, vibration and dust.

• Excavations.

• Manual handling.

• Working within the flood plain and adjacent to the River.

• Communication and co-ordination of sub-contractors.

Planning and managing health and safety on site is the responsibility of the Contractor. They should therefore detail within their Construction Phase Plan for the project their intended method for fulfilling these duties, including overseeing the health and safety standards and processes for sub-contractors’ health and safety.

The appointed Contractor will adopt a distinctive approach towards the implementation and maintenance of a safety culture on the site throughout the construction period.

It is vital that the Contractor applies innovative techniques and best practice to ensure that hazards arising from the works are kept to a minimum as is reasonably practicable.

3.2 Communication and liaison between parties.

In order to ensure the safety of all visitors (especially young persons/children) using the access road then communication with the Client will be of paramount importance.

The Contractor will nominate one point of contact, usually the Site

Manager to liaise with the Client on a daily basis. NB: via phone or email,

together with minuted monthly progress meetings with the project team.

Any day-to-day issues (including those relating to health and safety) should be directed to Angie Brown who can be contacted on 07812 301586 or 01332

641601.

Any issues that may have a contractual or financial implication should also be discussed with Angie Brown as laid out within the contract documents.

The Contractor shall be responsible for the co-ordination of all health and safety and welfare for the duration of the construction period. Health and safety will form part of both the agenda for any site meetings and the Contractor’s progress report.

As stated previously, project progress meetings will be held on a regular basis for the duration of works. Any non-urgent matters relating to health and safety should be raised at such meetings. Where project meetings are called the Contractor will issue a progress report, this report shall include any issues or incidents relating to health and safety.

The Client (Angie Brown) will be informed as soon as is practicably possible of any accidents or incidents reported to the HSE under the requirements of the Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR) 2013.

The Contractor will be required to demonstrate the means by which he ensures the information, relevant to any work activity is disseminated to those operatives actually carrying out the work. Full details of these processes should be included within the Contractor’s Construction Phase Plan.

The Contractor must carry out regular safety inspections on site, whether by external consultants or in-house departments (not directly connected with the project). Copies of safety inspection reports or a summary of the reports are to be available for review at all times.

3.3	Site security

Upon commencement, the site will be released into the management and control of the appointed Contractor during periods of work as set out in the program. During these periods, the site will be under his direct and total control with regards to safety, security, site access/egress and construction operations etc.

Whilst the main area of work will be within the contractor’s site boundary, the responsibility will extend to any areas used for storage of plant, equipment or materials, access and egress routes and areas outside the main compound used only for short periods of time, e.g. vehicles waiting to off-load deliveries etc.

All works will be to external areas, the Contractor shall therefore ensure that robust security procedures are in place for the site, i.e. Heras fencing or similar (solid hoarding - free standing) etc.

Areas of access (including gates to the site compound, site areas etc.) along with tools, plant, materials or equipment must never be left unsecured or unattended.

The Contractor will demonstrate within their Construction Phase Plan the means by which they will ensure that all areas of the works are separated from areas remaining available to the general public in order to ensure their safety.

The Contractor will operate a ‘signing in and out’ procedure for the site to which all operatives and visitors will adhere. This shall be kept easily accessible at all times and shall be removed from site in the event of a fire for reference by the designated fire marshal.

Suitable signs must be erected around the site to make the general public (including young persons/children) etc. aware of the dangers involved. These must be of a type that is easy to understand (i.e. pictorial rather than word) and at a height they can see it (i.e. eye level). Every effort shall be made to exclude members of the public from the site.

Visitor access to site areas shall be subject to an induction or by accompaniment by the Contractors site management to ensure their safety.

The site shall be left and kept in a safe condition outside working hours with all plant immobilised and equipment left secure.

Details for all the above will be included within the Contractor’s Construction Phase Plan.

3.4 Welfare provision

The Client has advised that the Contractor will be required to provide their own welfare facilities for the site.

As such, the Contractor shall ensure that suitable and sufficient welfare facilities are provided prior to the commencement of any construction works on site, as required under Schedule 2 (Regulations 13(7) and 22(1)(c)) of CDMR

2007. NB: refer to Section 9 below for guidance.

An area will be given over to the Contractor for positioning of cabins and storing materials. These must be suitably fenced to secure against trespass. The Contractor will detail their procedures for this within their initial Construction Phase Plan.

Details of the type and the location of welfare facilities will be included within the Contractor’s Construction Phase Plan for the project.

The Contractor shall be responsible for providing personal protective equipment (PPE) and any safety items associated directly with the work being carried out and for providing such equipment to visitors on site, in accordance with his general obligations under health and safety legislation.

4	Requirements relating to the health and safety of the client’s employees, customers or those involved in the project, such as:

4.1 Site transport arrangements or vehicle movement restrictions

Access to the Alvaston Park is via Meadow Lane, off London Road, Alvaston, Derby.

Lockable height barriers are in place at the entrance to the park and shall be kept locked at all times unless additional height is needed. Ensure the height barrier is locked at the end of each working day.

Access to the site is from the main car park in the park via a macadam surfaced pedestrian path adjacent to the community building.

See Location Plan P5-7-1.

The Community building houses changing rooms, public toilets, Rangers office and a café and there is a popular play area adjacent to the path.

Adequate notice shall be given of the start date for the works to allow for display of information signs and contact to be made informing the public and stakeholders of any alternative routes and of vehicles crossing.  Also to provide directional signage for delivery vehicles.

The Contractor shall be required to enforce a 5mph speed limit and use hazard warning lights for all construction traffic on site. The Contractor must use a trained banksman as necessary to access the area of work.

The Contractor is to ensure that access and egress is kept clear at all times for emergency vehicles.

The Contractor will take all of the above into consideration when producing their Traffic Management Plan for the site. A copy of this will be included within the Construction Phase Plan for the project.

4.2	 Site hoardings

As previously state, security of the site (including site compound) must be of paramount importance, hoarding and security fences must be designed to a standard to ensure that all reasonable control measures are applied to restrict access by unauthorised persons to work areas, i.e. general public (including young persons/children) etc.

The above requirements shall include areas used outside of the site boundary for the storage of materials, plant and equipment.

As stated previously, any areas of access (including gates to the site compound, site areas etc.) along with tools, plant, materials or equipment must never be left unsecured or unattended.

4.3	Vehicle parking restrictions.

Contractors vehicles may park in the main car park during the construction works.

4.4	Client permit-to-work systems

The Client will not operate a permit-to-work system for those activities under the control of the Contractor. The Contractor shall therefore assess the risks involved in each individual piece of work and install their own permit-to- work system.

The Contractor will therefore include within their Construction Phase Plan template copies of all permit-to-works they consider necessary for the project, i.e. permit-to-dig etc.

4.5	Fire precautions

The Contractor shall provide a Fire Risk Assessment and Safety

Management Plan in accordance with CDMR 2007 for the project.

The Contractor will be required within the Construction Phase Plan to establish emergency procedures (i.e. fire alarm, muster point etc.).

The Contractor must supply their own fire extinguishers for the site. These must be appropriate for the work being undertaken.

The Contractor will be responsible for calling the fire brigade to inform them of any fires that start on site/site compound.

The nearest fire station is;

Kingsway Fire Station,

Kingsway Hospital,

Kingsway, Derby,

DE22 3LZ (tel: 01332 367 270).

The Contractor will be responsible for their own staff, including bringing the site register to the assembly point (the location of this is to be identified within the initial Construction Phase Plan).

Where possible any skips used should be positioned at least six metres from surrounding structures and/or temporary buildings, i.e. site cabins, storage containers etc. Where this is not possible the skip should be suitably secured within Heras fencing and lockable.

NB: it shall be of the highest importance that access and egress for emergency vehicles is kept clear and maintained at all times during the construction period.

Details of the Contractor’s proposal for this must be included within their Construction Phase Plan.

4.6 Emergency procedures

The Contractor shall provide full written details within the Construction Phase Health and Safety Plan immediate actions to be taken in case of an emergency on site. Details of A&E are supplied at time of tender. A plan showing the quickest route from the site to the hospital shall be displayed within the site office.

The Nearest Hospital for accident and emergencies is

Royal Derby,

Uttoxeter Road

Derby DE22 3NE

Tel 01332 340 131

4.7 ‘No-go’ areas or other authorisation requirements

All areas not forming part of the site (including site compound) are out of bounds to the Contractor and their sub-contractors unless given express permission by the Client, Angie Brown.

4.8 Smoking restrictions

Smoking is to be restricted to a designated area of the site compound only - away from the view of young persons/children.

4.9 Visitors to the site

The Contractor shall make mandatory the wearing of all appropriate Personal Protective Equipment (PPE) suitable for the site location and nature of construction work. This shall be identified within the Contractors risk assessment. Procedures are to be in place for site visitors.

No smoking or use of illegal drugs in to be permitted at any time

4.10 Permitted hours of Working

Monday to Friday - 7.00am 5.00pm

Saturday - No works unless by previous agreement with the Client.

Sunday No - works unless by previous agreement with the Client.

Bank holidays - No works unless by previous agreement with the Client

School holidays - No works unless by previous agreement with the Client

4.11 Client Specified Rules

The Client has not stipulated any site specific rules at the time of producing this document. NB: please refer to the General Conditions of Contract for Landscape Works contained within the Preliminaries documentation.

5	Existing on-site risks and environmental restrictions

5.1 Environmental restrictions

All works are subject to Environmental permit from the EA and License from Natural England and working methods are to be adhered to. The contractor shall demonstrate in his Construction Phase Health & Safety Plan how environmental damage is to be avoided and procedures in place for reacting to accidental spillage etc.

5.2 Boundaries and access

The Contractor will produce a Site Plan as necessary to show the transport routes, work areas, storage areas, fire escape routes, muster points and location of welfare facilities (not an exhaustive list).

5.3 Deliveries/ storage.

All materials and waste must be stored either within the site compound or carted straight off site and where applicable be of an enclosed type to reduce the potential risk of arson. NB: the temporary storage of waste outside the site boundary will not be permitted.

As stated previously, the Contractor shall liaise with the Client to confirm and agree arrangements for work restrictions, deliveries, positioning of a site compound and parking prior to the commencement of any works on site.

5.4 Adjacent land

The site is within a public park and adjacent to the River Derwent.

5.5 Existing storage of hazardous waste

No hazardous materials were being stored on site at the time of producing this document.

5.6 Location of existing services

See details of known services in Appendix. 1.

However, the drawing is to be treated as indicative only, the Contractor must therefore verify the status of any services (including underground) prior to the commencement of any works on site. The location of which are to be marked accurately on a drawing and shall be maintained within the Construction Phase Plan and made available for inclusion within the Health and Safety File.

The Contractor will also demonstrate within their Construction Phase Plan the procedures by which they will communicate pertinent information to those actually at risk (i.e. operatives carrying out work, or those in close proximity to the works).

5.7	Ground conditions which may affect operations-

The site is within a flood plain and may be subject to flooding during heavy rain and adjacent ground may be soft.

5.8 Information about existing structures – The lake is a concrete lined construction with macadam perimeter path.

5.9 Any previous fire damage, ground movement, etc. – not applicable

5.10 Any access problems for plant and equipment

•	The contractor shall visit site to assess access restrictions such, but not limited to:

•	Width and height of access barriers into the park

•	Width of existing access road and paths

•	Overhanging tree branches on access road

5.11 Vehicle Movements to and from the area of work

The Contractor shall allow for use of appropriate size plant to the area of work allowing for shared use with pedestrians.

The access to the area of work shall be kept free of mud and debris at all times.

The Contractor shall supply all necessary warning signs at key locations of maximum risk. The signs are to be displayed at all times whilst work is in progress.

Contractor must use a banksman as necessary.

6 Health Hazards including:

6.1 Asbestos-

Not applicable but should any materials be discovered that are suspected of containing asbestos during the life of the project, then all work in that area should cease immediately with the area withdrawn from by contractor staff. The Principal Contactor will then notify the Client, Angie Brown of the situation.

A UKAS accredited analyst should be arranged to analyse the suspected material. If the material is confirmed as containing asbestos of a type notifiable to the HSE, then the Contractor shall follow the guidelines as laid down under

Regulation 8.2 of the Control of Asbestos at Work Regulations (CAWR) 2002.

Following removal the Contractor will ensure copies of Waste Consignment Notes are obtained and retained for inclusion within the Health and Safety File.

NB: the Contractor will be required to demonstrate within their Construction Phase Plan that they will have operatives on site trained to recognise asbestos containing materials at all times.

6.2 Contaminated land, include results of surveys -

No information was available (relating to contamination) at the time of producing this document.

6.3 Working at height

Working at height may be present during the project, as such the Contractor will demonstrate within their Construction Phase Plan their method for eliminating the risks involved in working at height.

Any work at height must be undertaken in line with the requirements of the

Working at Height Regulations (WHR) 2005 (amended).

7 Significant Design and Construction Hazards

7.1 Areas the client has designated as confined spaces

The Client has not identified any areas designated as a confined space.

7.2 Significant design assumptions and suggested work methods, sequences or other control measures

Refer to tender package, i.e. drawings, specifications etc. for relevant information provided by the design team disciplines.

The Contractor is required to carry out a detailed hazard identification exercise to state required controls, provide necessary method statements and incorporate these into the Construction Phase Plan.

The risk analysis take into consideration previously identified hazards, assess the severity of the risk and where appropriate indicate the consideration given by Designer’s to health and safety.

The Contractor is required to fully address the issue of risk analysis in developing the Construction Phase Plan.

The Contractor must ensure that method statements and risk assessments are obtained (for sub-contractors (if applicable)) prior to relevant activities being undertaken on site.

7.3 Suggested work methods / sequences

Refer to the tender package released by the Client.

7.4 Please refer to the Construction Phase Designers Risk Assessment and Health and Safety Table for the following;

7.4.1 Underground services

Refer to item 4.7 above.

7.4.2 Excavations

7.4.3 Mechanical hazards

The Contractor shall ensure that operatives are fully trained in manual handling where possible and provide mechanical handling aids to avoid accident or injury.

7.4.4 Working with Substances Hazardous to Health

7.4.5 Environmental hazards

7.4.6 Work place hazards - not applicable

7.4.7 Work Practice

The Contractor will take all necessary precautions to minimise risks when working at height. The Contractor shall submit a risk assessed method statement on how risks of working at height will be mitigated.

7.4.8 Traffic hazards – refer to Section 4 Environmental restrictions and on-site

risks

7.4.9 Public Safety    - refer to Section 4 Environmental restrictions and on-site

risks

8 Overlap with Client’s Undertaking

8.1 Access

Access is required for grounds maintenance, deliveries to café etc.

8.2 Arrangements for co-ordination of on-going design work and handling design changes

The Contractor will liaise with the design team relating to any design undertaken in the construction stage.

The Contractor will be responsible for co-ordinating any design carried out by sub-contractors including where this has an impact on the health and safety of those carrying out construction work, cleaning, maintenance or demolition of the structure or any equipment installed as part of the project. NB: minutes of relevant meetings will be taken and recorded within the Construction Phase Plan.

Any changes in design that have a significant impact on health and safety will be notified to the Client at the earliest possible opportunity. Where these have a significant effect on health and safety, the proper risk review should be undertaken by the designer in line with their duties under CDMR 2015.

Where the Contractor (including his sub-contractors) and others have a design input into elements or components of the works, their duties under the CDMR 2015 are the same as any other ‘Designer’. They shall give the same due consideration to their designs in terms of health and safety and follow the same procedures of hazard identificati on and risk assessment as required of all Designer’s within the CDMR 2015 and the Approved Code of Practice.

8.3 Materials requiring particular precautions –

We were not aware of any specified materials that require particular precautions

at the time of producing this document. However, a number of common

materials may be used that could cause hazards if manufacturer’s instructions are

not followed.

The Contractor is to obtain manufacturer’s COSHH datasheets on all

products that they may have identified as a potential risk, to enable them to carry out

suitable and sufficient risk assessments and dependent on the findings introduce

adequate control measures within his Construction Phase Plan.

9 The Health and Safety File and any conditions relating to its content.

The Contractor will be responsible for ensuring that relevant health and safety information is provided to the client (including information that is provided and collated from appointed sub-contractors). The minimum requirement for the Client is two hard copies and one soft copy (CD ROM).

The Health and Safety File must meet CDMR 2015 ACOP requirements, and Client’s requirement document. The Health and Safety File will provide information needed during future construction work which includes as built drawings, procedures for cleaning, maintenance, alteration, refurbishment and demolition and will be submitted to the Client who will make it available when required.

Contents of the Construction Phase Plan

The checklist below is a guide for the Contractor to use in the compilation

of the Construction Phase Plan, in accordance with the HSE Publication L144,

Approved Code of Practice (Appendix 3) for the CDMR 2015.

1 Description of Project

a) Project description and programme details including any key dates.

b) Project directory.

c) Existing records.

2 Communication and Management of the Work

a) Management structure and responsibilities.

b) Health and safety goals for the project and arrangements for monitoring and review of health and safety performance.

c) Arrangements for;

• Regular liaison between parties on site.

• Consultation with the workforce.

• The exchange of design information between the client, designers, CDM-C and contractors on site.

• Handling design changes.

• The selection and control of sub-contractors.

• The exchange of health and safety information between contractors.

• Security arrangements.

• Site induction and on site training.

• Welfare facilities.

• First aid.

• The reporting and investigation of accidents and incidents during near misses.

• The production and approval of risk assessments and method statements.

• Site rules.

• Fire and emergency procedures.

3 Arrangements for Controlling Significant Site Risks

a) Safety Risks;

• Delivery and removal of materials (including waste) and work equipment, taking into account any risks to the public e.g. during access and egress from the site.

• Services including temporary electrical installations.

• Preventing falls.

• Work with or on fragile materials.

• Control of lifting operations.

• Dealing with services - water, gas, electricity etc.

• Maintenance of plant and equipment.

• Poor ground conditions.

• Traffic routes and segregation of vehicles and pedestrians.

• Storage of materials, particularly hazardous materials) and work equipment.

• Dealing with unstable structures.

• Accommodating adjacent land use.

• Other significant safety risks. b) Health Risks;

• Procedures for the discovery of asbestos.

• The removal of asbestos.

• Dealing with contaminated land.

• Manual Handling.

• Used of hazardous materials.

• Reduction and monitoring of noise and vibration, including HAVs.

• Other significant health risks.

NB: works shall not commence on site until the Construction Phase Plan has been developed by the Contractor and reviewed by the client in line with the requirements of CDMR 2015.

10 Welfare Facilities Guidance

CDMR 2015 - Minimum welfare facilities required for construction sites

Mobile welfare facilities

Category B Welfare Toilet unit –

• Plumbed in WC or alternatively a chemical type may be sufficient for works of a shorter duration.

• Cubicles must have doors with locks fitted.

• Toilet consumables for example soap/hand towels.

• Sanitary disposal facilities (where women may be expected on site).

• Adequate lighting/windows.

• Accessible non slip steps.

• Maintained in a clean and hygienic condition at all times.

• The unit must be level and stable. • All waste must be suitably contained and removed from site as required.

• The facilities should be robust enough to withstand daily use.

Washing facilities –

• Plumbed in wash basin complete with plug or alternatively a basin integral to the chemical toilet unit may be sufficient for works of a shorter duration.

• Hot/warm and cold running water.

• Soap and/or other hand cleaning material.

Classification: OFFICIAL

• Provision for drying hands/forearm.

• Sinks large enough to submerge entire forearm.

• Adequate heating, lighting and ventilation.

• The facilities should be robust enough to withstand daily use.

• All waste must be suitably contained and removed from site as required.

• Waste bin.

Drinking water –

• A supply of fresh drinking water must be provided which can be mains, bottled or in a container and clearly marked.

• An adequate supply of cups must also be available.

Classification: OFFICIAL

Maintenance and cleaning

• Systems must be in place to ensure all welfare facilities, cabins, offices etc are maintained in a clean and tidy condition and are fit for purpose.

• All consumables are to be replenished as and when required.

DESIGNERS RISK ASSESSMENT

Relating to the Construction Phase of the Contract

RISK ASSESSMENT GUIDANCE NOTES

Hazard – The potential to cause harm, including ill health and injury; damage to people, property, plant, products or to the environment; production losses or increased liabilities.

Risk – The likelihood that a specified undesired event will occur, due to the realisation of a hazard by, or during, work activities or by the products and services created by work activities.

Hazard (Impact) Rating

4 = Very High – Causing multiple deaths and widespread destruction.  Such a risk would include a major refinery or oil rig explosion, a mine collapse or nuclear accident.  It may cause death and injury both on and off site, and would be the subject of regulations under CIMAH.  (The Control of Industrial Major Accident Hazards 1984 – as amended 1988).

3 = High – Causing death or serious injury to an individual.  Death or serious injury must be reported to the regulating authority under the terms of RIDDOR (The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations 1995).  The disease and injury categories are defined in Schedule 3 of RIDDOR.

2 = Medium – Causing injury or disease capable of keeping an individual off work for three days or more and reportable under RIDDOR.

1 = Low – Causing minor injury which would allow the individual to continue work after First Aid treatment on site or at local surgery.  The duration of the stoppage/treatment is such that the normal flow of work is not seriously interrupted.

0 = Nil – No risk of injury or disease.

Risk (Likelihood) Rating

4 = Very likely – If the work continues as it is, there is almost 100% certainly that an accident will happen, for example broken stair or broken rung of ladder, bare exposed electrical conductor, tall, unstable stack of heavy articles.

3 = Likely – The effects of vibration, wind or human carelessness could precipitate an accident, but which is unlikely to happen without this additional factor, for example ladder not secured to scaffolding, pile of tubes with temporary or makeshift wedge, temporary electrical hook-up to live supply, puddle or slippery or oily waste on walkway.

2 = Quite Possible – The accident may happen if additional factors precipitate it, but is unlikely to happen without them.  The additional factor is more than a casual slip or nudge and would require an additional action or event to trigger it, for example leaving a vehicle with the engine running, obstructing as aisle, leaving a welding torch alight on the bench, failing to replace a defective light in a storage room used at night.

1 = Possible – If other factors were present, this incident or illness might occur, but the probability is low and the risk minimal, for example storing, heavy items above shoulder level, cracked or chipped electrical plug or frayed cable, cracked glass window, worn steps.

0 = Not likely – There is no risk at present.  Only under freak conditions could there be any possibility of an accident or illness.  All reasonable precautions have been taken so far as is reasonably practicable.  This should be the normal state of the work-place.

Risk Level

The risk level should be obtained by multiply hazard rating by risk rating.  For example a hazard rating of 4 and risk rating of 3 will give a risk level of 12.

Risk Level is calculated as follows:

Low – 0-5

Medium – 6-10

High – 11-16

Commonplace hazards that should be controlled by good site management, organisation and practices expected of a competent contractor are not listed – only site-specific hazards are included.

This Assessment is not exhaustive and work not covered by this Risk Assessment should only be undertaken after a suitable Risk Assessment has been made.  Certain activities should only be carried out in conjunction with a written safe system of work.

| No | Hazard details/risk assessment | Hazard impact rating 0-4 | Persons affected | Risk likelihood rating 0-4 | Possible control actions for the Contractor | Risk level Low 0-5 Med 6-10 High11-16 |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Underground services including cables and pipes and overhead cables in areas of excavations. | 0 | Contractor’s operatives, site visitors and other third parties of physical injury resulting from damage, breaking, bursting of services leading to possibility of electrocution, fire, explosion, flooding. | 0 | Ensure that all service plans are available on site and readily accessible, services are located, marked, trial pitted and so on before excavation commences. Use safe systems of work. Confirm location of services by hand dug trial holes. Check if service is live or redundant. Mains and services must be protected and supported as required and regular checks are made of exposed services. Allow for hand digging around services. | Low |
| No | Hazard details/risk assessment | Hazard impact rating 0-4 | Persons affected | Risk likelihood rating 0-4 | Possible control actions for the Contractor | Risk level Low 0-5 Med 6-10 High11-16 |
| 2 | Working in a flood plain – risk of flooding from river channel. Risk of drowning, injury or death. | 3 | Contractors operatives | 1 | Register for EA heavy rainfall warning Develop a plan for making safe the site and timely evacuation in a flood event | Low |
| 3 | Working within a watercourse – biological hazards / waterbourne diseases, slopping / uneven / slippery / unstable banks, confined spaces / difficult access & egress / underwater debris, accidental immersion / entanglement / impacts / drowning / axphyxiation | 3 | Contractors operatives | 2 | Include in RAMS and site induction Assess stability of banks prior to works | Medium |
| 4 | Excavations, holes and trenches | 2 | Contractor’s operatives, site visitors and other third parties of physical injury resulting from falls into excavations and collapse of unsupported trenches while working in them. | 1 | The Contractor shall: Establish a safe method of working. Do not store materials and equipment adjacent to excavations. All excavations to be fenced off or must be suitably covered if left over night. | Low |

| No | Hazard details/risk assessment | Hazard impact rating 0-4 | Persons affected | Risk likelihood rating 0-4 | Possible control actions for the Contractor | Risk level Low 0-5 Med 6-10 High 11-16 |
| --- | --- | --- | --- | --- | --- | --- |
| 5. | Mechanical Hazard Physical injury resulting from: |  | General public using the open space. |  | Cordon off working area from general public and users of open space. |  |
| 5.1 5.2 5.3 5.4 5.5 5.6 5.7 5.8 | Impact Crushing Trapping Cutting Entanglement Falls/trips/slips Abrasion Materials stored or stacked on site. | 2 | Contractor’s operatives, site visitors and other third parties of physical injury. Contractor’s operatives, site visitors and other third parties of physical injury resulting from inadequately stacked or stored materials, which may fall, lead to falls/ tripping or restrict visibility. | 2 | Ensure safe systems of work to minimise hazards associated with moving machinery Ensure site operatives wear adequate protective clothing including safety helmet. Undertake handling assessment and use appropriate lifting methods. Ensure lifting equipment is suitable for the object to be moved. Ladders to be footed by colleagues. Secure items until concrete foundations are fully cured Ensure that materials are securely stored within cordoned areas, stacked below specified height | Low |

| No | Hazard details/risk assessment | Hazard impact rating 0-4 | Persons affected | Risk likelihood rating 0-4 | Possible control actions for the Contractor | Risk level Low 0-5 Med 6-10 High 11-16 |
| --- | --- | --- | --- | --- | --- | --- |
| 6. 6.1 6.2 6.3 6.4 6.5 6.6 | Hazard Substances. Toxic Substances Toxic Fumes Dust Flammable Substances Explosive Substances Biological Hazard | 2 | General public using the open space. Contractor’s operatives, site visitors and other third parties of burns, skin irritation, damage to the respiratory system. | 2 | Carry out COSHH assessments for all substances and implement control measures including use of suitable equipment, restricting use to appropriate weather conditions and informing the public Records of the assessments and monitoring of safeguards will be made by the Contractor Implement control measures including covering up / shielding materials and activities generating dust and emissions, restricting activities to appropriate weather conditions and informing the public Ensure site operatives wear adequate protective clothing – See Mechanical Hazard. Also ensure site operative wear adequate respiratory protection. Ensure safe and secure storage of materials on site. | Low |

| No | Hazard details/risk assessment | Hazard impact rating 0-4 | Persons affected | Risk likelihood rating 0-4 | Possible control actions for the Contractor | Risk level Low 0-5 Med 6-10 High 11-16 |
| --- | --- | --- | --- | --- | --- | --- |
| 7 7.1 7.2 7.3 7.4 | Environmental Hazards Hot Materials/Surfaces - bituminous material safety surface materials High Ambient Temperature - Safety surface materials Significant Noise - Excavation operations Cutting concrete edgings Breeding birds – risk that breeding birds are disturbed / killed, due to works | 1 | General public using the open space Residents living adjacent to the site Contractor’s operatives and site visitors. Breeding birds | 1 | Ensure safe working practices and establish safe method of working Ensure site operatives wear adequate protective clothing. See Section 3 Mechanical Hazard A noise assessment must be carried out and appropriate ear protectors provided and worn if considered necessary. (Ear protectors to BS6344 or EN Standard) Ensure that noise from operations is limited during peak times, for example before 9.00 am and after 5.00 pm Plan for works to take place out of bird nesting season. Pre-start checks by ecologist | Low |

| No | Hazard details/risk assessment | Hazard impact rating 0-4 | Persons affected | Risk likelihood rating 0-4 | Possible control actions for the Contractor | Risk level Low 0-5 Med 6-10 High 11-16 |
| --- | --- | --- | --- | --- | --- | --- |
| 8. | Work practice Hazards |  |  |  |  |  |
| 8.1 | Lifting/Handling - concrete edgings playground equipment | 1 | Contractor’s operatives of physical injury | 1 | Establish a safe method of working | Low |
| 8.2 8.3 | Repetitive Actions Stressful Postures |  |  |  | Undertake handling assessment and use appropriate lifting methods |  |
| 8.4 | Long Operative Hours |  |  |  | Ensure lifting equipment is suitable for the object to be moved |  |

| No | Hazard details/risk assessment | Hazard impact rating 0-4 | Persons affected | Risk likelihood rating 0-4 | Possible control actions for the Contractor | Risk level Low 0-5 Med 6-10 High 11-16 |
| --- | --- | --- | --- | --- | --- | --- |
| 9 9.1 9.2 9.3 9.4 9.5 | Work practice Health and Hygiene First Aid Fire Training Audit | 1 | Site visitors. Contractor’s operatives of physical injury | 1 | The Contractor will be responsible for the provision of welfare facilities for his staff and sub contractors Ensure adequate provision for first aid (including trained first aider) Contractors Emergency procedure will clearly set out the mean of dealing with any emergency and summoning assistance The Contractor will make appropriate arrangements for dealing with fires which are appropriate to his plant, equipment and method of working. The Contractor’s procedures will identify his own fire fighting equipment and location and his arrangements for summoning assistance. Emergency procedures for the safety of his employees will also be included. The Contractor will ensure that employees are properly trained for their respective duties. Emphasis is to be placed on health and safety matters and all employees will be made aware of site rules; all staff will undergo site-specific induction training before being allowed on site. The senior management person on site will have had formal Health and Safety training within the last five years. The Contractor will carry out periodically a Health and Safety audit – and make available the results to the client and the planning supervisor. | Low |

| No | Hazard details/risk assessment | Hazard impact rating 0-4 | Persons affected | Risk likelihood rating 0-4 | Possible control actions for the Contractor | Risk level Low 0-5 Med 6-10 High 11-16 |
| --- | --- | --- | --- | --- | --- | --- |
| 10. | Traffic Hazard |  |  |  |  |  |
| 10.1 | Contractor’s vehicles entering and leaving the area of work and crossing areas of public open space. | 3 | Contractor’s operatives, site visitors and general public of physical injury resulting from vehicles accessing the site of the works. | 2 | Secure the working area and plant from adjacent public areas, for example provide suitability robust fencing where required; if necessary, provide security presence on site Mark out and maintain safe routes of adequate width for vehicles to and from the working area. Display relevant danger signs to the public Work areas and plant are to be left safe when not supervised Contractor to liaise with occupiers when works interfere with free access to premises. Particular vigilance is required with regard to trespass by children and other young persons. Establish a safe method of working including control of timing of vehicle movements, use of appropriate vehicles. Use banksmen to direct vehicles and plant in and out of site and while reversing and to assist pedestrians to pass through works areas safely. Access routes and pedestrians routes where they cross works are to be clearly marked and/or diverted as required Operate appropriate traffic management system. Signage in accordance with Chapter 8 of the Traffic Signs Manual 1991 All vehicles shall be clearly visible and use rotating beacons. Position so as not to obstruct visibility of road users Ensure all hard surfaces are kept free of mud and debris. Provide warning ‘mud on road’ signs, if necessary Site personnel to wear high visibility florescent clothing and to cordoned areas Be aware of public leaving and entering the area at set times. Ensure that vehicle movements are limited during peak times | Medium |

| No | Hazard details/risk assessment | Hazard impact rating 0-4 | Persons affected | Risk likelihood rating 0-4 | Possible control actions for the Contractor | Risk level Low 0-5 Med 6-10 High 11-16 |
| --- | --- | --- | --- | --- | --- | --- |
| 11 | Public Safety Use of public highways to access the open space by Contractors operatives | 3 | Highway users – in vehicles or pedestrian of physical injury | 2 | Establish a safe method of working including control of timing of vehicle movements, use of appropriate vehicle Use banksmen to direct vehicles and plant in and out of site while reversing and to assist pedestrians to pass through work areas safely. Access routes and pedestrian routes where they cross works are to be clearly marked and/or diverted as required Operate appropriate traffic management system. Signage in accordance with Chapter 8 of the Traffic Signs Manual 1991 All vehicles shall be clearly visible and use rotating beacons. Position so as not to obstruct visibility of road users The Contractor will ensure that employees are properly trained for their respective duties. Emphasis is to be placed on health and safety matters and all employees will be made aware of site rules; all staff will undergo site-specific induction training before being allowed on site. Ensure the highways and footpaths are kept free of mud and debris at all times. Provide warning ‘mud on road’ signs, if necessary Site personnel to wear high visibility fluorescent clothing and to work in cordoned areas Be aware of public leaving and entering the area at set times. Ensure that vehicle movements especially deliveries to site are avoided during peak times. Key times will be established at the Pre-contract meeting | Medium |

# Text boxes

Please note:

Place any partner logos beneath this line. If there are no partner logos delete this box and the line.

Please note:

Place any partner logos beneath this line. If there are no partner logos delete this box and the line.